8051 CROSS ASSEMBLER
   
   
                             USER'S MANUAL
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
                         MetaLink Corporation
                           Chandler, Arizona






     
                         MetaLink Corporation  
                            P.O. BOX 1329
                     Chandler, Arizona  85244-1329  
                            (602) 926-0797
                         TELEX: 4998050 MTLNK
                         FAX:  (602) 926-1198
 
     
     
     
                     PURCHASE TERMS AND CONDITIONS
     
     
     Since MetaLink Corporation does business and is located solely in
     the State of Arizona, such orders or agreements and the rights of
     the parties hereunder  shall be governed by the laws of the State
     of Arizona.
     
     
     
     LIMITED WARRANTY:  METALINK MAKES NO WARRANTIES OTHER THAN THOSE 
     CONTAINED HEREIN AND METALINK EXPRESSLY DISCLAIMS ANY AND ALL 
     IMPLIED WARRANTIES, INCLUDING ANY WARRANTY OF FITNESS FOR A 
     PARTICULAR PURPOSE OR OF MERCHANTABILITY.
     
     
     The foregoing limited warranty shall not apply unless Buyer has 
     paid for in full the MetaLink products.  Updates to the MetaLink
     Assembler User's Manual and MetaLink Assembler software are 
     available free to Registered Buyer upon request for a one (1) year
     period from the invoice date.
     






     
     
                               NOTICE
     
     MetaLink Corp. reserves the right to make improvements in the
     software product described in this manual as well as the manual
     itself at any time and without notice.
     
     
     
     
     
     
     
             DISCLAIMER OF ALL WARRANTIES AND LIABILITY
     
     METALINK CORP. MAKES NO WARRANTIES, EITHER EXPRESSED OR IMPLIED,
     WITH RESPECT TO THIS MANUAL OR WITH RESPECT TO THE SOFTWARE 
     DESCRIBED IN THIS MANUAL, ITS QUALITY, PERFORMANCE, MERCHANTABILITY,
     OR FITNESS FOR ANY PARTICULAR PURPOSE.  METALINK CORP. SOFTWARE
     IS SOLD OR LICENSED "AS IS".  IN NO EVENT SHALL METALINK CORP. BE
     LIABLE FOR INCIDENTAL OR CONSEQUENTIAL DAMAGES RESULTING FROM ANY
     DEFECT IN THE SOFTWARE.
     
     
     
     
     
     
     
      
     
     
     
     
     Copyright (c) 1984, 1985, 1986, 1987, 1988, 1989, 1990 MetaLink Corp.
     
     All rights are reserved.  This manual may not, in whole or part, 
     be copied, photocopied, reproduced, translated, or reduced to any
     electronic medium or machine readable form without the prior 
     agreement and written permission of MetaLink Corp.
     
     
     
     
     
               MS-DOS is a trademark of Microsoft,  Inc.
     
               IBM is a registered trademark of IBM Corp.
     
               Intel is a registered trademark of Intel Corp.
     
               MetaLink is a trademark of MetaLink Corp.









                           T A B L E   O F   C O N T E N T S 
            
              1. 8051 OVERVIEW............................................1-1
                 1.1. Introduction........................................1-1
                 1.2. 8051 Architecture...................................1-2
                 1.3. Summary of the 8051 Family of Components............1-4
                 1.4. References..........................................1-5
            
              2. 8051 CROSS ASSEMBLER OVERVIEW............................2-1
                 2.1. Introduction........................................2-1
                 2.2. Symbols.............................................2-1
                 2.3. Labels..............................................2-2
                 2.4. Assembler Controls..................................2-3
                 2.5. Assembler Directives................................2-3
                 2.6. 8051 Instruction Mnemonics..........................2-4
                 2.7. Bit Addressing......................................2-6
                 2.8. ASCII Literals......................................2-6
                 2.9. Comments............................................2-6
                 2.10. The Location Counter...............................2-7
                 2.11. Syntax Summary.....................................2-7
                 2.12. Numbers and Operators..............................2-7
                 2.13. Source File Listing...............................2-10
                 2.14. Object File.......................................2-11
            
              3. RUNNING THE 8051 CROSS ASSEMBLER.........................3-1
                 3.1. Cross Assembler Files...............................3-1
                 3.2. Minimum System Requirements.........................3-1
                 3.3. Running the Cross Assembler.........................3-1
                 3.4. Example Running the Cross Assembler.................3-3
                 3.5. DOS Hints and Suggestions...........................3-3
                 3.6. References..........................................3-4
            
              4. 8051 INSTRUCTION SET.....................................4-1
                 4.1. Notation............................................4-1
                 4.2. 8051 Instruction Set Summary........................4-4
                 4.3. Notes..............................................4-14
                 4.4. References.........................................4-14
            
              5. 8051 CROSS ASSEMBLER DIRECTIVES..........................5-1
                 5.1. Introduction........................................5-1
                 5.2. Symbol Definition Directives........................5-1
                 5.3. Segment Selection Directives........................5-4
                 5.4. Memory Reservation and Storage Directives...........5-5
                 5.5. Miscellaneous Directives............................5-7
                 5.6. Conditional Assembly Directives.....................5-8
            
              6. 8051 CROSS ASSEMBLER CONTROLS............................6-1
                 6.1. Introduction........................................6-1
                 6.2. Assembler Control Descriptions......................6-1
            





              7. 8051 CROSS ASSEMBLER MACRO PROCESSOR.....................7-1
                 7.1. Introduction........................................7-1
                 7.2. Macro Definition....................................7-1
                 7.3. Special Macro Operators.............................7-4
                 7.4. Using Macros........................................7-4
                      7.4.1. NESTING MACROS...............................7-4
                      7.4.2. LABELS IN MACROS.............................7-6
            
              8. 8051 CROSS ASSEMBLER ERROR CODES.........................8-1
                 8.1. Introduction........................................8-1
                 8.2. Explanation of Error Messages.......................8-2
            
            
            
            Appendices
            
              A. SAMPLE PROGRAM AND LISTING...............................A-1
                 A.1. Source File.........................................A-1
                 A.2. Source File Listing.................................A-4
            
              B. PRE-DEFINED BYTE AND BIT ADDRESSES.......................B-1
                 B.1. Pre-defined Byte Addresses..........................B-1
                 B.2. Pre-defined Bit Addresses..........................B-11
            
              C. RESERVED SYMBOLS.........................................C-1
            
              D. CROSS ASSEMBLER CHARACTER SET............................D-1
 






                                      CHAPTER 1
           
           
                                     8051 OVERVIEW
           
           1.1. Introduction
           
           The 8051 series of microcontrollers are highly integrated single 
           chip microcomputers with an 8-bit CPU, memory, interrupt 
           controller, timers, serial I/O and digital I/O on a single piece 
           of silicon. The current members of the 8051 family of components 
           include: 
           
                   80C152JA/JB/JC/JD, 83C152JA/JC, 80C157        
                   80C154, 83C154, 85C154
                   8044, 8344, 8744
                   80C451, 83C451, 87C451         
                   80C452, 83C452, 87C452 
                   8051, 8031, 8751, 80C51, 80C31, 87C51
                   80512, 80532
                   80515, 80535, 80C535, 80C515
                   80C517, 80C537
                   80C51FA, 83C51FA, 87C51FA, 83C51FB, 87C51FB, 83C51FC, 87C51FC
                   8052, 8032, 8752
                   80C321, 80C521, 87C521, 80C541, 87C541 
                   8053, 9761, 8753
                   80C552, 83C552, 87C552
                   80C652, 83C652, 87C652
                   83C654, 87C654
                   83C751, 87C751
                   83C752, 87C752
                   80C851, 83C851
           
           All members of the 8051 series of microcontrollers share a common 
           architecture.  They all have the same instruction set, addressing 
           modes, addressing range and memory spaces.  The primary 
           differences between different 8051 based products are the amount 
           of memory on chip, the amount and types of I/O and peripheral 
           functions, and the component's technology (see Table 1-1).  
           
           In the brief summary of the 8051 architecture that follows, the 
           term 8051 is used to mean collectively all available members of 
           the 8051 family.  Please refer to reference (1) for a complete 
           description of the 8051 architecture and the specifications for 
           all the currently available 8051 based products.  









           
      
      
                                          1-1


      
      
      
           1.2. 8051 Architecture
           
           The 8051 is an 8-bit machine.  Its memory is organized in bytes 
           and practically all its instruction deal with byte quantities.  
           It uses an Accumulator as the primary register for instruction 
           results. Other operands can be accessed using one of the four 
           different addressing modes available:  register implicit, direct, 
           indirect or immediate.  Operands reside in one of the five memory 
           spaces of the 8051.
           
           The five memory spaces of the 8051 are: Program Memory, External 
           Data Memory, Internal Data Memory, Special Function Registers and 
           Bit Memory.
           
           The Program Memory space contains all the instructions, immediate 
           data and constant tables and strings.  It is principally 
           addressed by the 16-bit Program Counter (PC), but it can also be 
           accessed by a few instructions using the 16-bit Data Pointer 
           (DPTR).  The maximum size of the Program Memory space is 64K 
           bytes.  Several 8051 family members integrate on-chip some amount 
           of either masked programmed ROM or EPROM as part of this memory 
           space (refer to Table 1-1).
           
           The External Data Memory space contains all the variables, 
           buffers and data structures that can't fit on-chip.  It is 
           principally addressed by the 16-bit Data Pointer (DPTR), although 
           the first two general purpose register (R0,R1) of the currently 
           selected register bank can access a 256-byte bank of External 
           Data Memory.  The maximum size of the External Data Memory space 
           is 64Kbytes.  External  data memory can only be accessed using 
           the indirect addressing mode with the DPTR, R0 or R1.
           
           The Internal Data Memory space is functionally the most important 
           data memory space.  In it resides up to four banks of general 
           purpose registers, the program stack, 128 bits of the 256-bit 
           memory, and all the variables and data structures that are 
           operated on directly by the program.  The maximum size of the 
           Internal Data Memory  space is 256-bytes.  However, different 
           8051 family members integrate different amounts of this memory 
           space on chip (see Amnt of RAM in Table 1-1).  The register 
           implicit, indirect and direct addressing modes can be used in 
           different parts of the Internal Data Memory space.
           
           The Special Function Register space contains all the on-chip 
           peripheral I/O registers as well as particular registers that 
           need program access.  These registers include the Stack Pointer, 
           the PSW and the Accumulator. The maximum number of Special 
           Function Registers (SFRs) is 128, though the actual number on a 
           particular 8051 family member depends on the number and type of 
           peripheral functions integrated on-chip (see Table 1-1).  The 
           SFRs all have addresses greater than 127 and overlap the address 
           space of the upper 128 bytes of the Internal Data Memory space.  
           The two memory spaces are differentiated by addressing mode.  The 
           SFRs can only be accessed using the Direct addressing mode while 
           the upper 128 bytes of the Internal Data Memory (if integrated 
           on-chip) can only be accessed using the Indirect addressing mode.
      
      
                                          1-2


      
      
           
           The Bit Memory space is used for storing bit variables and flags.  
           There are specific instructions in the 8051 that operate only in 
           the Bit Memory space.  The maximum size of the Bit Memory space 
           is 256-bits.  128 of the bits overlap with 16-bytes of the 
           Internal Data Memory space and 128 of the bits overlap with 16 
           Special Function Registers.  Bits can only be accessed using the 
           bit instructions and the Direct addressing mode.
           
           The 8051 has a fairly  complete set of arithmetic and logical 
           instructions.  It includes an 8X8 multiply and an 8/8 divide.  
           The 8051 is particularly good at processing bits (sometimes 
           called Boolean Processing).  Using the Carry Flag in the PSW as a 
           single bit accumulator, the 8051 can move and do logical 
           operations between the Bit Memory space and the Carry Flag.  Bits 
           in the Bit Memory space can also be used as general purpose flags 
           for the test bit and jump instructions.
           
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          1-3


      
      
      
           Except for the MOVE instruction, the 8051 instructions can only 
           operate on either the Internal Data Memory space or the Special 
           Function Registers.  The MOVE instruction operates in all memory 
           spaces, including the External Memory space and Program Memory 
           space.
           
           Program control instructions include the usual unconditional 
           calls and jumps as well as conditional relative jumps based on 
           the Carry Flag, the Accumulator's zero state, and the state of 
           any bit in the Bit Memory space.  Also available is a Compare and 
           Jump if Not Equal instruction and a Decrement Counter and Jump if 
           Not Zero loop instruction.  See Chapter 4 for a description of 
           the complete 8051 instruction set.
           
           1.3. Summary of the 8051 Family of Components
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          1-4


      
      
      
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
                         Table 1-1: 8051 Family of Components
           
           
           1.4. References
           
           1. Intel Corp., 8-Bit Embedded Controllers, 1990.
           2. Siemens Corp., Microcontroller Component 80515, 1985. 
           3. AMD Corp., Eight-Bit 80C51 Embedded Processors, 1990.
           4. Signetics Corp., Microcontroller Users' Guide, 1989.
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          1-5








                                       CHAPTER 2
           
           
                             8051 CROSS ASSEMBLER OVERVIEW
           
           
           2.1. Introduction
           
           The 8051 Cross Assembler takes an assembly language source file 
           created with a text editor and translates it into a machine 
           language object file. This translation process is done in two 
           passes over the source file.  During the first pass, the Cross 
           Assembler builds a symbol table from the symbols and labels used 
           in the source file.  It's during the second pass that the Cross 
           Assembler actually translates the source file into the machine 
           language object file.  It is also during the second pass that the 
           listing is generated.
           
           The following is a discussion of the syntax required by the Cross 
           Assembler to generate error free assemblies.
           
           
           2.2. Symbols
           
           Symbols are alphanumeric representations of numeric constants, 
           addresses, macros, etc.  The legal character set for symbols is 
           the set of letters, both upper and lower case (A..Z,a..z), the 
           set of decimal numbers (0..9) and the special characters, 
           question mark (?) and underscore (_).  To ensure that the Cross 
           Assembler can distinguish between a symbol and a number, all 
           symbols must start with either a letter or special character (? 
           or _).  The following are examples of legal symbols:
           
           PI
           Serial_Port_Buffer
           LOC_4096
           ?_?_?
                 
           In using a symbol, the Cross Assembler converts all letters to 
           upper case. As a result, the Cross Assembler makes no distinction 
           between upper and lower case letters.  For example, the following 
           two symbols would be seen as the same symbol by the Cross 
           Assembler:
           
           Serial_Port_Buffer
           SERIAL_PORT_BUFFER
           
           Symbols can be defined only once.  Symbols can be up to 255 
           characters in length, though only the first 32 are significant.  
           Therefore, for symbols to be unique, they must have a unique 
           character pattern within the first 32 characters.  In the 
           following example, the first two symbols would be seen by the 
           Cross Assembler as duplicate symbols, while the third and fourth 
      
      
                                          2-1


      
      
      
           symbols are unique.
           
           BEGINNING_ADDRESS_OF_CONSTANT_TABLE_1
           BEGINNING_ADDRESS_OF_CONSTANT_TABLE_2
           
           CONSTANT_TABLE_1_BEGINNING_ADDRESS
           CONSTANT_TABLE_2_BEGINNING_ADDRESS
           
           There are certain symbols that are reserved and can't be defined 
           by the user.  These reserved symbols are listed in Appendix C and 
           include the assembler directives, the 8051 instruction mnemonics, 
           implicit operand symbols, and the following assembly time 
           operators that have alphanumeric symbols: EQ, NE, GT, GE, LT, LE, 
           HIGH, LOW, MOD, SHR, SHL, NOT, 
           AND, OR and XOR.  
           
           The reserved implicit operands include the symbols A, AB, C, 
           DPTR, PC, R0, R1, R2, R3, R4, R5, R6, R7, AR0, AR1, AR2, AR3, 
           AR4, AR5, AR6 and AR7.  These symbols are used primarily as 
           instruction operands.  Except for AB, C,  DPTR or PC, these 
           symbols can also be used to define other symbols (see EQU 
           directive in Chapter 5).
           
           The following are examples of illegal symbols with an explanation 
           of why they are illegal:
           
           1ST_VARIABLE        (Symbols can not start with a number.)
           ALPHA#              (Illegal character "#" in symbol.)
           MOV                 (8051 instruction mnemonic)
           LOW                 (Assembly operator)
           DATA                (Assembly directive)
           
           
           2.3. Labels
           
           Labels are special cases of symbols.  Labels are used only before 
           statements that have physical addresses associated with them.  
           Examples of such statements are assembly language instructions, 
           data storage directives (DB and DW), and data reservation 
           directives (DS and DBIT).  Labels must follow all the rules of 
           symbol creation with the additional requirement that they be 
           followed by a colon.  The following are legal examples of label 
           uses:
           
           TABLE_OF_CONTROL_CONSTANTS:
                           DB    0,1,2,3,4,5   (Data storage)
           MESSAGE:        DB    'HELP'        (Data storage)
           VARIABLES:      DS    10            (Data reservation)
           BIT_VARIABLES:  DBIT  16            (Data reservation)
           START:          MOV   A,#23         (Assembly language instruction)
           
           
           
           
           2.4. Assembler Controls
           
      
      
                                          2-2


      
      
      
           Assembler controls are used to control where the Cross Assembler 
           gets its input source file, where it puts the object file, and 
           how it formats the listing file.  Table 2-1 summarizes the 
           assembler controls available.  Refer to Chapter 6 for a detailed 
           explanation of the controls.
           
           
           
           
           
           
           
           
           
           
           
           
           
                          Table 2-1: Summary of Cross Assembler Controls
           
           
           As can be seen in Table 2-1, all assembler controls are prefaced 
           with a dollar sign ($). No spaces or tabs are allowed between the 
           dollar sign and the body of the control.  Also, only one control 
           per line is permitted.  However, comments can be on the same line 
           as a control.  The following are examples of assembler controls:
           
           $TITLE(8051 Program Ver. 1.0)
           $LIST
           $PAGEWIDTH(132)
           
           
           2.5. Assembler Directives
           
           Assembler directives are used to define symbols, reserve memory 
           space, store values in program memory and switch between 
           different memory spaces.  There are also directives that set the 
           location counter for the active segment and identify the end of 
           the source file.  Table 2-2 summarizes the assembler directives 
           available.  These directives are fully explained in Chapter 5.
           
           
           
           
           
           
           
           
           
           
           
           
                         Table 2-2: Summary of Cross Assembler Directives
           
           
           Only one directive per line is allowed, however comments may be 
      
      
                                          2-3


      
      
      
           included.  The following are examples of assembler directives:
           
           TEN       EQU       10
           RESET     CODE      0
                     ORG       4096
           
           
           2.6. 8051 Instruction Mnemonics
           
           The standard 8051 Assembly Language Instruction mnemonics plus 
           the generic CALL and JMP instructions are recognized by the Cross 
           Assembler and are summarized in Table 2-3. See Chapter 4 for the 
           operation of the individual instructions.
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          2-4


            
      
      
      
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
           
                            Table 2-3: 8051 Instructions and Mnemonics
           
           When the Cross Assembler sees a generic CALL or JMP instruction, 
           it will try to translate the instruction into its most byte 
           efficient form.  The Cross Assembler will translate a CALL into 
           one of two instructions (ACALL or LCALL) and it will translate a 
           generic JMP into one of three instructions (SJMP, AJMP or LJMP).  
           The choice of instructions is based on which one is most byte 
           efficient.  The generic CALL or JMP instructions saves the 
           programmer the trouble of determining which form is best.
           
           However, generic CALLs and JMPs do have their limitations.  While 
           the byte efficiency algorithm works well for previously defined 
           locations, when the target location of the CALL or JMP is a forward
           location (a location later on in the program), the assembler has no
           way of determining the best form of the instruction.  In this case
           the Cross Assembler simply puts in the long version (LCALL or LJMP)
           of the instruction, which may not be the most byte efficient.  NOTE
           that the generic CALLs and JMPs must not be used for the 751/752
           device as LCALL and LJMP are not legal instructions for those
           devices.  Instead use ACALL and AJMP explicitly.
           
           For instructions that have operands, the operands must be 
           separated from the mnemonic by at least one space or tab.  For 
           instructions that have multiple operands, each operand must be 
           separated from the others by a comma.  
           
           Two addressing modes require the operands to be preceded by 
           special symbols to designate the addressing mode.  The AT sign 
           (@) is used to designate the indirect addressing mode.  It is 
           used primarily with Register 0 and Register 1 (R0, R1), but is 
           can also be used with the DPTR in the MOVX and the Accumulator in 
           MOVC and JMP @A+DPTR instructions.  The POUND sign (#) is used to 
           designate an immediate  operand.  It can be used to preface 
           either a number or a symbol representing a number.
           
           A third symbol used with the operands actually specifies an 
           operation.  The SLASH (/) is used to specify that the contents of 
           a particular bit address is to be complemented before the 
      
                                          2-5


      
      
      
           instruction operation.  This is used with the ANL and ORL bit 
           instructions.
           
           Only one assembly language instruction is allowed per line.  
           Comments are allowed on the same line as an instruction, but only 
           after all operands have been specified.  The following are 
           examples of instruction statements:
           
           START:    LJMP      INIT
                     MOV       @R0,Serial_Port_Buffer
                     CJNE      R0 , #TEN, INC_TEN
                     ANL       C,/START_FLAG
                     CALL      GET_BYTE
                     RET
           
           
           2.7. Bit Addressing
           
           The period (.) has special meaning to the Cross Assembler when 
           used in a symbol.  It is used to explicitly specify a bit in a 
           bit-addressable symbol.  For example, it you wanted to specify 
           the most significant bit in the Accumulator, you could write 
           ACC.7, where ACC was previously defined as the Accumulator 
           address.  The same bit can also be selected using the physical 
           address of the byte it's in.  For example, the Accumulator's 
           physical address is 224.  The most significant bit of the 
           Accumulator can be selected by specifying 224.7.  If the symbol 
           ON was defined to be equal to the value 7, you could also specify 
           the same bit by either ACC.ON or 224.ON.
           
           
           2.8. ASCII Literals
           
           Printable characters from the ASCII character set can be used 
           directly as an immediate operand, or they can used to define 
           symbols or store ASCII bytes in Program Memory.  Such use of the 
           ASCII character set is called ASCII literals.  ASCII literals are 
           identified by the apostrophe (') delimiter.  The apostrophe 
           itself can be used as an ASCII literal.  In this case, use two 
           apostrophes in a row.  Below are examples of using ASCII 
           literals.
           
                     MOV  A,#'m'    ;Load A with 06DH (ASCII m)
           QUOTE     EQU  ''''      ;QUOTE defined as 27H (ASCII single quote)
                     DB   '8051'    ;Store in Program Memory
           
           
           2.9. Comments
           
           Comments are user defined character strings that are not 
           processed by the Cross Assembler.  A comment begins with a 
           semicolon ( ; )  and ends at the carriage return/line feed pair 
           that terminates the line.  A comment can appear anywhere in a 
           line, but it has to be the last field.  The following are 
           examples of comment lines:
           
      
      
                                          2-6


            
      
      
           ; Begin initialization routine here
           $TITLE(8051 Program Vers. 1.0)          ;Place version number here
           TEN       EQU       10                  ;Constant
                     ; Comment can begin anywhere in a line
                     MOV  A,Serial_Port_Buffer     ; Get character
           
           
           2.10. The Location Counter
           
           The Cross Assembler keeps a location counter for each of the five 
           segments (code, internal data, external data, indirect internal 
           data and bit data).  Each location counter is initialized to zero 
           and can be modified using Assembler Directives described in 
           Chapter 5.
           
           The dollar sign ($) can be used to specify the current value of 
           the location counter of the active segment.  The following are 
           examples of how this can be used:
           
                     JNB  FLAG,$        ;Jump on self until flag is reset
           CPYRGHT:  DB   'Copyright, 1983'
           CPYRGHT_LENGTH
                     EQU  $-CPYRGHT-1   ;Calculate length of copyright message
              
           
           
           2.11. Syntax Summary
           
           Since the Cross Assembler essentially translates the source file 
           on a line by line basis, certain rules must be followed to ensure 
           the translation process is done correctly.  First of all, since 
           the Cross Assembler's line buffer is 256 characters deep, there 
           must always be a carriage return/line feed pair within the first 
           256 columns of the line.
           
           A legal source file line must begin with either a control, a 
           symbol, a label, an instruction mnemonic, a directive, a comment 
           or it can be null (just the carriage return/line feed pair).  Any 
           other beginning to a line will be flagged as an error.  
           
           While a legal source file line must begin with one of the above 
           items, the item doesn't have to begin in the first column of the 
           line.  It only must be the first field of the line.  Any number 
           (including zero) of spaces or tabs, up to the maximum line size, 
           may precede it.
           
           Comments can be placed anywhere, but they must be the last field 
           in any line.
           
           
           2.12. Numbers and Operators
           
           The Cross Assembler accepts numbers in any one of four radices: 
           binary, octal, decimal and hexadecimal.  To specify a number in a 
           specific radix, the number must use the correct digits for the 
           particular radix and immediately following the number with its 
      
      
                                          2-7


      
      
      
           radix designator.  Decimal is the default radix and the use of 
           its designator is optional.  An hexadecimal number that would 
           begin with a letter digit must be preceded by a 0 (zero) to 
           distinguish it from a symbol. The internal representation of 
           numbers is 16-bits, which limits the maximum number possible.  
           Table 2-4 summarizes the radices available.
           
                                                              MAXIMUM LEGAL
           RADIX          DESIGNATOR      LEGAL DIGITS            NUMBER
           -----------    ----------      ------------     -----------------
           Binary             B           0,1              1111111111111111B
           Octal             O,Q          0,1,2,3,4,5,          177777O
                                          6,7                   177777Q
           Decimal        D,(default)     0,1,2,3,4,5,           65535D
                                          6,7,8,9                65535
           Hexadecimal        H           0,1,2,3,4,5,           0FFFFH
                                          6,7,8,9,A,B,        
                                          C,D,E,F             
           
                                Table 2-4: Cross Assembler Radices
           
           
           No spaces or tabs are allowed between the number and the radix 
           designator.  The letter digits and radix designators can be in 
           upper or lower case.  The following examples list the decimal 
           number 2957 in each of the available radices:
           
           
           101110001101B            (Binary)
           5615o or 5615Q           (Octal)
           2957 or 2957D            (Decimal)
           0B8DH, 0b8dh             (Hexadecimal)
           
           When using radices with explicit bit symbols, the radix 
           designator follows the byte portion of the address as shown in 
           the following examples:
           
           0E0H.7         Bit seven of hexadecimal address 0E0
           200Q.ON        Bit ON of octal address 200
           
           The Cross Assembler also allows assembly time evaluation of 
           arithmetic expressions up to thirty-two levels of embedded 
           parentheses.  All calculations use integer numbers and are done 
           in sixteen bit precision.  
           
           OPERATOR SYMBOL          OPERATION
           ---------------          ------------------------
                 +                  Addition
                                    Unary positive
                 -                  Subtraction
                                    Unary negation (2's complement)
                 *                  Multiplication
                 /                  Integer division (no remainder)
                MOD                 Modulus (remainder of integer division)
                SHR                 Shift right
                SHL                 Shift left
      
      
                                          2-8


      
      
      
                NOT                 Logical negation (1's complement)
                AND                 Logical and
                OR                  Inclusive or
                XOR                 Exclusive or
                LOW                 Low order 8-bits
                HIGH                High order 8-bits
                EQ, =               Relational equal
                NE, <>              Relational not equal
                GT, >               Relational greater than
                GE, >=              Relational greater than or equal
                LT, <               Relational less than
                LE, <=              Relational less than or equal
                ( )                 Parenthetical statement
           
                               Table 2-5: Assembly Time Operations
           
           
           The relational operators test the specified values and return 
           either a True or False.  False is represented by a zero value, 
           True is represented by a non zero value (the True condition 
           actually returns a 16-bit value with every bit set; i.e., 
           0FFFFH).  The relational operators are used primarily with the 
           Conditional Assembly capability of the Cross Assembler.
           
           Table 2-5 lists the operations available while Table 2-6 lists 
           the operations precedence in descending order.  Operations with 
           higher precedence are done first.  Operations with equal 
           precedence are evaluated from left to right.
           
                     OPERATION                PRECEDENCE
                     ---------                ----------
                        (,)                   HIGHEST
                     HIGH,LOW
                     *,/,MOD,SHR,SHL
                     +,-
                     EQ,LT,GT,LE,GE,NE,=,<,>,<=,>=,<>
                     NOT
                     AND
                     OR,XOR                   LOWEST
           
                                 Table 2-6: Operators Precedence
           
           
           The following are examples of all the available operations and 
           their result:
           
           HIGH(0AADDH)        will return a result of 0AAH
           LOW(0AADDH)         will return a result of 0DDH
           7*4                 will return a result of 28
           7/4                 will return a result of 1
           7 MOD 4             will return a result of 3
           1000B SHR 2         will return a result of 0010B
           1010B SHL 2         will return a result of 101000B
           10+5                will return a result of 15
           +72                 will return a result of 72
           25-17               will return a result of 8 
      
      
                                          2-9


            
      
      
           -1                  will return a result of 1111111111111111B
           NOT 1               will return a result of 1111111111111110B
           7 EQ 4, 7 = 4       will return a result of 0
           7 LT 4, 7 < 4       will return a result of 0
           7 GT 4, 7 > 4       will return a result of 0FFFFH
           7 LE 4, 7 <= 4      will return a result of 0
           7 GE 4, 7 >= 4      will return a result of 0FFFFH
           7 NE 4, 7 <> 4      will return a result of 0FFFFH
           1101B AND 0101B     will return a result of 0101B
           1101B OR 0101B      will return a result of 1101B
           1101B XOR 0101B     will return a result of 1000B
           
           
           2.13. Source File Listing
           
           The source file listing displays the results of the Cross 
           Assembler translation.  Every line of the listing includes a copy 
           of the original source line as well as a line number and the 
           Cross Assembler translation.
           
           For example, in translating the following line taken from the 
           middle of a source file:
           
           TRANS:    MOV  R7,#32         ;Set up pointer
           
           the listing will print:
           
           002F 7920         152   TRANS:  MOV   R1,#32        ;Set up pointer
           
           The '002F' is the current value of the location counter in 
           hexadecimal.   The '7920' is the translated instruction, also in 
           hexadecimal.  The '152' is the decimal line number of the current 
           assembly.  After the line number is a copy of the source file 
           line that was translated. 
           
           Another example of a line in the listing file is as follows:
           
           015B 13      =1 267 +2          RRC   A
           
           Here we see two additional fields.  The '=1' before the line 
           number gives the current nesting of include files.  The '+2' 
           after the line number gives the current macro nesting.  This line 
           essentially says that this line comes from a second level nesting 
           of a macro that is part of an include file.
           
           Another line format that is used in the listing is that of symbol 
           definition.  In this case the location counter value and 
           translated instruction fields described above are replaced with 
           the definition of the symbol.  The following are examples of 
           this:
           
             00FF             67   MAX_NUM      EQU       255
             REG              68   COUNTER      EQU       R7
           
           The '00FF' is the hexadecimal value of the symbol MAX_NUM.  
           Again, '67'is the decimal line number of the source file and the 
      
      
                                          2-10


      
      
      
           remainder of the first line is a copy of the source file.  In the 
           second line above, the 'REG' shows that the symbol COUNTER was 
           defined to be a general purpose register.
           
           Optionally, a listing can have a page header that includes the 
           name of the file being assembled, title of program, date and page 
           number.  The header and its fields are controlled by specific 
           Assembler Controls (see Chapter 6).
           
           The default case is for a listing to be output as a file on the 
           default drive with the same name as the entered source file and 
           an extension of .LST.  For example, if the source file name was 
           PROGRAM.ASM, the listing file would be called PROGRAM.LST.  Or if 
           the source file was called MODULE1, the listing file would be 
           stored as MODULE1.LST.  The default can be changed using the 
           $NOPRINT and $PRINT() Assembler Controls (see Chapter 6).
           
           
           2.14. Object File
           
           The 8051 Cross Assembler also creates a machine language object 
           file.  The format of the object file is standard Intel 
           Hexadecimal.  This Hexadeciaml file can be used to either program 
           EPROMs using standard PROM Programmers for prototyping, or used 
           to pattern masked ROMs for production.
           
           The default case is for the object file to be output on the 
           default drive with the same name as the first source file and an 
           extension of .HEX.  For example, if the source file name was 
           PROGRAM.ASM, the object file would be called PROGRAM.HEX.  Or if 
           the source file was called MODULE1, the object file would be 
           stored as MODULE1.HEX.  The default can be changed using the 
           $NOOBJECT and $OBJECT() Assembler Controls (see Chapter 6).
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          2-11








                                       CHAPTER 3
           
           
               RUNNING THE 8051 CROSS ASSEMBLER ON PC-DOS/MS-DOS SYSTEMS
           
           3.1. Cross Assembler Files
           
           The floppy disk you receive with this manual is an 8 sector, 
           single-sided, double density disk.  This distribution disk will 
           contain the following files:
           
                ASM51.EXE           The Cross Assembler program itself
                MOD152              Source file for the $MOD152 control
                MOD154              Source file for the $MOD154 control
                MOD252              Source file for the $MOD252 control
                MOD44               Source file for the $MOD44 control
                MOD451              Source file for the $MOD451 control
                MOD452              Source file for the $MOD452 control
                MOD51               Source file for the $MOD51 control
                MOD512              Source file for the $MOD512 control
                MOD515              Source file for the $MOD515 control
                MOD517              Source file for the $MOD517 control
                MOD52               Source file for the $MOD52 control
                MOD521              Source file for the $MOD521 control
                MOD552              Source file for the $MOD552 control
                MOD652              Source file for the $MOD652 control
                MOD751              Source file for the $MOD751 control
                MOD752              Source file for the $MOD752 control
                MOD851              Source file for the $MOD851 control
           
           There will also be one or more files with an extension of .ASM.  
           These are sample programs.  Listings of these programs can be 
           found in Appendix A.
           
           DON'T USE THE DISTRIBUTION DISK.  MAKE WORKING AND BACKUP COPIES 
           FROM THE DISTRIBUTION DISK AND THEN STORE THE DISTRIBUTION DISK 
           IN A SAFE PLACE.
           
           
           3.2. Minimum System Requirements
           
              With DOS 2.0 or later - 96K RAM
              1 Floppy Disk Drive
           
           
           3.3. Running the Cross Assembler
           
           Once you've created an 8051 assembly language source text file in 
           accordance with the guidelines in Chapter 2, you are now ready to 
           run the Cross Assembler.  Make sure your system is booted and the 
           DOS prompt ( A> ) appears on the screen.  Place the disk with the 
           8051 Cross Assembler on it in the drive and simply type (in all 
           the following examples, the symbol <CR> is used to show where the 
      
      
                                          3-1


      
      
      
           ENTER key was hit):
           
           ASM51<CR>
           
           
           If the 8051 Cross Assembler disk was placed in a drive other than 
           the default drive, the drive name would have to be typed first.  
           For example, if the A drive is the default drive, and the 8051 
           Cross Assembler is in the B drive, you would then type:
           
           B:ASM51<CR>
           
           After loading the program from the disk, the program's name, its 
           version number and general copyright information will be dis-
           played on the screen.  The Cross Assembler then asks for the 
           source file name to begin the assembly process. 
           
           Source file drive and name [.ASM]: 
           
           At this point, if you have only one floppy disk drive and the 
           8051 Cross Assembler and source files are on separate disks, 
           remove the disk with the 8051 Cross Assembler on it and replace 
           it with your source file disk.
           
           Next, enter the source file name.  If no extension is given, the 
           Cross Assembler will assume an extension of .ASM.  If no drive is 
           given, the Cross Assembler will assume the default drive.  Since 
           in every case where no drive is given, the Cross Assembler 
           assumes the default drive, it is generally a good practice to 
           change the default drive to the drive with your source files.
           
           An alternative method for entering the source file is in the 
           command line.  In this case, after typing in ASM51, type in a 
           space and the source file name (again if no extension is given, 
           source file on the command line:
           
           A>ASM51 B:CONTROL.A51<CR>
           
           After the source file name has been accepted, the Cross Assembler 
           will begin the translation process.  As it starts the first pass 
           of its two pass process, it will print on the screen:
           
           First pass
           
           At the completion of the first pass, and as it starts its second 
           pass through the source file, the Cross Assembler will display:
           
           Second pass
           
           When second pass is completed, the translation process is done 
           and the Cross Assembler will print the following message:
           
           ASSEMBLY COMPLETE, XX ERRORS FOUND
           
           XX is replaced with the actual number of errors that were found.  
           Disk I/O may continue for a while as the Cross Assembler appends 
      
      
                                          3-2


      
      
      
           the symbol table to the listing file.
           
           
           3.4. Example Running the Cross Assembler
           
           The following is an example of an actual run.  The Cross 
           Assembler will take the source file SAMPLE.ASM from Drive A 
           (default drive).
           
           Again, the symbol <CR> is used to show where the ENTER key was 
           hit.
           
           A>ASM51<CR>
           
           
           
           
                       8 0 5 1    C R O S S    A S S E M B L E R
           
           
                                     Version  1.2
           
                (c) Copyright 1984, 1985, 1986, 1987, 1988, 1989, 1990
           
                                 MetaLink Corporation
           
           
           
           Source file drive and name [.ASM]: sample<CR>
           
           First pass
           
           Second pass
           
           ASSEMBLY COMPLETE, 0 ERRORS FOUND
           
           
           3.5. DOS Hints and Suggestions
           
           If you are using DOS 2.0 or later, you may want to use the BREAK 
           ON command before you run the Cross Assembler.  This will allow 
           you to abort (Ctrl-Break) the Cross Assembler at any time.  
           Otherwise, you will only be able to abort the Cross Assembler 
           after it completes a pass through the source file.  If you are 
           assembling a large file, this could cause you a several minute 
           wait before the Cross Assembler aborts.
           
           The reason for this it that the  default condition  for DOS  to 
           recognizes a Ctrl-Break is when the program (in this case the 
           Cross Assembler) does keyboard, screen or printer I/O.  
           Unfortunately, the assembler does this very rarely (once each 
           pass).  By using the BREAK ON command, DOS will recognize a Ctrl-
           Break for all I/O, including disk I/O.  Since the Cross Assembler 
           is constantly doing disk I/O, with BREAK ON you can abort almost 
           immediately by hitting the Ctrl-Break keys.
           
      
      
                                          3-3


      
      
      
           So much for the good news.  However, aborting a program can cause 
           some undesirable side-effects.  Aborting a program while files 
           are open causes DOS to drop some information about the open 
           files.  This results in disk sectors being allocated when they 
           are actually free.  Your total available disk storage shrinks.  
           You should make the practice of running CHKDSK with the /F switch 
           periodically to recover these sectors.
           
           The Cross Assembler run under DOS 2.0 or later supports 
           redirection. You can specify the redirection on the command line.  
           Use the following form:
           
           ASM51 <infile >outfile
           
           "infile" and "outfile" can be any legal file designator. The 
           Cross Assembler will take its input from the "infile" instead of 
           the keyboard and will send its output to "outfile" instead of the 
           screen.
           
           Note that redirection of input in ASM51 is redundant since the 
           assembler is an absolute assembler and has no command line 
           options other than the file name argument.
           
           Output redirection is useful for speeding up the assembly 
           process.  Because assembly-time errors are directed to std_err in 
           DOS, an error listing cannot be redirected to a file
           
           To make the .lst file serve as an error-only file, use the Cross 
           Assembler Controls $PRINT (create a list file) $NOLIST (turn the 
           listing off).  Use the Cross Assembler Controls $NOSYMBOLS to 
           further compress the error-only listing resulting from the 
           manipulation of the list file controls.  See Chapter 6 for more 
           information.  The errors will be listed in the .lst file, as 
           usual.
           
           If the control $NOPRINT (see Chapter 6) is active, all error 
           messages are send to the screen.  
           
            
           
           3.6. References
           
           1. IBM Corp., Disk Operating System, Version 1.10, May 1982.
           2. IBM Corp., Disk Operating System, Version 2.00, January 1983.
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          3-4





                                       CHAPTER 4
           
           
                                 8051 INSTRUCTION SET
           
           
           4.1. Notation
           
           Below is an explanation of the column headings and column 
           contents of the 8051 Instruction Set Summary Table that follows 
           in this chapter.
           
           
           MNEMONIC
           
           The MNEMONIC column contains the 8051 Instruction Set Mnemonic 
           and a brief description of the instruction's operation.
           
           
           OPERATION
           
           The OPERATION column describes the 8051 Instruction Set in unam-
           biguous symbology.  Following are the definitions of the symbols 
           used in this column.
           
           <n:m>                  Bits of a register inclusive.  For 
                                  example, PC<10:0> means bits 0 through 10                        
                                  inclusive of the PC. Bit 0 is always the 
                                  least significant bit.
             +                    Binary addition
             -                    Binary 2s complement subtraction
             /                    Unsigned integer division
             X                    Unsigned integer multiplication
             ~                    Binary complement (1s complement)
             ^                    Logical And
             v                    Inclusive Or
             v                    Exclusive Or
             >                    Greater than
            <>                    Not equal to
             =                    Equals
            ->                    Is written into.  For example, A + SOper -
                                  > A means the result of the binary                        
                                  addition between A and the Source Operand 
                                  is written into A.
           
             A                    The 8-bit Accumulator Register.
            AC                    The Auxiliary Carry Flag in the Program 
                                  Status Word
            CF                    The Carry Flag in the Program Status Word
           DOper                  The Destination Operand used in the 
                                  instruction.
           DPTR                   16-bit Data Pointer
           Intrupt Active Flag    Internal Flag that holds off interrupts 
      
      
                                          4-1



      
                                  until the Flag is cleared.
           Jump Relative to PC    A Jump that can range between -128 bytes 
                                  and +127 bytes from the PC value of                        
                                  the next instruction.
           Paddr                  A 16-bit Program Memory address
            PC                    The 8051 Program Counter. This 16-bit 
                                  register points to the byte in the                        
                                  Program Memory space that is fetched as 
                                  part of the instruction stream.
           PM(addr)               Byte in Program Memory space pointed 
                                  to by addr.
           Remainder              Integer remainder of unsigned integer division
           SOper                  The Source Operand used in the instruction.
            SP                    8-bit Stack Pointer
           STACK                  The Last In First Out data structure that 
                                  is controlled by the 8-bit Stack                        
                                  Pointer (SP).  Sixteen bit quantities are 
                                  pushed on the stack low byte first.
           
            
           DEST ADDR MODE/SOURCE ADDR MODE
           
           These two columns specify the Destination and Source Addressing 
           Modes, respectively, that are available for each instruction.
           
           AB             The Accumulator-B Register pair.
           Accumulator    Operand resides in the accumulator
           Bit Direct     Operand is the state of the bit specified by the 
                          Bit Memory address.
           Carry Flag     Operand is the state of the 1-bit Carry flag in 
                          the Program Status Word (PSW).
           Data Pointer   Operand resides in the 16-bit Data Pointer 
                          Register.
           Direct         Operand is the contents of the specified 8-bit 
                          Internal Data Memory address from 0                
                          (00H) to 127 (7FH) or a Special Function Register 
                          address. 
           Indirect       Operand is the contents of the address contained 
                          in the register specified.
           Immediate      Operand is the next sequential byte after the 
                          instruction in Program Memory space
           Prog Direct    16-bit address in Program Memory Space.
           Prog Indir     Operand in Program Memory Space is the address 
                          contained in the register specified.
           Register       Operand is the contents of the register specified.
           Stack          Operand is on the top of the Stack.
           
           
           ASSEMBLY LANGUAGE FORM
           
           This column contains the correct format of the instructions that 
           are recognized by the Cross Assembler.
           
           A         Accumulator
           AB        Accumulator-B Register pair.
      
                                          4-2


      
      
      
           C         Carry Flag
           Baddr     Bit Memory Direct Address.
           Daddr     Internal Data Memory or Special Function Register 
                     Direct Address. 
           data      8-bit constant data.
           data16    16-bit constant data.
           DPTR      16-bit Data Pointer Register.
           PC        16-bit Program Counter.
           Paddr     16-bit Program Memory address
           Ri        Indirect Register. R0 or R1 are the only indirect 
                     registers.
           Roff      8-bit offset for Relative Jump.
           Rn        Implicit Register.  Each register bank has 8 general 
                     purpose registers, designated R0, R1, R2, R3, 
                     R4, R5, R6, R7.
           
           
           HEX OPCODE
           
           This column gives the machine language hexadecimal opcode for 
           each 8051 instruction.
           
           
           
           BYT
           
           This column gives the number of bytes in each 8051 instruction.
           
           
           CYC
           
           This column gives the number of cycles of each 8051 instruction. 
           The time value of a cycle is defined as 12 divided by the 
           oscillator frequency. For example, if running an 8051 family 
           component at 12 MHz, each cycle takes 1 microsecond.
           
           
           PSW
           
           This column identifies which condition code flags are affected by 
           the operation of the individual instructions.  The condition code 
           flags available on the 8051 are the Carry Flag, CF, the Auxiliary 
           Carry Flag, AC, and the Overflow Flag, OV.
           
           It should be noted that the PSW is both byte and bit directly 
           addressable.  Should the PSW be the operand of an instruction 
           that modifies it, the condition codes could be changed even if 
           this column states that the instruction doesn't affect them.
           
            0        Condition code is cleared
            1        Condition code is set
            *        Condition code is modified by instruction
            -        Condition code is not affected by instruction
           
           4.2. 8051 Instruction Set Summary
      
      
      
                                          4-3


            
      
      
      
           
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          4-4


            
      
      
      
           
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          4-5


            
      
      
      
           
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          4-6


            
      
      
      
           
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          4-7


            
      
      
      
           
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          4-8


            
      
      
      
           
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          4-9


            
      
      
      
           
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          4-10


            
      
      
      
           
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          4-11


            
      
      
      
           
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          4-12


      
      
         
         4.3. Notes
         
         
           1       There are 8 possible opcodes.  Starting with 11H as the 
         opcode base, the final opcode is formed by placing bits 8, 9 and 
         10 of the target address in bits 5, 6 and 7 of the opcode.  The 8 
         possible opcodes in hexadecimal are then: 11, 31, 51, 71, 91, B1, 
         D1, F1.
         
           2        There are 8 possible opcodes.  Starting with 01H as 
         the opcode base, the final opcode is formed by placing bits 8, 9 
         and 10 of the target address in bits 5, 6 and 7 of the opcode.  
         The 8 possible opcodes in hexadecimal are then: 01, 21, 41, 61, 
         81, A1, C1, E1.  
         
           3        The Carry Flag is set if the Destination Operand is 
         less than the Source Operand.  Otherwise the Carry Flag is 
         cleared.
         
           4        The Carry Flag is set if the BCD result in the 
         Accumulator is greater than decimal 99.
         
           5        The Overflow Flag is set if the B Register contains 
         zero (flags a divide by zero operation).  Otherwise the Overflow 
         Flag is cleared.
         
           6         If any of the condition code flags are specified as 
         the operand of this instruction, they will be reset by the 
         instruction if they were originally set.
         
           7         The high byte of the 16-bit product is placed in the 
         B Register, the low byte in Accumulator.
         
         
         4.4. References
         
         1. Intel Corp., Microcontroller Handbook, 1984.
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                        4-13








                                       CHAPTER 5
           
           
                            8051 CROSS ASSEMBLER DIRECTIVES
           
           5.1. Introduction
           
           The 8051 Cross Assembler Directives are used to define symbols, 
           reserve memory space, store values in program memory,  select 
           various memory spaces, set the current segment's location counter 
           and identify the end of the source file.
           
           Only one directive per line is allowed, however comments may be 
           included.  The remaining part of this chapter details the 
           function of each directive.
           
           
           5.2. Symbol Definition Directives
           
           EQU Directive
           
           The EQUate directive is used to assign a value to a symbol.  It 
           can also be used to specify user defined names for the  implicit 
           operand symbols predefined for the Accumulator (i.e., A) and the 
           eight General Purpose Registers (i.e., R0 thru R7).
           
           The format for the EQU directive is: symbol, followed by one or 
           more spaces or tabs, followed by EQU, followed by one or more 
           spaces or tabs, followed by a number, arithmetic expression, 
           previously defined symbol (no forward references allowed) or one 
           of the allowed implicit operand symbols (e.g., A, R0, R1, R2, R3, 
           R4, R5, R6, R7), followed by an optional comment.
           
           Below are examples of using the EQU Directive:
           
           TEN        EQU     10      ;Symbol equated to a number
           COUNTER    EQU     R7      ;User defined symbol for the implicit
                                      ;operand symbol R7.  COUNTER can now
                                      ;be used wherever it is legal to use
                                      ;R7.  For example the instruction
                                      ;INC R7 could now be written INC COUNTER.
           ALSO_TEN   EQU     TEN     ;Symbol equated to a previously defined
                                      ;symbol.
           FIVE       EQU     TEN/2   ;Symbol equated to an arithmetic exp.
           A_REG      EQU     A       ;User defined symbol for the implicit
                                      ;operand symbol A.
           ASCII_D    EQU     'D'     ;Symbol equated to an ASCII literal
           
           
           SET Directive
           
           Similar to the EQU directive, the SET directive is used to assign 
           a value or implicit operand to a user defined symbol.  The 
           difference however, is that with the EQU directive, a symbol can 
      
      
                                          5-1


      
      
      
           only be defined once.  Any attempt to define the symbol again 
           will cause the Cross Assembler to flag it as an error.  On the 
           other hand, with the SET directive, symbols are redefineable.  
           There is no limit to the number of times a symbol can be 
           redefined with the SET directive.
           
           The format for the SET directive is: symbol, followed by one or 
           more spaces or tabs, followed by SET, followed by one or more 
           spaces or tabs, followed by a number, arithmetic expression, 
           previously defined symbol (no forward references allowed) or one 
           of the allowed implicit operand symbols (e.g., A, R0, R1, R2, R3, 
           R4, R5, R6, R7), followed by an optional comment.
           
           Below are examples of using the SET Directive:
           
           POINTER   SET       R0          ;Symbol equated to register 0
           POINTER   SET       R1          ;POINTER redefined to register 1
           
           COUNTER   SET       1           ;Symbol initialized to 1
           COUNTER   SET       COUNTER+1   ;An incrementing symbol
           
           
           BIT Directive
           
           The BIT Directive assigns an internal bit memory direct address 
           to the symbol.  If the numeric value of the address is between 0 
           and 127 decimal, it is a bit address mapped in the Internal 
           Memory Space.  If the numeric value of the address is between 128 
           and 255, it is an address of a bit located in one of the Special 
           Function Registers.  Addresses greater than 255 are illegal and 
           will be flagged as an error.
           
           The format for the BIT Directive is: symbol, followed by one or 
           more spaces or tabs, followed by BIT, followed by one or more 
           spaces or tabs, followed by a number, arithmetic expression, or 
           previously defined symbol (no forward references allowed), 
           followed by an optional comment.
           
           Below are examples of using the BIT Directive:
           
           CF        BIT     0D7H         ;The single bit Carry Flag in PSW
           OFF_FLAG  BIT     6            ;Memory address of single bit flag
           ON_FLAG   BIT     OFF_FLAG+1   ;Next bit is another flag
           
           
           CODE Directive
           
           The CODE Directive assigns an address located in the Program 
           Memory Space to the symbol.  The numeric value of the address 
           cannot exceed 65535.
           
           The format for the CODE Directive is: symbol, followed by one or 
           more spaces or tabs, followed by CODE, followed by one or more 
           spaces or tabs, followed by a number, arithmetic expression, or 
           previously defined symbol (no forward references allowed), 
           followed by an optional comment.
      
      
                                          5-2


            
      
           
           Below are examples of using the CODE Directive:
           
           RESET     CODE      0
           EXTI0     CODE      RESET + (1024/16)
           
           
           DATA Directive
           
           The DATA Directive assigns a directly addressable internal memory 
           address to the symbol.  If the numeric value of the address is 
           between 0 and 127 decimal, it is an address of an Internal Data 
           Memory location.  If the numeric value of the address is between 
           128 and 255, it is an address of a Special Function Register.  
           Addresses greater than 255 are illegal and will be flagged as an 
           error.
           
           The format for the DATA Directive is: symbol, followed by one or 
           more spaces or tabs, followed by DATA, followed by one or more 
           spaces or tabs, followed by a number, arithmetic expression, or 
           previously defined symbol (no forward references allowed), 
           followed by an optional comment.
           
           Below are examples of using the DATA Directive:
           
           PSW         DATA      0D0H       ;Defining the Program Status address
           BUFFER      DATA      32         ;Internal Data Memory address
           FREE_SPAC   DATA      BUFFER+16  ;Arithmetic expression.
           
           
           IDATA Directive
           
           The IDATA Directive assigns an indirectly addressable internal 
           data memory address to the symbol.  The numeric value of the 
           address can be between 0 and 255 decimal.  Addresses greater than 
           255 are illegal and will be flagged as an error.
           
           The format for the IDATA Directive is: symbol, followed by one or 
           more spaces or tabs, followed by IDATA, followed by one or more 
           spaces or tabs, followed by a number, arithmetic expression, or 
           previously defined symbol (no forward references allowed), 
           followed by an optional comment.
           
           Below are examples of using the IDATA Directive:
           
           TOKEN      IDATA     60  
           BYTE_CNT   IDATA     TOKEN + 1
           ADDR       IDATA     TOKEN + 2
           
           
           XDATA Directive
           
           The XDATA Directive assigns an address located in the External 
           Data Memory Space to the symbol.  The numeric value of the 
           address cannot exceed 65535.
           
      
      
                                          5-3


      
      
      
           The format for the XDATA Directive is: symbol, followed by one or 
           more spaces or tabs, followed by XDATA, followed by one or more 
           spaces or tabs, followed by a number, arithmetic expression, or 
           previously defined symbol (no forward references allowed), 
           followed by an optional comment.
           
           Below are examples of using the XDATA Directive:
           
           USER_BASE      XDATA     2048
           HOST_BASE      XDATA     USER_BASE + 1000H
           
           
           5.3. Segment Selection Directives
            
           There are five Segment Selection Directives: CSEG, BSEG, DSEG, 
           ISEG, XSEG, one for each of the five memory spaces in the 8051 
           architecture.  The CSEG Directive is used to select the Program 
           Memory Space.  The BSEG Directive is used to select the Bit 
           Memory Space.  The DSEG Directive is used to select the directly 
           addressable Internal Data Memory Space.  The ISEG is used to 
           select the indirectly addressable Internal Data Memory Space.  
           The XSEG is used to select the External Data Memory Space.
           
           Each segment has its own location counter that is reset to zero 
           during the Cross Assembler program initialization.  The contents 
           of the location counter can be overridden by using the optional 
           AT after selecting the segment.
           
           The Program Memory Space, or CSEG, is the default segment and is 
           selected when the Cross Assembler is run.
           
           The format of the Segment Selection Directives are: zero or more 
           spaces or tabs, followed by the Segment Selection Directive, 
           followed by one or more spaces or tabs,  followed by the optional 
           segment location counter override AT command and value, followed 
           by an optional comment.
           
           The value of the AT command can be a number, arithmetic 
           expression or previously defined symbol (forward references are 
           not allowed).  Care should be taken to ensure that the location 
           counter does not advance beyond the limit of the selected 
           segment.
           
           Below are examples of the Segment Selection Directives:
           
           DSEG                           ;Select direct data segment using
                                          ;current location counter value.
           BSEG AT 32                     ;Select bit data segment forcing
                                          ;location counter to 32 decimal.
           XSEG AT (USER_BASE * 5) MOD 16 ;Arithmetic expressions can be
                                          ;used to specify location.
           
           
           5.4. Memory Reservation and Storage Directives
           
           
      
                                          5-4


            
      
      
           DS Directive
           
           The DS Directive is used to reserve space in the currently 
           selected segment in byte units.  It can only be used when ISEG, 
           DSEG or XSEG are the currently active segments.  The location 
           counter of the segment is advanced by the value of the directive.  
           Care should be taken to ensure that the location counter does not 
           advance beyond the limit of the segment.
           
           The format for the DS Directive is: optional label, followed by 
           one or more spaces or tabs, followed by DS, followed by one or 
           more spaces or tabs, followed by a number, arithmetic expression, 
           or previously defined symbol (no forward references allowed), 
           followed by an optional comment.
           
           Below is an example of using the DS Directive in the internal 
           Data Segment.  If, for example, the Data Segment location counter 
           contained 48 decimal before the example below, it would contain 
           104 decimal after processing the example.
           
                          DSEG           ;Select the data segment
                          DS        32   ;Label is optional
           SP_BUFFER:     DS        16   ;Reserve a buffer for the serial port
           IO_BUFFER:     DS        8    ;Reserve a buffer for the I/O
           
           
           DBIT Directive
           
           The DBIT Directive is used to reserve bits within the BIT 
           segment.  It can only be used when BSEG is the active segment.  
           The location counter of the segment is advanced by the value of 
           the directive.  Care should be taken to ensure that the location 
           counter does not advance beyond the limit of the segment.
           
           The format for the DBIT Directive is: optional label, followed by 
           one or more spaces or tabs, followed by DBIT, followed by one or 
           more spaces or tabs, followed by a number, arithmetic expression, 
           or previously defined symbol (no forward references allowed), 
           followed by an optional comment.
           
           Below  is  an example of using the DBIT Directive:
           
                          BSEG                ;Select the bit segment
                          DBIT      16        ;Label is optional
           IO_MAP:        DBIT      32        ;Reserve a bit buffer for I/O
           
           
           DB Directive 
           
           The DB Directive is used to store byte constants in the Program 
           Memory Space.  It can only be used when CSEG is the active 
           segment.
           
           The format for the DB Directive is: optional label, followed by 
           one or more spaces or tabs, followed by DB, followed by one or 
           more spaces or tabs,  followed by the byte constants that are 
      
      
                                          5-5


      
      
      
           separated by commas, followed by an optional comment.
           
           The byte constants can be numbers, arithmetic expressions, symbol 
           values or ASCII literals.  ASCII literals have to be delimited by 
           apostrophes ( ' ), but they can be strung together up to the 
           length of the line.
           
           Below are examples of using the DB Directive.  If an optional 
           label is used, its value will point to the first byte constant 
           listed.
           
           COPYRGHT_MSG:
                     DB        '(c) Copyright, 1984'    ;ASCII Literal
           RUNTIME_CONSTANTS:
                     DB        127,13,54,0,99           ;Table of constants
                     DB        17,32,239,163,49         ;Label is optional
           MIXED:    DB        2*8,'MPG',2*16,'abc'     ;Can mix literals & no.
           
           
           DW Directive 
           
           The DW Directive is used to store word constants in the Program 
           Memory Space.  It can only be used when CSEG is the active 
           segment.
           
           The format for the DW Directive is: optional label, followed by 
           one or more spaces or tabs, followed by DW, followed by one or 
           more spaces or tabs, followed by the word constants that are 
           separated by commas, followed by an optional comment.
           
           The word constants can be numbers, arithmetic expressions, symbol 
           values or ASCII literals.  ASCII literals must be delimited by 
           apostrophes ( ' ), but unlike the DB Directive, only a maximum of 
           two ASCII characters can be strung together.  The first character 
           is placed in the high byte of the word and the second character 
           is placed in the low byte.  If only one character is enclosed by 
           the apostrophes, a zero will be placed in the high byte of the 
           word.
           
           Below are examples of using the DW Directive.  If an optional 
           label is used, its value will point to the high byte of the first 
           word constant listed.
           
           JUMP_TABLE:    DW   RESET,START,END     ;Table of addresses
                          DW   TEST,TRUE,FALSE     ;Optional label
           RADIX:         DW   'H',1000H           ;1st byte contains 0
                                                   ;2nd byte contains 48H (H)
                                                   ;3rd byte contains 10H
                                                   ;4th byte contains 0
           
           
           5.5. Miscellaneous Directives
           
           
           ORG Directive
           
      
      
                                          5-6


      
      

           The ORG Directive is used to specify a value for the currently 
           active segment's location counter.  It cannot be used to select 
           segments like the directives above.  It can only be used within a 
           segment when the location counter needs to be changed.  Care 
           should be taken to ensure that the location counter does not 
           advance beyond the limit of the selected segment.
           
           The format of the ORG Directive is: zero or more spaces or tabs, 
           followed by ORG, followed by one or more spaces or tabs, followed 
           by a number, arithmetic expression, or previously defined symbol 
           (no forward references are allowed), followed by an optional 
           comment.
           
           Below are examples of the ORG directive.
           
                ORG  1000H                ;Location counter set at 4096 decimal
                ORG  RESET                ;Previously defined symbol
                ORG  BASE + MODULE_NO     ;Arithmetic expression
           
           
           USING DIRECTIVE
           
           The USING Directive is used to specify which of the four General 
           Purpose Register banks is used in the code that follows the 
           directive.  It allows the use of the predefined register symbols 
           AR0 thru AR7 instead of the register's direct addresses.  It 
           should be noted that the actual register bank switching must 
           still be done in the code.  This directive simplifies the direct 
           addressing of a specified register bank.
           
           The format of the USING Directive is: zero or more spaces or 
           tabs, followed by USING, followed by one or more spaces or tabs, 
           followed by a number, arithmetic expression, or previously 
           defined symbol (no forward references are allowed), followed by 
           an optional comment.
           
           The number, arithmetic expression, or previously defined symbol 
           must result in a number between 0 and 3 in order to specify one 
           of the four register banks in the 8051.
           
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          5-7


      
      
      
           The following table maps the specified value in the USING 
           directive with the direct addresses of the predefined symbols.
           
                Predefined |        USING Value                  |
                   Symbol  |    0         1         2         3  |
                   -----------------------------------------------
                     AR0        0         8        16        24
                     AR1        1         9        17        25
                     AR2        2        10        18        26
                     AR3        3        11        19        27
                     AR4        4        12        20        28
                     AR5        5        13        21        29
                     AR6        6        14        22        30
                     AR7        7        15        23        31
           
           
           Below are examples of the USING Directive:
           
                USING     0         ;Select addresses for Bank 0
                USING     1+1+1     ;Arithmetic expressions
           
           
           END Directive
           
           The END Directive is used to signal the end of the source program 
           to the Cross Assembler.  Every source program must have one and 
           only one END Directive.  A missing END Directive, as well as text 
           beyond the occurrence of the END Directive are not allowed and 
           will be flagged as errors.
           
           The format of the END Directive is: zero or more spaces or tabs, 
           followed by END, followed by an optional comment. All text must 
           appear in the source program before the occurrence of the END 
           Directive.
           
           Below is an example of the END Directive:
           
                   END         ;This is the End
           
           
           5.6. Conditional Assembly Directives
           
           IF, ELSE and ENDIF Directive
            
           The IF, ELSE and ENDIF directives are used to define conditional 
           assembly blocks.  A conditional assembly block begins with an IF 
           statement and must end with the ENDIF directive.  In between the 
           IF statement and ENDIF directive can be any number of assembly 
           language statements, including directives, controls, 
           instructions, the ELSE directive and nested IF-ENDIF conditional 
           assembly blocks.
           
           The IF statement starts with the keyword IF, followed by one or 
           more spaces or tabs, followed by a number, arithmetic expression, 
           or previously defined symbol (no forward references are allowed), 
           followed by an optional comment.  The number, arithmetic 
      
      
                                          5-8


      
      
      
           expression or symbol is evaluated and if found to be TRUE (non-
           zero),  the assembly language statements are translated up to the 
           next ELSE or ENDIF directives.  If the IF statement was evaluated 
           FALSE (zero), the assembly language statements are considered 
           null up to the next ELSE or ENDIF directives.
           
           If an optional ELSE appears in the conditional assembly block, 
           the assembly language statements following are handled oppositely 
           from the assembly language statements following the IF statement.  
           In other words, if the IF statement was evaluated TRUE, the 
           statements following it are translated, while the statements 
           following the ELSE will be handled as if they were null.  On the 
           other hand, if the IF statement was evaluated FALSE, only the 
           assembly language statements following the ELSE directive would 
           be translated.
           
           IF-ELSE-ENDIF conditional assembly blocks can be nested up to 255 
           levels deep.  The following are some examples of conditional 
           assembly blocks.  This first conditional assembly block simply 
           checks the symbol DEBUG.  If DEBUG is non-zero, the MOV and CALL 
           instructions will be translated by the Cross Assembler.
           
           IF (DEBUG)
                MOV    A,#25
                CALL   OUTPUT
           ENDIF
           
           The next example used the optional ELSE directive.  If 
           SMALL_MODEL is zero, only the statements following the ELSE 
           directive will be translated.
           
           IF (SMALL_MODEL)
                MOV  R0,#BUFFER
                MOV  A,@R0
           ELSE
                MOV  R0,#EXT_BUFFER
                MOVX A,@R0
           ENDIF
           
           The last example shows nested conditional assembly blocks.  
           Conditional assembly blocks can be nested up to 255 levels deep.  
           Every level of nesting must have balanced IF-ENDIF statements.
                                                        _
           IF (VERSION > 10)                             \
                CALL DOUBLE_PRECISION                     |    
                CALL UPDATE_STATUS      _                 |    
             IF (DEBUG)                  \                |
                CALL DUMP_REGISTERS       >  Nested       |     
             ENDIF                      _/   Block        |
           ELSE                                            >  Outer Block
                CALL SINGLE_PRECISION                     |
                CALL UPDATE_STATUS      _                 |
             IF (DEBUG)                  \                |
                CALL DUMP_REGISTERS       >   Nested      |
             ENDIF                      _/    Block       |
           ENDIF                                        _/
      
                                          5-9








                                       CHAPTER 6
           
           
                             8051 CROSS ASSEMBLER CONTROLS
           
           
           6.1. Introduction
           
           Assembler controls are used to control where the Cross Assembler 
           gets its input source file, where it stores the object file, how 
           it formats and where it outputs the listing.
           
           All Assembler controls are prefaced with a dollar sign, ($).  No 
           spaces or tabs are allowed between the dollar sign and the body 
           of the control.  Also, only one control per line is permitted.  
           Comments are allowed on the same line as an Assembler control.
           
           There are two types of controls, Primary controls and General 
           controls.  Primary controls can be invoked only  once per 
           assembly.  If an attempt is made to change a previously invoked 
           primary control, the attempt is ignored.  For example, if 
           $NOPRINT is put on line 1 of the source file and $PRINT is put on 
           line 2, the $PRINT control will be ignored and the listing will 
           not be output.  General controls can be invoked any number of 
           times in a source program.
           
           There are two legal forms for each Assembler control, the full 
           form and the abbreviated form.  The two forms can be used inter-
           changeable in the source program.
           
           Below is a description of each Assembler control.  Assembler 
           controls with common functionality are grouped together.
           
           
           6.2. Assembler Control Descriptions
           
           
           $DATE(date)
              Places the ASCII string enclosed by parenthesis in the date 
              field of the page header.  The ASCII string can be from 0 to 9 
              characters long.
              CONTROL:   $DATE(date)
              ABBREV:    $DA(date)
              TYPE:      Primary
              DEFAULT:   No date in page header
              EXAMPLES:  $DATE(1-JUL-84)
                         $DA(7/22/84)
           
           
      
      
      
      
      
      
                                          6-1


      
      
      
           $DEBUG(file)
           $NODEBUG
              These controls determine whether or not a MetaLink Absolute 
              Object Module format file is created. The MetaLink Absolute 
              Object Module format file is used in conjunction with 
              MetaLink's MetaICE series of in-circuit-emulators.  Among 
              other advantages, it provides powerful symbolic debug 
              capability in the emulator debug environment.  $NODEBUG 
              specifies that a MetaLink Absolute Object Module file will not 
              be created. $DEBUG specifies that a MetaLink Absolute Object 
              Module file will be created.  The $DEBUG control allows any 
              legal file name to be specified as the MetaLink Absolute 
              Object Module filename.  If no filename is specified, a 
              default name is used.  The default name used for the file is 
              the source file name root with a .DBG extension.  If the 
              $DEBUG control is used, both a MetaLink Absolute Object Module 
              file and a standard Intel Hexadecimal format object file can 
              be generated at the same time.  Refer to the $OBJECT control 
              description later in this chapter for information on 
              controlling the Hexadecimal format object file output.
              CONTROL:   $DEBUG(file)
                         $NODEBUG
              ABBREV:    $DB(file)
                         $NODB
              DEFAULT:   $NODEBUG
              TYPE:      Primary
              EXAMPLES:  $DB(A:NEWNAME.ICE)
                         $DEBUG
                         $NOOBJECT
           
           
           $EJECT
              Places a form feed (ASCII 0CH) in the listing output.  The 
              $NOPAGING control will override this control.
              CONTROL:   $EJECT
              ABBREV:    $EJ
              DEFAULT:   No form feeds in listing output
              TYPE:      General
              EXAMPLES:  $EJECT
                         $EJ
           
           
           $INCLUDE(file)
              Inserts a file in source program as part of the input source 
              program.  The file field in this control can be any legal file 
              designator. No extension is assumed, so the whole file name 
              must be specified.  Any number of files can be included in a 
              source program. Includes can be nested up to 8 level deep.  It 
              is important to note that this control inserts files, it does 
              not chain or concatenate files.
              CONTROL:   $INCLUDE(file)
              ABBREV:    $IC(file)
              DEFAULT:   No file included in source program
              TYPE:      General
              EXAMPLES:  $INCLUDE(B:COMMON.EQU
                         $IC(TABLES.ASM)            ;Uses default drive
      
      
                                          6-2


      
           
           
           $LIST
           $NOLIST
              These controls determine whether or not the source program 
              listing is output or not. $LIST will allow the source program 
              listing to be output.  $NOLIST stops the source program 
              listing from being output.  The $NOPRINT control overrides the 
              $LIST control.
              CONTROL:   $LIST
                         $NOLIST
              ABBREV:    $LI
                         $NOLI
              DEFAULT:   $LIST
              TYPE:      General
              EXAMPLES:  $NOLIST                 ;This will cause the included
                         $INCLUDE(COMMON.TBL)    ;file not to be listed
                         $LI                     ;Listing continues
           
           
           $MOD51
           $MOD52
           $MOD44
           $MOD515
           $MOD512
           $MOD517
           $MOD152
           $MOD451
           $MOD452
           $MOD751
           $MOD752
           $MOD154
           $MOD252
           $MOD521
           $MOD552
           $MOD652
           $MOD851
           $NOMOD
              Recognizes predefined special function register symbols in the 
              source program.  This saves the user from having to define all 
              the registers in the source program. Appendix B lists the 
              symbols that are defined by these controls.  $NOMOD disables 
              the recognizing function.  These controls access a files of 
              the same name that are included with the MetaLink 8051 CROSS 
              ASSEMBLER distribution diskette.  When a $MOD control is used 
              in a source program, it is important that the $MOD file be 
              available to the Cross Assembler.  The Cross Assembler first 
              looks for the $MOD file on the default drive, if it isn't 
              found there, the Cross Assembler looks for it on the A: drive.  
              The components supported by each switch are:
                 $MOD51:  8051, 8751, 8031, 80C51, 80C31, 87C51, 9761, 8053
                 $MOD52:  8052, 8032, 8752
                 $MOD44:  8044, 8344, 8744
                 $MOD515: 80515, 80535, 80C515, 80C535
                 $MOD512: 80512, 80532
                 $MOD517: 80C517, 80C537
      
      
                                          6-3


      
      
      
                 $MOD152: 80C152, 83C152, 80C157
                 $MOD451: 80C451. 83C451, 87C451
                 $MOD452: 80C452, 83C452, 87C452
                 $MOD752: 83C752, 87C752
                 $MOD751: 83C751, 87C751
                 $MOD154: 83C514, 80C154, 85C154
                 $MOD252: 80C252, 83C252, 87C252, 80C51FA, 83C51FA, 87C51FA, 
                          83C51FB, 87C51FB
                 $MOD521: 80C521, 80C321, 87C521, 80C541, 87C541
                 $MOD552: 80C552, 83C552, 87C552
                 $MOD652: 80C652, 83C652
                 $MOD851: 80C851, 83C851
              CONTROL:  $MOD51
                        $MOD52
                        $MOD44
                        $MOD152
                        $MOD515
                        $MOD512
                        $MOD451
                        $MOD452
                        $MOD751
                        $MOD752
                        $MOD154
                        $MOD252
                        $MOD521
                        $MOD552
                        $MOD652
                        $MOD517
                        $MOD851
                        $NOMOD
           
              ABBREV:
              DEFAULT:  $NOMOD
              TYPE:     Primary
              EXAMPLES: $MOD51
                        $MOD52
                        $MOD44
                        $MOD515
                        $MOD512
                        $MOD152
                        $MOD451
                        $MOD452
                        $MOD751
                        $MOD752
                        $MOD154
                        $MOD252
                        $MOD521
                        $MOD552
                        $MOD652
                        $MOD517
                        $MOD851
                        $NOMOD
           
           
           $OBJECT(file)
           $NOOBJECT
      
      
                                          6-4


      
      
      
              These controls determine whether or not a standard Intel 
              Hexadecimal format object file is created.  $NOOBJECT 
              specifies that an object file will not be created. $OBJECT 
              specifies that an object file will be created.  If other than 
              the default name is to be used for the object file, the 
              $OBJECT control allows any legal file name to be specified as 
              the object filename.  The default name used for the object 
              file is the source file name root with a .HEX extension. 
              CONTROL:   $OBJECT(file)
                         $NOOBJECT
              ABBREV:    $OJ(file)
                         $NOOJ
              DEFAULT:   $OBJECT(source.HEX)
              TYPE:      Primary
              EXAMPLES:  $OJ(A:NEWNAME.OBJ)
                         $NOOBJECT
           
           
           $PAGING
           $NOPAGING
              These controls specify whether or not the output listing will 
              be broken into pages or will be output as one continuous 
              listing.  When the $NOPAGING control is used, the $EJECT and 
              $PAGELENGTH controls are ignored.  With the $PAGING control, a 
              form feed and header line is inserted into the output listing 
              whenever an $EJECT control is met, or whenever the number of 
              lines output on the current page exceeds the value specified 
              by the $PAGELENGTH control.  The header line contains source 
              file name, title (if $TITLE control was used), date (if $DATE 
              control was used) and page number.
              CONTROL:   $PAGING
                         $NOPAGING
              ABBREV:    $PI
                         $NOPI
              DEFAULT:   $PAGING
              TYPE:      Primary
              EXAMPLES:  $PAGING
                         $NOPI
           
           
           
           $PAGELENGTH(n)
              Sets the maximum number of lines, (n), on a page of the output 
              listing.  If the maximum is exceeded, a form feed and page 
              header is inserted in the output listing.  This control allows 
              the number of lines per page to be set anywhere between 10 and 
              255.  If the number of lines specified is less than 10, 
              pagelength will be set to 10.  If the number of lines 
              specified is greater than 255, pagelength will be set to 255.  
           
              The $NOPAGING control will override this control.
              CONTROL:   $PAGELENGTH(n)
              ABBREV:    $PL(n)
              DEFAULT:   $PAGELENGTH(60)
              TYPE:      Primary
              EXAMPLES:  $PAGELENGTH(48)
      
      
                                          6-5



      
      
      
                         $PL(58)
           
           
           
           $PAGEWIDTH(n)
              Sets the maximum number of characters, (n), on a line of the 
              output listing.  This control allows the number of characters 
              per line to be set anywhere between 72 and 132.  If the number 
              specified is less than 72, the pagewidth is set at 72.  If the 
              number specified is greater than 132, the pagewidth is set at 
              132.  If the pagewidth is specified between 72 and 100 and the 
              line being output exceeds the pagewidth specification, the 
              line is truncated at the specified pagewidth and a carriage 
              return/line feed pair is inserted in the listing.  If the 
              pagewidth is specified to be greater than 100 and the line 
              being output exceed the pagewidth specification, a carriage 
              return/line feed pair is inserted at the specified pagewidth 
              and the line will continue to be listed on the next line 
              beginning at column 80.
              CONTROL:   $PAGEWIDTH(n)
              ABBREV:    $PW(n)
              DEFAULT    $PAGEWIDTH(72)
              TYPE:      Primary
              EXAMPLES:  $PAGEWIDTH(132)
                         $PW(80)
           
           
           
           $PRINT(file)
           $NOPRINT
              These controls determine whether or not a listing file is 
              created.  $NOPRINT  specifies that a listing file will not be 
              created. $PRINT specifies that an listing file will be 
              created.  If other than the default name is to be used for the 
              listing file, the $PRINT control allows any legal file name to 
              be specified as the listing filename.  The default name used 
              for the listing file is the source file name root with a .LST 
              extension. 
           
              CONTROL:   $PRINT(file)
                         $NOPRINT
              ABBREV:    $PR
                         $NOPR
              DEFAULT:   $PRINT(source.LST)
              TYPE:      Primary
              EXAMPLES:  $PRINT(A:CONTROL.OUT)
                         $NOPR
           
           
           $SYMBOLS
           $NOSYMBOLS
              Selects whether or not the symbol table is appended to the 
              listing output.  $SYMBOLS causes the symbol table to be sorted 
              alphabetically by symbol, formatted and output to the listing 
              file.  Along with the symbol name, its value and type are 
              output.  Values are output in hexadecimal.  Types include NUMB 
      
      
                                          6-6


      
      
      
              (number), ADDR (address), REG (register symbol) and ACC 
              (accumulator symbol).  If a symbol was of type ADDR, it 
              segment is also output as either C (code), D (data) or X 
              (external).  Other information listed with the symbols is NOT    
              USED (symbol defined but never referenced), UNDEFINED (symbol    
              referenced but never defined) and REDEFINEABLE (symbol defined    
              using the SET directive).  The type and value listed for a    
              REDEFINABLE symbol is that of its last definition in the    
              source program. $NOSYMBOLS does not output the symbol table.
              CONTROL:   $SYMBOLS
                         $NOSYMBOLS
              ABBREV:    $SB
                         $NOSB
              DEFAULT:   $SYMBOLS
              TYPE:      Primary
              EXAMPLES:  $SB
                         $NOSYMBOLS
           
           
           $TITLE(string)
              Places the ASCII string enclosed by the parenthesis in the 
              title field of the page header.  The ASCII string can be from 
              0 to 64 characters long.  If the string is greater than 64 
              characters or if the width of the page will not support such a 
              long title, the title will be truncated.  If parentheses are 
              part of the string, they must be balanced.
              CONTROL:   $TITLE(string)
              ABBREV:    $TT(string)
              DEFAULT:   No title in page header
              TYPE:      Primary
              EXAMPLES:  $TITLE(SAMPLE PROGRAM V1.2)
                         $TT(METALINK (TM) CROSS ASSEMBLER) 
              
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          6-7








                                       CHAPTER 7
           
           
                         8051 CROSS ASSEMBLER MACRO PROCESSOR
           
           
           7.1. Introduction
           
           Macros are useful for code that is used repetitively throughout 
           the program.  It saves the programmer the time and tedium of 
           having to specify the code every time it is used.  The code is 
           written only once in the macro definition and it can be used 
           anywhere in the source program any number of times by simply 
           using the macro name.
           
           Sometimes there is confusion between macros and subroutines.  
           Subroutines are common routines that are written once by the 
           programmer and then accessed by CALLing them.  Subroutines are 
           usually used for longer and more complex routines where the 
           call/return overhead can be tolerated.  Macros are commonly used 
           for simpler routines or where the speed of in-line code is 
           required.
           
           
           7.2. Macro Definition
           
           Before a macro can be used, it first must be defined.  The macro 
           definition specifies a template that is inserted into the source 
           program whenever the macro name is encountered.  Macro 
           definitions can not be nested, but once a macro is defined, it 
           can be used in other macro definitions.  Macros used this way can 
           be nested up to nine levels deep.
           
           The macro definition has three parts to it: 1) the macro header 
           which specifies the macro name and its parameter list, 2) the 
           macro body which is the part that is actually inserted into the 
           source program, and 3) the macro terminator.
           
           The macro header has the following form:
           
           name    MACRO     <parameter list>
           
           The name field contains a unique symbol that it used to identify 
           the macro.  Whenever that symbol is encountered in the source 
           program, the Cross Assembler will automatically insert the macro 
           body in the source program at that point.  The name must be a 
           unique symbol that follows all the rules of symbol formation as 
           outlined in Chapter 2.  
           
           The MACRO field of the macro header contains the keyword MACRO.  
           This is used to notify the Cross Assembler that this is the 
           beginning of a macro definition.
           
      
      
                                          7-1


            
      
      
           The <parameter list> field of the macro header lists anywhere 
           from zero to 16 parameters that are used in the macro body and 
           are defined at assembly time.  The symbols used in the parameter 
           list are only used by the Cross Assembler during the storing of 
           the macro definition.  As a result, while symbols used in the 
           parameter list must be unique symbols that follow all the the 
           rules of symbol formation as outlined in Chapter 2, they can be 
           reissued in the parameter list of another macro definition 
           without conflict.  Parameter list items are separated from one 
           another by a comma.  The following are examples of macro 
           definition headers:
           
           MULT_BY_16     MACRO                              (no parameters)
           DIRECT_ADD     MACRO        DESTINATION,SOURCE    (two parameters)
           
           The macro body contains the template that will replace the macro 
           name in the source program.  The macro body can contain 
           instructions, directives, conditional assembly statements or 
           controls.  As a matter of fact, the macro body can contain any 
           legal Cross Assembler construct as defined in Chapters 2, 4, 5 
           and 6.
           
           There are two macro definition terminators: ENDM and EXITM.  
           Every macro definition must have an ENDM at the end of its 
           definition to notify the Cross Assembler that the macro 
           definition is complete.  The EXITM terminator is an alternative 
           ending of the macro that is useful with conditional assembly 
           statements.  When a EXITM is encountered in a program, all 
           remaining statements (to the ENDM) are ignored.
           
           The following is an example of a macro definition that multiplies 
           the Accumulator by 16:
           
           MULT_BY_16     MACRO
                     RL   A         ;* 2
                     RL   A         ;* 4
                     RL   A         ;* 8
                     RL   A         ;* 16
                ENDM
           
           The following is an example of a macro that adds two numbers 
           together.  This could be used by the programmer to do direct 
           memory to memory adds of external variables (create a virtual 
           instruction).
           
           
           DIRECT_ADDX    MACRO    DESTINATION,SOURCE      (two parameters)
                     MOV  R0,#SOURCE
                     MOVX A,@R0
                     MOV  R1,A
                     MOV  R0,#DESTINATION
                     MOVX A,@R0
                     ADD  A,R1
                     MOVX @R0,A
           ENDM
           
      
      
                                          7-2


      
      
      
           A final  macro definition example shows the use of the EXITM 
           macro terminator.  If CMOS is non-zero, the MOV and only the MOV 
           instruction will be translated by the Cross Assembler.
           
           IDLE      MACRO
                IF (CMOS)
                     MOV  PCON,#IDL
                   EXITM
                ENDIF
                     JMP  $
           ENDM
           
           
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          7-3



      
      
           7.3. Special Macro Operators
           
           There are four special macro operators that are defined below:
           
                %         when the PERCENT sign prefaces a symbol in the
                          parameter list, the symbol's value is passed to 
                          the macro's body instead of the symbol itself.
           
                !         when the EXCLAMATION POINT precedes a character, 
                          that character is handled as a literal and is 
                          passed to the macro body with the EXCLAMATION 
                          POINT removed.  This is useful when it is 
                          necessary to pass a delimiter to the macro body.  
                          For example, in the following parameter list, the 
                          second parameter passed to the macro body would be 
                          a COMMA ( , ):
                               GENERATE_INST       75,!,,STK_VALUE
           
                &         when the AMPERSAND is used in the macro body, the 
                          symbols on both sides of it are concatenated 
                          together and the AMPERSAND is removed.
           
                ;;        when double SEMI-COLONS are used in a macro 
                          definition, the comment preceded by the double 
                          SEMI_COLONS will not be saved and thus will not 
                          appear in the listing whenever the macro is 
                          invoked.  Using the double SEMI-COLONS lowers the 
                          memory requirement in storing the macro 
                          definitions and should be used whenever possible.
           
           Examples of using the above special macro operators follow in the 
           "Using Macros" section.
           
           
           7.4. Using Macros
           
           This section section discusses several situations that arise 
           using macros and how to handle them.  In general the discussion 
           uses examples to get the point across.  First the macro 
           definition is listed, then the source line program that will 
           invoke the macro and finally how the macro was expanded by the 
           Cross Assembler.
           
           7.4.1. NESTING MACROS
           
           The following shows a macro nested to a depth of three.  
           Remember, definitions cannot be nested.  Macros must be defined 
           before they are used in other macro definitions.
           
           ;MACRO DEFINITIONS
           
           GET_EXT_BYTE     MACRO     EXT_ADDR
                    MOV    R0,#EXT_ADDR
                    MOVX   A,@R0
           ENDM
           
      
      
                                          7-4


            
      
      
           ADD_EXT_BYTES    MACRO     EXT_DEST,EXT_SRC
                    GET_EXT_BYTE     EXT_DEST
                    MOV    R1,A
                    GET_EXT_BYTE     EXT_SRC
                    ADD    A,R1
           ENDM
           
           ADD_DIRECT_BYTES      MACRO     DESTINATION,SOURCE
                IF (SMALL_MODEL)
                     MOV    A,SOURCE
                     ADD    A,DESTINATION
                     MOV    DESTINATION
                ELSE
                     ADD_EXT_BYTES    DESTINATION,SOURCE
                     MOVX   @R0,A
                ENDIF
           ENDM
           
           
           ;USAGE IN PROGRAM
           
           ADD_DIRECT_BYTES         127,128
           
           ;TRANSLATED MACRO
           
           
                                 30 +1 ADD_DIRECT_BYTES         127,128
                                 31 +1      IF (SMALL_MODEL)
                                 32 +1           MOV    A,128
                                 33 +1           ADD    A,127
                                 34 +1           MOV    127
                                 35 +1      ELSE
                                 36 +2          ADD_EXT_BYTES  127,128
                                 37 +3          GET_EXT_BYTE   127
           0100 787F             38 +3          MOV    R0,#127
           0102 E2               39 +3          MOVX   A,@R0
           0103 F9               40 +2          MOV    R1,A
                                 41 +3          GET_EXT_BYTE   128
           0104 7880             42 +3          MOV    R0,#128
           0106 E2               43 +3          MOVX   A,@R0
           0107 29               44 +2          ADD    A,R1
           0108 F2               45 +1          MOVX   @R0,A
                                 46 +1      ENDIF
                                 48    
           
           Two things should be pointed out from the above example.  First, 
           the order of the parameter list is important.  You must maintain 
           the the order of parameters from the macro definition if the 
           Cross Assembler is to translate the macro correctly.
           
           Secondly, in order to pass parameters to nested macros, simply 
           use the same parameter symbol in the parameter list of the 
           definition.  For example, the parameter DESTINATION was passed 
           properly to the nested macros ADD_EXT_BYTES and GET_EXT_BYTE. 
           This occurred because in the macro definition of 
           ADD_DIRECT_BYTES, the parameter DESTINATION was specified in the 
      
      
                                          7-5


      
      
      
           parameter lists of both ADD_EXT_BYTES and GET_EXT_BYTE.
           
           
           7.4.2. LABELS IN MACROS
           
           You have two choices for specifying labels in a macro body.  A 
           label can either be passed to the body as a parameter or it can 
           be generated within the body.  The following example shows both 
           ways.
           
           
           ;MACRO DEFINITION
           
           MULTIPLE_SHIFT      MACRO          LABEL,LABEL_SUFFIX,COUNTER,N
                COUNTER    SET    COUNTER+1    ;INCREMENT SUFFIX  FOR  NEXT 
           USAGE
           
           LABEL:         MOV    R0,#N
           SHIFT&LABEL_SUFFIX:   RL     A
                          DJNZ   R0,SHIFT&LABEL_SUFFIX
           ENDM
           
           
           ;USAGE IN PROGRAM
           
           MULTIPLE_SHIFT   LOOP_SHIFT,%COUNT,COUNT,4
           
           
           ;TRANSLATED MACRO
           
                             15 +1 MULTIPLE_SHIFT   LOOP_SHIFT,%COUNT,COUNT,4
             0006            16 +1      COUNT   SET    COUNT+1    
                             17 +1 
           0100 7804         18 +1 LOOP_SHIFT:  MOV    R0,#4
           0102 23           19 +1 SHIFT5:      RL     A
           0103 D8FD         20 +1              DJNZ    R0,SHIFT5
                             22    
           
           Points to note in the above example: 1) the double semi-colon 
           caused the comment not to be listed in the translated macro; 2) 
           the percent sign caused the value of COUNT (in this case the 
           value 5) to be passed to the macro body instead of the symbol;  
           and 3) the ampersand allowed two symbols to be concatenated to 
           form the label SHIFT5.
           
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          7-6





                                       CHAPTER 8
           
           
                           8051 CROSS ASSEMBLER ERROR CODES
           
           
           8.1. Introduction
           
           When the Cross Assembler encounters an error in the source 
           program, it will emit an error message in the listing file.  If 
           the $NOPRINT control has been invoked, the error message will be 
           output to the screen.  
           
           There are basically two types of errors that are encountered by 
           the Cross Assembler, translation errors and I/O errors.  I/O 
           errors are usually fatal errors.  However, whenever an error is 
           detected, the Cross Assembler makes every effort possible to 
           continue with the assembly.
           
           If it is possible to recover from the error and continue 
           assembling, the Cross Assembler will report the error, use a 
           default condition and continue on its way. However, when a fatal 
           error is encountered, it is impossible for the Cross Assembler to 
           proceed.  In this case, the Cross Assembler reports the error and 
           then aborts the assembly process.  
           
           Fatal I/O error messages are displayed on the screen and are of 
           the form:
           
           FATAL ERROR opening <filename>
           
           where <filename> would be replaced with the file designator 
           initially entered or read from the source program.  The cause of 
           this error is usually obvious, typically a typographical error or 
           the wrong drive specification.
           
           Another fatal I/O error message is:
           
           FATAL ERROR writing to <type> file
           
           where <type> would be replaced with either "listing" or "object".  
           The cause of this error is usually either a write protected disk 
           or a full disk.
           
           Translation error reports contain at least three lines.  The 
           first line is the source line in which the error was detected, 
           the second line is a pointer to the character, symbol, expression 
           or line that caused the error.  The final line is the error 
           message itself.  There may be more than one error message, 
           depending on the number of errors in the source line.  An example 
           of a source line with two errors in it follows:
           
           0100 2323             26    START:  MOV     AB,@35
      
      
                                          8-1


       
      
           ****----------------------------------------^---^
           ****ERROR #20: Illegal operand
           ****ERROR #20: Illegal operand
           
           The errors are pointed out by the up-arrows ( ^ ).  For every up-
           arrow there will be an error message.  Errors are ordered left to 
           right, so the first error message corresponds to the left-most 
           up-arrow and so on.  The error message includes an error number 
           and an description of the error.  The error number can be used as 
           an index to the more detailed error explanations that follow in 
           this chapter.
           
           After the Cross Assembler has completed its translation process, 
           it will print an assembly complete message:
           
           ASSEMBLY COMPLETE, nn ERRORS FOUND
           
           If it was an error free assembly, in place of the "nn" above the 
           word "NO" will be output.  However, if errors were encountered 
           during the assembly process, the "nn" will be replaced with the 
           number of errors that were found (up to a maximum of 50).  In this
           case, an error summary will follow in the listing file with all 
           the errors that were reported during the assembly.  An error 
           summary looks like the following:
           
           ERROR SUMMARY:
           Line #26, ERROR #20: Illegal operand
           Line #26, ERROR #20: Illegal operand
           
           The same error message that occurred after the source line 
           appears again prefaced by the source line number to aid in 
           tracking down the error in the source listing.
           
           
           8.2. Explanation of Error Messages
           
           ERROR #1: Illegal character
              This error occurs when the Cross Assembler encounters a 
              character that is not part of its legal character set.  The 
              Cross Assembler character set can be found in Appendix D.
           
           ERROR #2: Undefined symbol
              This error occurs when the Cross Assembler tries to use a 
              symbol that hasn't been defined.  The two most common reasons 
              for this error are typographical errors and forward 
              references.
           
           ERROR #3: Duplicate symbol
              This error occurs when a previously defined symbol or a 
              reserved symbol is attempted to be defined again.  Refer to 
              Appendix C for the reserved words.  Also inspect the symbol in 
              the symbol table listing.  If the symbol doesn't appear there, 
              you are using a reserved word.  If the symbol does appear, its 
              original definition will be listed.
           
           ERROR #4: Illegal digit for radix
              A digit was encountered that is not part of the legal digits 
      
      
                                          8-2


      
      
      
              for the radix specified.  Chapter 2 lists the legal digits for 
              each radix available.  Often this error occurs because a 
              symbol was started with a number instead of a letter, question 
              mark, or underscore.
           
           ERROR #5: Number too large
              The number specified, or the returned value of the expression, 
              exceeds 16-bit precision.  The largest value allowed is 
              65,535.
           
           ERROR #6: Missing END directive
              The source program must end with one and only one END 
              directive.  The END is placed after all the assembly line 
              statements.
           
           ERROR #7: Illegal opcode/directive after label
              The symbol after a label is not an opcode nor a directive that 
              allows labels.  The only thing permitted on a line after a 
              label is an instruction, the DS, DB or DW directives, or a 
              comment.  If none of these are found, this error will be 
              reported.
           
           ERROR #8: Illegal assembly line
              The assembly line doesn't begin with a symbol, label, 
              instruction mnemonic, control, directive, comment or null 
              line.  No attempt is made to translate such a line.
           
           ERROR #9: Text beyond END directive
              The END directive must be the last line of the source program.  
              Any text beyond the END line will cause this error.  Any such 
              text is ignore.  Text here is defined as any printable ASCII 
              characters.
           
           ERROR #10: Illegal or missing expression
              A number, symbol or arithmetic expression was expected, but it 
              was either found to be missing or the Cross Assembler was 
              unable to evaluate it properly.
           
           ERROR #11: Illegal or missing expression operator
              An arithmetic operator was expected but it is either missing 
              or it is not one of the legal operators specified in Chapter 
              2.
           
           ERROR #12: Unbalanced parentheses
              In evaluating an expression, the parentheses in the expression 
              were found not to balance.
             
           ERROR #13: Illegal or missing expression value
              In evaluating an expression, the Cross Assembler expected to 
              find either a number or a symbol, but it was either missing or 
              illegal.
           
           ERROR #14: Illegal literal expression
              This error occurs when a null ASCII literal string  is found.  
              A null ASCII literal is nothing more than two apostrophes 
              together ( '' ) and is illegal.
      
      
                                          8-3


      
      
      
           ERROR #15: Expression stack overflow
              The expression stack has a depth of 32 values.  The expression 
              being evaluated exceeds this depth.  This is a very rare 
              error.  However, if you ever get it, divide the expression 
              into two or more expressions using the EQU directive.
           
           ERROR #16: Division by zero
              The expression being evaluated includes an attempt to divide 
              by zero.
           
           ERROR #17: Illegal bit designator
              A bit designator address was specified in the source program 
              and it points to an illegal bit address.  A bit designator 
              contains a byte address, followed by a PERIOD, followed by the 
              bit index into the byte address (e.g., ACC.7) as discussed in 
              Chapter 2.  This error can occur for one of two reasons.  
              First, if the number or a symbol that is used to specify the 
              byte address part of the bit designator is not a legal bit 
              addressable address, ERROR #17 will occur.  Second, if the bit 
              index into the byte address exceeds the number 7, again ERROR 
              #17 will be output.
           
           ERROR #18: Target address exceeds relative address range
              A Program Counter relative jump instruction (e.g., SJMP, JZ, 
              JNC, etc.) was decoded with the target address of the jump 
              exceeding the maximum possible forward jump of 127 bytes or 
              the maximum possible backward jump of 128 bytes.
           
           ERROR #20: Illegal operand
              The operand specified is not a legal operand for the 
              instruction.  Review the legal operands allowed for the 
              instruction.
           
           ERROR #21: Illegal indirect register
              R0 and R1 are the only primary legal indirect register.  This 
              error occurs when the indirect addressing mode designator (@) 
              is not followed by either R0, R1 or symbols that were defined 
              to be equivalent to either R0 or R1.  This error can also 
              occur in the MOVC A,@A+DPTR, MOVC A,@A+PC, MOVX A,@DPTR, MOVX  
              @DPTR,A and the JMP @A+DPTR instructions if the operands after 
              the indirect addressing mode designator ( @ ) aren't specified 
              properly. 
           
           ERROR #22: Missing operand delimiter
              A COMMA operand delimiter is missing from the operand fields 
              of the instruction.
           
           ERROR #23: Illegal or missing directive
              This error occurs when the Cross Assembler cannot find a legal 
              directive.  The most common cause of this error is due to 
              leaving the COLON off a label.  As a result, the following 
              opcode mnemonic is attempted to be decoded as a directive.
           
           ERROR #24: Attempting to EQUate a previously SET symbol
              Once a symbol is defined using the SET directive, it cannot be 
      
      
                                          8-4


      
      
      
              later redefined using the EQU directive.  
           
           ERROR #25: Attempting to SET a previously EQUated symbol
              Once a symbol is defined using the EQU directive, it cannot be 
              redefined.  If you want the symbol to be redefineable, use the 
              SET directive.
           
           ERROR #26: Illegal SET/EQU expression
              The expression following the SET or EQU directive is illegal.  
              This typically occurs when an attempt is made to define a 
              symbol to be equivalent to an implicit register other than A, 
              R0, R1, R2, R3, R4, R5, R6 or R7.
           
           ERROR #27: Illegal expression with forward reference
              This error occurs when an expression contains a symbol that 
              hasn't been defined yet.  Move the symbol definition earlier 
              in the source file.
           
           ERROR #28: Address exceeds segment range
              The address specified exceeds 255 and you are in the DSEG, 
              BSEG, or ISEG.
           
           ERROR #29: Expecting an EOL or COMMENT
              The Cross Assembler has completed processing a legal assembly 
              language line and expected the line to be terminated with 
              either a COMMENT or a carriage return/line         feed pair.
           
           ERROR #30: Illegal directive with current active segment
              The specified directive is not legal in the active segment.  
              This can happen by trying to use the DBIT directive in other 
              than the BSEG, or using the DS directive in the BSEG.
           
           ERROR #31: Only two character string allowed
              This error occurs using the DW directive.  The maximum ASCII 
              literal allowed in a DW specification is a two character 
              string.                 
           
           ERROR #32: Byte definition exceeds 255
              This error occurs using the DB directive.  The value specified 
              in the DB specification cannot fit into a byte.
           
           ERROR #33: Premature end of string
              An ASCII literal string was not terminated properly with an 
              apostrophe.
           
           ERROR #34: Illegal register bank number
              This error occurs when the number specified with the USING 
              directive exceed 3.  Legal register bank numbers are: 0, 1, 2, 
              3.
           
           ERROR #35: Include file nesting exceeds 8
              The maximum number of nested include files is eight. You will 
              get this error if you exceed this limit.
           
           ERROR #36: Illegal or missing argument
              This error occurs when the syntax of a Cross Assembler control 
      
      
                                          8-5


      
      
      
              requires an argument and it was either incorrectly specified 
              or is missing all together.
           
           ERROR #37: Illegal control statement
              The Cross Assembler does not recognize the specified control.  
              The legal controls are detailed in Chapter 6.
           
           ERROR #38: Unable to open file
              The Cross Assembler is unable to open the file as specified.  
              This is a fatal error which will abort the assembly process.
           
           ERROR #39: Illegal file specification
              The file specification is not a legal file designator.  Refer 
              to your DOS manual for a description of legal file 
              designators.  This is a fatal error which will abort the 
              assembly process.
           
           ERROR #40: Program synchronization error
              This error occurs when the Cross Assembler is generating the 
              object hex file and finds that the code segment location 
              counter is not advancing properly.  There are two cases where 
              this can happen.  First, if the source program uses ORG 
              directives and they are not placed in ascending order. Second, 
              if a generic CALL or JMP is made to a forward reference that 
              is actually defined later in the program to be a backward 
              reference. For example, the following code sequence will cause 
              this error due to the second reason:
           
                          BACK_REF:      NOP
                                         CALL      FORWARD_REF
                          FORWARD_REF    EQU       BACK_REF
           
              During the first pass, the generic CALL will be replaced with 
              a 3-byte LCALL instruction.  During the second pass, the 
              generic CALL will be replaced with a 2-byte ACALL instruction.  
              To prevent this kind of problem, use the generic CALLs and 
              JMPs with labeled targets, not EQU or SET defined symbols.
           
           ERROR #41: Insufficient memory
              This error occurs when there isn't enough memory to hold all 
              the symbols that have been generated by the source program.  
              If you have 96 Kbytes or more of RAM this will be a very rare 
              error.  Only a massive source program or numerous large macros 
              could potentially cause this error.  However, if this error 
              does occur, your best bet is to either buy more memory or to 
              break up your program into smaller pieces and share common 
              symbols with a common $INCLUDE file.
           
           ERROR #42: More errors detected, not listed
              The internal error buffer can hold 50 errors.  If more than 50 
              errors occur, only the first 50 will be reported.
           
           ERROR #43: ENDIF without IF
              The terminator of a conditional assembly block (ENDIF) was 
              recognized without seeing a matching IF.
           
      
      
                                          8-6


            
      
      
           ERROR #44: Missing ENDIF
              A conditional assembly block was begun with an IF statement, 
              but no matching ENDIF was detected.
           
           ERROR #45: Illegal or missing macro name
              The MACRO keyword was recognized, but the symbol that is    
              supposed to precede the MACRO keyword was missing, an illegal    
              symbol or a duplicate symbol.
           
           ERROR #46: Macro nesting too deep
              Macros can be nested to a depth of 9 levels.  Exceeding this 
              limit will cause this error.
           
           ERROR #47: Number of parameters doesn't match definition
              In attempting to use a macro, the number of parameters in the 
              parameter list does not equal the number of parameters 
              specified in the macro definition.  They must match.
           
           ERROR #48: Illegal parameter specification
              This error typically occurs when a previously defined symbol 
              is used in the parameter list of the macro definition.
           
           ERROR #49: Too many parameters
              The maximum number of parameters in a macro parameter list is 
              sixteen.  This error occurs when you exceed that limit.
           
           ERROR #50: Line exceeds 255 characters
              The maximum length of a source line is 255 characters.  If a 
              carriage return/line feed pair is not detected in the first 
              256 characters of a line, this error is reported and the line 
              is truncated at 255 characters.
           
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          8-7








                                       APPENDIX A
           
           
                              SAMPLE PROGRAM AND LISTING
           
           
           
           A.1. Source File
           
           
           ;
           ;  8-bit by 8-bit signed multiply--byte signed multiply
           ;
           ;    This routine takes the signed byte in multiplicand and 
           ;    multiplies it by the signed byte in multiplier and places 
           ;    the signed 16-bit product in product_high and product_low.
           ;
           ;    This routine assumes 2s complement representation of signed 
           ;    numbers.  The maximum numbers possible are then -128 and 
           ;    +127.  Multiplying the possible maximum numbers together 
           ;    easily fits into a 16-bit product, so no overflow test is 
           ;    done on the answer.
           ;
           ;    Registers altered by routine: A, B, PSW.
           ;
           ;
           ;  Primary controls
           $MOD51
           $TITLE(BYTE SIGNED MULTIPLY)
           $DATE(JUL-30-84)
           $PAGEWIDTH(132)
           $OBJECT(B:BMULB.OBJ)
           ;
           ;
           ;  Variable declarations
           ;
           sign_flag  BIT     0F0H            ;sign of product
           multiplier DATA    030H            ;8-bit multiplier
           multiplicand       DATA    031H    ;8-bit multiplicand
           product_high       DATA    032H    ;high byte of 16-bit answer
           product_low        DATA    033H    ;low byte of answer
           ;
           ;
           ;
              ORG     100H                    ;arbitrary start
           ;
           byte_signed_multiply:
                      CLR     sign_flag       ;reset sign
                      MOV     A,multiplier    ;put multiplier in accumulator
                      JNB     ACC.7,positive  ;test sign bit of multiplier
                      CPL     A               ;negative--complement and
                      INC     A               ;add 1 to convert to positive
                      SETB    sign_flag       ;and set sign flag
           ;
      
      
                                          A-1


      
      
      
           positive:  MOV     B,multiplicand  ;put multiplicand in B register
                      JNB     B.7,multiply    ;test sign bit of multiplicand
                      XRL     B,#0FFh         ;negative--complement and
                      INC     B               ;add 1 to convert to positive
                      CPL     sign_flag       ;complement sign flag
           ;
           multiply:  MUL     AB              ;do unsigned multiplication
           ;
           sign_test: JNB     sign_flag,byte_signed_exit   ;if positive,done
                      XRL     B,#0FFh         ;else have to complement both
                      CPL     A               ;bytes of the product and inc
                      ADD     A,#1            ;add here because inc doesn't
                      JNC     byte_signed_exit      ;set the carry flag
                      INC     B               ;if add overflowed A, inc the 
                                              ;high byte
           byte_signed_exit:
                      MOV     product_high,B  ;save the answer
                      MOV     product_low,A   
           ;
                      RET                     ;and return
              END
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          A-2


      
      
      
           A.2. Source File Listing
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          A-3


            
      
      
      
           
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          A-4


            
      
      
      
           
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          A-5







                                APPENDIX B
     
                    PRE-DEFINED BYTE AND BIT ADDRESSES
     
     The following tables detail the pre-defined byte and bit addresses 
     for the 8051/8031 microcontrollers supported by the MetaLink family 
     of emulators.  Proliferation parts are delimited from the standard 
     MCS-51 definitions by asterisk ("*") boxes.  
     
     This list covers these microcontrollers:
     
     8044  8031   8032   8051   8052   8053  80C154  80C321
     8344  80C31  80C32  8751   8752   8753  83C154  80C521
     8744                80C51  80C52        85C154  87C521
                         87C51
     
     80C321  80C51FA(80C252)  80C452  80C152JA/JB/JC/JD    80C851
     80C541  83C51FA(83C252)  83C452  83C152JA/JC          83C851
     87C541  87C51FA(87C252)  87C452
     
     80C451  80C652  80C552  83C751  83C752  80512  80515  80C515  80C517
     83C451  83C652  83C552  87C751  87C752  80532  80535  80C535  80C537
     87C451  87C652  87C552
          
     B.1. Pre-defined Byte Addresses
     
       P0        DATA      080H      ;PORT 0
       SP        DATA      081H      ;STACK POINTER
       DPL       DATA      082H      ;DATA POINTER - LOW BYTE
       DPH       DATA      083H      ;DATA POINTER - HIGH BYTE
     
     ************************************************************************
       for the 80C321/80C521                                                
       DPL1      DATA      084H      ;DATA POINTER LOW 1                    
       DPH1      DATA      085H      ;DATA POINTER HIGH 1                   
       DPS       DATA      086H      ;DATA POINTER SELECTION                
     ************************************************************************
     ************************************************************************
       for the 83C152/80C152                                                 
       GMOD      DATA      084H      ;GSC MODE
       TFIFO     DATA      085H      ;GSC TRANSMIT BUFFER
     ************************************************************************
     ************************************************************************
       for the 80C517/80C537                                                
       WDTREL    DATA      086H      ;WATCHDOG TIMER RELOAD REG
     ************************************************************************
     
       PCON      DATA      087H      ;POWER CONTROL
       TCON      DATA      088H      ;TIMER CONTROL
       TMOD      DATA      089H      ;TIMER MODE
       TL0       DATA      08AH      ;TIMER 0 - LOW BYTE
       TL1       DATA      08BH      ;TIMER 1 - LOW BYTE
     

                                    B-1





     ************************************************************************
       for the 83C751/83C752                                                
       RTL       DATA      08BH      ;TIMER 0 - LOW BYTE RELOAD
     ************************************************************************
     
       TH0       DATA      08CH      ;TIMER 0 - HIGH BYTE
       TH1       DATA      08DH      ;TIMER 1 - HIGH BYTE
     
     ************************************************************************
       for the 83C751/83C752                                                
       RTH       DATA      08DH      ;TIMER 0 - HIGH BYTE RELOAD
     ************************************************************************
     ************************************************************************
       for the 83C752                                                       
       PWM       DATA      08EH      ;PULSE WIDTH MODULATION
     ************************************************************************
     
       P1        DATA      090H      ;PORT 1
     
     ************************************************************************
       for the 83C152/80C152                                                 
       P5        DATA      091H      ;PORT 5
       DCON0     DATA      092H      ;DMA CONTROL 0
       DCON1     DATA      093H      ;DMA CONTROL 1
       BAUD      DATA      094H      ;GSC BAUD RATE
       ADR0      DATA      095H      ;GSC MATCH ADDRESS 0
     ************************************************************************
     ************************************************************************
       for the 80C452/83C452                                                
       DCON0     DATA      092H      ;DMA CONTROL 0
       DCON1     DATA      093H      ;DMA CONTROL 1
     ************************************************************************
     ************************************************************************
       for the 80C517/80C537                                                
       DPSEL     DATA      092H      ;DATA POINTER SELECT REGISTER
     ************************************************************************
     
       SCON      DATA      098H      ;SERIAL PORT CONTROL
       SBUF      DATA      099H      ;SERIAL PORT BUFFER
     
     ************************************************************************
       for the 83C751/83C752                                                
       I2CON     DATA      098H      ;I2C CONTROL
       I2DAT     DATA      099H      ;I2C DATA
     ************************************************************************
     ************************************************************************
       for the 80C517/80C537                                                
       IEN2      DATA      09AH      ;INTERRUPT ENABLE REGISTER 2
       S1CON     DATA      09BH      ;SERIAL PORT CONTROL 1
       S1BUF     DATA      09CH      ;SERIAL PORT BUFFER 1
       S1REL     DATA      09DH      ;SERIAL RELOAD REG 1
     ************************************************************************
     
       P2        DATA      0A0H      ;PORT 2
       IE        DATA      0A8H      ;INTERRUPT ENABLE
     


                                    B-2





     ************************************************************************
       for the 80C51FA/83C51FA(83C252/80C252)                 
       SADDR     DATA      0A9H      ;SLAVE INDIVIDUAL ADDRESS              
     ************************************************************************
     ************************************************************************
       for the 80515/80535 and 80C517/80C537
       IP0       DATA      0A9H      ;INTERRUPT PRIORITY REGISTER 0         
     ************************************************************************
     ************************************************************************
       for the 80C321/80C521                                                
       WDS       DATA      0A9H      ;WATCHDOG SELECTION                    
       WDK       DATA      0AAH      ;WATCHDOG KEY                          
     ************************************************************************
     ************************************************************************
       for the 83C152/80C152                                                 
       P6        DATA      0A1H      ;PORT 6
       SARL0     DATA      0A2H      ;DMA SOURCE ADDR. 0 (LOW)
       SARH0     DATA      0A3H      ;DMA SOURCE ADDR. 0 (HIGH)
       IFS       DATA      0A4H      ;GSC INTERFRAME SPACING
       ADR1      DATA      0A5H      ;GSC MATCH ADDRESS 1
     ************************************************************************
     ************************************************************************
       for the 80C452/83C452                                                
       SARL0     DATA      0A2H      ;DMA SOURCE ADDR. 0 (LOW)
       SARH0     DATA      0A3H      ;DMA SOURCE ADDR. 0 (HIGH)
     ************************************************************************
     ************************************************************************
       for the 80C552/83C552                                                
       CML0      DATA      0A9H      ;COMPARE 0 - LOW BYTE
       CML1      DATA      0AAH      ;COMPARE 1 - LOW BYTE
       CML2      DATA      0ABH      ;COMPARE 2 - LOW BYTE
       CTL0      DATA      0ACH      ;CAPTURE 0 - LOW BYTE
       CTL1      DATA      0ADH      ;CAPTURE 1 - LOW BYTE
       CTL2      DATA      0AEH      ;CAPTURE 2 - LOW BYTE
       CTL3      DATA      0AFH      ;CAPTURE 3 - LOW BYTE
     ************************************************************************
     
       P3        DATA      0B0H      ;PORT 3
     
     ************************************************************************
       for the 83C152/80C152                                                 
       SARL1     DATA      0B2H      ;DMA SOURCE ADDR. 1 (LOW)
       SARH1     DATA      0B3H      ;DMA SOURCE ADDR. 1 (HIGH)
       SLOTTM    DATA      0B4H      ;GSC SLOT TIME
       ADR2      DATA      0B5H      ;GSC MATCH ADDRESS 2
     ************************************************************************
     ************************************************************************
       for the 80C452/83C452                                                
       SARL1     DATA      0B2H      ;DMA SOURCE ADDR. 1 (LOW)
       SARH1     DATA      0B3H      ;DMA SOURCE ADDR. 1 (HIGH)
     ************************************************************************
     
       IP        DATA      0B8H      ;INTERRUPT PRIORITY
     
     ************************************************************************
       for the 80C51FA/83C51FA(83C252/80C252)


                                    B-3





       SADEN     DATA      0B9H      ;SLAVE ADDRESS ENABLE                  
     ************************************************************************
     ************************************************************************
       for the 80515/80535 and 80C517/80C537
       IP1       DATA      0B9H      ;INTERRUPT PRIORITY REGISTER 1         
       IRCON     DATA      0C0H      ;INTERRUPT REQUEST CONTROL             
       CCEN      DATA      0C1H      ;COMPARE/CAPTURE ENABLE                
       CCL1      DATA      0C2H      ;COMPARE/CAPTURE REGISTER 1  - LOW BYTE
       CCH1      DATA      0C3H      ;COMPARE/CAPTURE REGISTER 1  - HIGH BYTE
       CCL2      DATA      0C4H      ;COMPARE/CAPTURE REGISTER 2  - LOW BYTE
       CCH2      DATA      0C5H      ;COMPARE/CAPTURE REGISTER 2  - HIGH BYTE
       CCL3      DATA      0C6H      ;COMPARE/CAPTURE REGISTER 3  - LOW BYTE
       CCH3      DATA      0C7H      ;COMPARE/CAPTURE REGISTER 3  - HIGH BYTE
       T2CON     DATA      0C8H      ;TIMER 2 CONTROL                       
       CRCL      DATA      0CAH      ;COMPARE/RELOAD/CAPTURE - LOW BYTE     
       CRCH      DATA      0CBH      ;COMPARE/RELOAD/CAPTURE - HIGH BYTE    
       TL2       DATA      0CCH      ;TIMER 2 - LOW BYTE                    
       TH2       DATA      0CDH      ;TIMER 2 - HIGH BYTE                   
     ************************************************************************
     ************************************************************************
       for the 80C517/80C537                                                
       CC4EN     DATA      0C9H      ;COMPARE/CAPTURE 4 ENABLE
       CCL4      DATA      0CEH      ;COMPARE/CAPTURE REGISTER 4  - LOW BYTE
       CCH4      DATA      0CFH      ;COMPARE/CAPTURE REGISTER 4  - HIGH BYTE
     ************************************************************************
     ************************************************************************
       for the RUPI-44                                                      
       STS       DATA      0C8H      ;SIU STATUS REGISTER                   
       SMD       DATA      0C9H      ;SERIAL MODE                           
       RCB       DATA      0CAH      ;RECEIVE CONTROL BYTE                  
       RBL       DATA      0CBH      ;RECEIVE BUFFER LENGTH                 
       RBS       DATA      0CCH      ;RECEIVE BUFFER START                  
       RFL       DATA      0CDH      ;RECEIVE FIELD LENGTH                  
       STAD      DATA      0CEH      ;STATION ADDRESS                       
       DMA_CNT   DATA      0CFH      ;DMA COUNT                             
     ************************************************************************
     ************************************************************************
       for the 8052/8032, 80C51FA/83C51FA(83C252/80C252), 80C154/83C154
       T2CON     DATA      0C8H      ;TIMER 2 CONTROL                       
     ************************************************************************
     ************************************************************************
       for the 80C51FA/83C51FA(83C252/80C252) 
       T2MOD     DATA      0C9H      ;TIMER 2 MODE CONTROL                  
     ************************************************************************
     ************************************************************************
       for the 8052/8032, 80C51FA/83C51FA(83C252/80C252), 80C154/83C154     
       RCAP2L    DATA      0CAH      ;TIMER 2 CAPTURE REGISTER, LOW BYTE    
       RCAP2H    DATA      0CBH      ;TIMER 2 CAPTURE REGISTER, HIGH BYTE   
       TL2       DATA      0CCH      ;TIMER 2 - LOW BYTE                    
       TH2       DATA      0CDH      ;TIMER 2 - HIGH BYTE                   
     ************************************************************************






                                    B-4




     ************************************************************************
       for the 83C152/80C152                                                 
       P4        DATA      0C0H      ;PORT 4
       DARL0     DATA      0C2H      ;DMA DESTINATION ADDR. 0 (LOW)
       DARH0     DATA      0C3H      ;DMA DESTINATION ADDR. 0 (HIGH)
       BKOFF     DATA      0C4H      ;GSC BACKOFF TIMER
       ADR3      DATA      0C5H      ;GSC MATCH ADDRESS 3
       IEN1      DATA      0C8H      ;INTERRUPT ENABLE REGISTER 1
     ************************************************************************
     ************************************************************************
       for the 80C452/83C452                                                
       P4        DATA      0C0H      ;PORT 4
       DARL0     DATA      0C2H      ;DMA DESTINATION ADDR. 0 (LOW)
       DARH0     DATA      0C3H      ;DMA DESTINATION ADDR. 0 (HIGH)
     ************************************************************************
     ************************************************************************
       for the 80C451/83C451                                                
       P4        DATA      0C0H      ;PORT 4
       P5        DATA      0C8H      ;PORT 5
     ************************************************************************
     ************************************************************************
       for the 80512/80532                                                  
       IRCON     DATA      0C0H      ;INTERRUPT REQUEST CONTROL
     ************************************************************************
     ************************************************************************
       for the 80C552/83C552                                                
       P4        DATA      0C0H      ;PORT 4
       P5        DATA      0C4H      ;PORT 5
       ADCON     DATA      0C5H      ;A/D CONVERTER CONTROL
       ADCH      DATA      0C6H      ;A/D CONVERTER HIGH BYTE
       TM2IR     DATA      0C8H      ;T2 INTERRUPT FLAGS
       CMH0      DATA      0C9H      ;COMPARE 0 - HIGH BYTE
       CMH1      DATA      0CAH      ;COMPARE 1 - HIGH BYTE
       CMH2      DATA      0CBH      ;COMPARE 2 - HIGH BYTE
       CTH0      DATA      0CCH      ;CAPTURE 0 - HIGH BYTE
       CTH1      DATA      0CDH      ;CAPTURE 1 - HIGH BYTE
       CTH2      DATA      0CEH      ;CAPTURE 2 - HIGH BYTE
       CTH3      DATA      0CFH      ;CAPTURE 3 - HIGH BYTE
     ************************************************************************
     
       PSW       DATA      0D0H      ;PROGRAM STATUS WORD
     
     ************************************************************************
       for the RUPI-44                                                      
       NSNR      DATA      0D8H      ;SEND COUNT/RECEIVE COUNT              
       SIUST     DATA      0D9H      ;SIU STATE COUNTER                     
       TCB       DATA      0DAH      ;TRANSMIT CONTROL BYTE                 
       TBL       DATA      0DBH      ;TRANSMIT BUFFER LENGTH                
       TBS       DATA      0DCH      ;TRANSMIT BUFFER START                 
       FIFO0     DATA      0DDH      ;THREE BYTE FIFO                       
       FIFO1     DATA      0DEH                                             
       FIFO2     DATA      0DFH                                             
     ************************************************************************




                                    B-5




     ************************************************************************
       for the 80C51FA/83C51FA(83C252/80C252) 
       CCON      DATA      0D8H      ;CONTROL COUNTER                       
       CMOD      DATA      0D9H      ;COUNTER MODE                          
       CCAPM0    DATA      0DAH      ;COMPARE/CAPTURE MODE FOR PCA MODULE 0 
       CCAPM1    DATA      0DBH      ;COMPARE/CAPTURE MODE FOR PCA MODULE 1 
       CCAPM2    DATA      0DCH      ;COMPARE/CAPTURE MODE FOR PCA MODULE 2 
       CCAPM3    DATA      0DDH      ;COMPARE/CAPTURE MODE FOR PCA MODULE 3 
       CCAPM4    DATA      0DEH      ;COMPARE/CAPTURE MODE FOR PCA MODULE 4 
     ************************************************************************
     ************************************************************************
       for the 80515/80535                                                   
       ADCON     DATA      0D8H      ;A/D CONVERTER CONTROL                 
       ADDAT     DATA      0D9H      ;A/D CONVERTER DATA                    
       DAPR      DATA      0DAH      ;D/A CONVERTER PROGRAM REGISTER        
     ************************************************************************
     ************************************************************************
       for the 83C152/80C152                                                 
       DARL1     DATA      0D2H      ;DMA DESTINATION ADDR. 1 (LOW)
       DARH1     DATA      0D3H      ;DMA DESTINATION ADDR. 1 (HIGH)
       TCDCNT    DATA      0D4H      ;GSC TRANSMIT COLLISION COUNTER
       AMSK0     DATA      0D5H      ;GSC ADDRESS MASK 0
       TSTAT     DATA      0D8H      ;TRANSMIT STATUS (DMA & GSC)
     ************************************************************************
     ************************************************************************
       for the 80C452/83C452                                                
       DARL1     DATA      0D2H      ;DMA DESTINATION ADDR. 1 (LOW)
       DARH1     DATA      0D3H      ;DMA DESTINATION ADDR. 1 (HIGH)
     ************************************************************************
     ************************************************************************
       for the 80C451/83C451                                                
       P6        DATA      0D8H      ;PORT 6
     ************************************************************************
     ************************************************************************
       for the 80512/80532                                                  
       ADCON     DATA      0D8H      ;A/D CONVERTER CONTROL
       ADDAT     DATA      0D9H      ;A/D CONVERTER DATA
       DAPR      DATA      0DAH      ;D/A CONVERTER PROGRAM REGISTER
       P6        DATA      0DBH      ;PORT 6
     ************************************************************************
     ************************************************************************
       for the 83C751/83C752                                                
       I2CFG     DATA      0D8H      ;I2C CONFIGURATION
     ************************************************************************
     ************************************************************************
       for the 80C552/83C552 and 80C652/83C652
       S1CON     DATA      0D8H      ;SERIAL 1 CONTROL
       S1STA     DATA      0D9H      ;SERIAL 1 STATUS
       S1DAT     DATA      0DAH      ;SERIAL 1 DATA
       S1ADR     DATA      0DBH      ;SERIAL 1 SLAVE ADDRESS
     ************************************************************************





                                    B-6




     ************************************************************************
       for the 80C517/80C537                                                
       CML0      DATA      0D2H      ;COMPARE REGISTER 0  - LOW BYTE
       CMH0      DATA      0D3H      ;COMPARE REGISTER 0  - HIGH BYTE
       CML1      DATA      0D4H      ;COMPARE REGISTER 1  - LOW BYTE
       CMH1      DATA      0D5H      ;COMPARE REGISTER 1  - HIGH BYTE
       CML2      DATA      0D6H      ;COMPARE REGISTER 2  - LOW BYTE
       CMH2      DATA      0D7H      ;COMPARE REGISTER 2  - HIGH BYTE
       ADCON0    DATA      0D8H      ;A/D CONVERTER CONTROL 0
       ADDAT     DATA      0D9H      ;A/D CONVERTER DATA
       DAPR      DATA      0DAH      ;D/A CONVERTER PROGRAM REGISTER
       P7        DATA      0DBH      ;PORT 7
       ADCON1    DATA      0DCH      ;A/D CONVERTER CONTROL 1
       P8        DATA      0DDH      ;PORT 8
       CTRELL    DATA      0DEH      ;COM TIMER REL REG - LOW BYTE
       CTRELH    DATA      0DFH      ;COM TIMER REL REG - HIGH BYTE
     ************************************************************************
     
       ACC       DATA      0E0H      ;ACCUMULATOR
     
     ************************************************************************
       for the 83C152/80C152                                                 
       BCRL0     DATA      0E2H      ;DMA BYTE COUNT 0 (LOW)
       BCRH0     DATA      0E3H      ;DMA BYTE COUNT 0 (HIGH)
       PRBS      DATA      0E4H      ;GSC PSEUDO-RANDOM SEQUENCE
       AMSK1     DATA      0E5H      ;GSC ADDRESS MASK 1
       RSTAT     DATA      0E8H      ;RECEIVE STATUS (DMA & GSC)
     ************************************************************************
     ************************************************************************
       for the 80C452/83C452                                                
       BCRL0     DATA      0E2H      ;DMA BYTE COUNT 0 (LOW)
       BCRH0     DATA      0E3H      ;DMA BYTE COUNT 0 (HIGH)
       HSTAT     DATA      0E6H      ;HOST STATUS
       HCON      DATA      0E7H      ;HOST CONTROL
       SLCON     DATA      0E8H      ;SLAVE CONTROL
       SSTAT     DATA      0E9H      ;SLAVE STATUS
       IWPR      DATA      0EAH      ;INPUT WRITE POINTER
       IRPR      DATA      0EBH      ;INPUT READ POINTER
       CBP       DATA      0ECH      ;CHANNEL BOUNDARY POINTER
       FIN       DATA      0EEH      ;FIFO IN
       CIN       DATA      0EFH      ;COMMAND IN
     ************************************************************************
     ************************************************************************
       for the 80515/80535                                                   
       P4        DATA      0E8H      ;PORT 4                                
     ************************************************************************
     ************************************************************************
       for the 80C451/83C451                                                
       CSR       DATA      0E8H      ;CONTROL STATUS
     ************************************************************************
     ************************************************************************
       for the 80512/80532                                                  
       P4        DATA      0E8H      ;PORT 4
     ************************************************************************




                                    B-7




     ************************************************************************
       for the 80C552/83C552                                                
       IEN1      DATA      0E8H      ;INTERRUPT ENABLE REGISTER 1
       TM2CON    DATA      0EAH      ;T2 COUNTER CONTROL
       CTCON     DATA      0EBH      ;CAPTURE CONTROL
       TML2      DATA      0ECH      ;TIMER 2 - LOW BYTE
       TMH2      DATA      0EDH      ;TIMER 2 - HIGH BYTE
       STE       DATA      0EEH      ;SET ENABLE
       RTE       DATA      0EFH      ;RESET/TOGGLE ENABLE
     ************************************************************************
     ************************************************************************
       for the 80C51FA/83C51FA(83C252/80C252)      
       CL        DATA      0E9H      ;CAPTURE BYTE LOW                      
       CCAP0L    DATA      0EAH      ;COMPARE/CAPTURE 0 LOW BYTE            
       CCAP1L    DATA      0EBH      ;COMPARE/CAPTURE 1 LOW BYTE            
       CCAP2L    DATA      0ECH      ;COMPARE/CAPTURE 2 LOW BYTE            
       CCAP3L    DATA      0EDH      ;COMPARE/CAPTURE 3 LOW BYTE            
       CCAP4L    DATA      0EEH      ;COMPARE/CAPTURE 4 LOW BYTE            
     ************************************************************************
     ************************************************************************
       for the 80C517/80C537                                                
       CTCON     DATA      0E1H      ;COM TIMER CONTROL REG
       CML3      DATA      0E2H      ;COMPARE REGISTER 3  - LOW BYTE
       CMH3      DATA      0E3H      ;COMPARE REGISTER 3  - HIGH BYTE
       CML4      DATA      0E4H      ;COMPARE REGISTER 4  - LOW BYTE
       CMH4      DATA      0E5H      ;COMPARE REGISTER 4  - HIGH BYTE
       CML5      DATA      0E6H      ;COMPARE REGISTER 5  - LOW BYTE
       CMH5      DATA      0E7H      ;COMPARE REGISTER 5  - HIGH BYTE
       P4        DATA      0E8H      ;PORT 4
       MD0       DATA      0E9H      ;MUL/DIV REG 0
       MD1       DATA      0EAH      ;MUL/DIV REG 1
       MD2       DATA      0EBH      ;MUL/DIV REG 2
       MD3       DATA      0ECH      ;MUL/DIV REG 3
       MD4       DATA      0EDH      ;MUL/DIV REG 4
       MD5       DATA      0EEH      ;MUL/DIV REG 5
       ARCON     DATA      0EFH      ;ARITHMETIC CONTROL REG
     ************************************************************************
     
       B         DATA      0F0H      ;MULTIPLICATION REGISTER
     
     ************************************************************************
       for the 80C154/83C154                                                 
       IOCON     DATA      0F8H      ;I/O CONTROL REGISTER                   
     ************************************************************************
     ************************************************************************
       for the 83C152/80C152                                                 
       BCRL1     DATA      0F2H      ;DMA BYTE COUNT 1 (LOW)
       BCRH1     DATA      0F3H      ;DMA BYTE COUNT 1 (HIGH)
       RFIFO     DATA      0F4H      ;GSC RECEIVE BUFFER
       MYSLOT    DATA      0F5H      ;GSC SLOT ADDRESS
       IPN1      DATA      0F8H      ;INTERRUPT PRIORITY REGISTER 1
     ************************************************************************





                                    B-8




     ************************************************************************
       for the 83C851/80C851                                                 
       EADRL     DATA      0F2H      ;EEPROM Address Register - Low Byte
       EADRH     DATA      0F3H      ;EEPROM Address Register - High Byte
       EDAT      DATA      0F4H      ;EEPROM Data Register
       ETIM      DATA      0F5H      ;EEPROM Timer Register
       ECNTRL    DATA      0F6H      ;EEPROM Control Register
     ************************************************************************
     ************************************************************************
       for the 80C452/83C452                                                
       BCRL1     DATA      0F2H      ;DMA BYTE COUNT 1 (LOW)
       BCRH1     DATA      0F3H      ;DMA BYTE COUNT 1 (HIGH)
       ITHR      DATA      0F6H      ;INPUT FIFO THRESHOLD
       OTHR      DATA      0F7H      ;OUTPUT FIFO THRESHOLD
       IEP       DATA      0F8H      ;INTERRUPT PRIORITY 
       MODE      DATA      0F9H      ;MODE 
       ORPR      DATA      0FAH      ;OUTPUT READ POINTER
       OWPR      DATA      0FBH      ;OUTPUT WRITE POINTER
       IMIN      DATA      0FCH      ;IMMEDIATE COMMAND IN
       IMOUT     DATA      0FDH      ;IMMEDIATE COMMAND OUT
       FOUT      DATA      0FEH      ;FIFO OUT
       COUT      DATA      0FFH      ;COMMAND OUT
     ************************************************************************
     ************************************************************************
       for the 80515/80535                                                   
       P5        DATA      0F8H      ;PORT 5                                
     ************************************************************************
     ************************************************************************
       for the 80512/80532                                                  
       P5        DATA      0F8H      ;PORT 5
     ************************************************************************
     ************************************************************************
       for the 83C751/83C752                                                
       I2STA     DATA      0F8H      ;I2C STATUS
     ************************************************************************
     ************************************************************************
       for the 80C552/83C552                                                
       IP1       DATA      0F8H      ;INTERRUPT PRIORITY REGISTER 1
       PWM0      DATA      0FCH      ;PULSE WIDTH REGISTER 0
       PWM1      DATA      0FDH      ;PULSE WIDTH REGISTER 1
       PWMP      DATA      0FEH      ;PRESCALER FREQUENCY CONTROL
       T3        DATA      0FFH      ;T3 - WATCHDOG TIMER
     ************************************************************************
     ************************************************************************
       for the 80C517/80C537                                                
       CMEN      DATA      0F6H      ;COMPARE ENABLE
       CML6      DATA      0F2H      ;COMPARE REGISTER 6  - LOW BYTE
       CMH6      DATA      0F3H      ;COMPARE REGISTER 6  - HIGH BYTE
       CML7      DATA      0F4H      ;COMPARE REGISTER 7  - LOW BYTE
       CMH7      DATA      0F5H      ;COMPARE REGISTER 7  - HIGH BYTE
       CMSEL     DATA      0F7H      ;COMPARE INPUT REGISTER 
       P5        DATA      0F8H      ;PORT 5
       P6        DATA      0FAH      ;PORT 6
     ************************************************************************



                                    B-9




     ************************************************************************
       for the 80C51FA/83C51FA(83C252/80C252)      
       CH        DATA      0F9H      ;CAPTURE HIGH BYTE                     
       CCAP0H    DATA      0FAH      ;COMPARE/CAPTURE 0 HIGH BYTE           
       CCAP1H    DATA      0FBH      ;COMPARE/CAPTURE 1 HIGH BYTE           
       CCAP2H    DATA      0FCH      ;COMPARE/CAPTURE 2 HIGH BYTE           
       CCAP3H    DATA      0FDH      ;COMPARE/CAPTURE 3 HIGH BYTE           
       CCAP4H    DATA      0FEH      ;COMPARE/CAPTURE 4 HIGH BYTE           
     ************************************************************************
     ************************************************************************
       for the 83C752                                                       
       PWENA     DATA      0FEH      ;PULSE WIDTH ENABLE
     ************************************************************************
     
     
     
     








































                                    B-10




     B.2. Pre-defined Bit Addresses
     
     ************************************************************************
       for the 83C751/83C752                                                
       SCL       BIT       080H      ;P0.0 - I2C SERIAL CLOCK
       SDA       BIT       081H      ;P0.1 - I2C SERIAL DATA
     ************************************************************************
     
       IT0       BIT       088H      ;TCON.0 - EXT. INTERRUPT 0 TYPE
       IE0       BIT       089H      ;TCON.1 - EXT. INTERRUPT 0 EDGE FLAG
       IT1       BIT       08AH      ;TCON.2 - EXT. INTERRUPT 1 TYPE
       IE1       BIT       08BH      ;TCON.3 - EXT. INTERRUPT 1 EDGE FLAG
       TR0       BIT       08CH      ;TCON.4 - TIMER 0 ON/OFF CONTROL
       TF0       BIT       08DH      ;TCON.5 - TIMER 0 OVERFLOW FLAG
       TR1       BIT       08EH      ;TCON.6 - TIMER 1 ON/OFF CONTROL
       TF1       BIT       08FH      ;TCON.7 - TIMER 1 OVERFLOW FLAG
     
     ************************************************************************
       for the 83C751/83C752                                                
       C/T       BIT       08EH      ;TCON.6 - COUNTER OR TIMER OPERATION
       GATE      BIT       08FH      ;TCON.7 - GATE TIMER 
     ************************************************************************
     ************************************************************************
       for the 80515/80535                                                   
       INT3      BIT       090H      ;P1.0 - EXT. INTERRUPT 3/CAPT & COMP 0 
       INT4      BIT       091H      ;P1.1 - EXT. INTERRUPT 4/CAPT & COMP 1 
       INT5      BIT       092H      ;P1.2 - EXT. INTERRUPT 5/CAPT & COMP 2 
       INT6      BIT       093H      ;P1.3 - EXT. INTERRUPT 6/CAPT & COMP 3 
       INT2      BIT       094H      ;P1.4 - EXT. INTERRUPT 2               
       T2EX      BIT       095H      ;P1.5 - TIMER 2 EXT. RELOAD TRIGGER INP
       CLKOUT    BIT       096H      ;P1.6 - SYSTEM CLOCK OUTPUT            
       T2        BIT       097H      ;P1.7 - TIMER 2 INPUT                  
     ************************************************************************
     ************************************************************************
       for the 83C152/80C152                                                 
       GRXD      BIT       090H      ;P1.0 - GSC RECEIVER DATA INPUT
       GTXD      BIT       091H      ;P1.1 - GSC TRANSMITTER DATA OUTPUT
       DEN       BIT       092H      ;P1.2 - DRIVE ENABLE TO ENABLE EXT DRIVE
       TXC       BIT       093H      ;P1.3 - GSC EXTERNAL TRANSMIT CLOCK INPU
       RXC       BIT       094H      ;P1.4 - GSC EXTERNAL RECEIVER CLOCK INPU
     ************************************************************************
     ************************************************************************
       for the 83C552/80C552                                                
       CT0I      BIT       090H      ;P1.0 - CAPTURE/TIMER INPUT 0
       CT1I      BIT       091H      ;P1.1 - CAPTURE/TIMER INPUT 1
       CT2I      BIT       092H      ;P1.2 - CAPTURE/TIMER INPUT 2
       CT3I      BIT       093H      ;P1.3 - CAPTURE/TIMER INPUT 3
       T2        BIT       094H      ;P1.4 - T2 EVENT INPUT
       RT2       BIT       095H      ;P1.5 - T2 TIMER RESET SIGNAL
       SCL       BIT       096H      ;P1.6 - SERIAL PORT CLOCK LINE I2C
       SDA       BIT       097H      ;P1.7 - SERIAL PORT DATA LINE I2C
     ************************************************************************





                                    B-11




     ************************************************************************
       for the 80C517/80C537                                                
       INT3      BIT       090H      ;P1.0 - EXT. INTERRUPT 3/CAPT & COMP 0
       INT4      BIT       091H      ;P1.1 - EXT. INTERRUPT 4/CAPT & COMP 1
       INT5      BIT       092H      ;P1.2 - EXT. INTERRUPT 5/CAPT & COMP 2
       INT6      BIT       093H      ;P1.3 - EXT. INTERRUPT 6/CAPT & COMP 3
       INT2      BIT       094H      ;P1.4 - EXT. INTERRUPT 2
       T2EX      BIT       095H      ;P1.5 - TIMER 2 EXT. RELOAD TRIGGER INPU
       CLKOUT    BIT       096H      ;P1.6 - SYSTEM CLOCK OUTPUT
       T2        BIT       097H      ;P1.7 - TIMER 2 INPUT
     ************************************************************************
     ************************************************************************
       for the 80C452/83C452 and 80C152/83C152
       HLD       BIT       095H      ;P1.5 - DMA HOLD REQUEST I/O
       HLDA      BIT       096H      ;P1.6 - DMA HOLD ACKNOWLEDGE OUTPUT
     ************************************************************************
     ************************************************************************
       for the 83C751/83C752                                                
       INT0      BIT       095H      ;P1.5 - EXTERNAL INTERRUPT 0 INPUT
       INT1      BIT       096H      ;P1.6 - EXTERNAL INTERRUPT 1 INPUT
       T0        BIT       096H      ;P1.7 - TIMER 0 COUNT INPUT
     ************************************************************************
     
       RI        BIT       098H      ;SCON.0 - RECEIVE INTERRUPT FLAG
       TI        BIT       099H      ;SCON.1 - TRANSMIT INTERRUPT FLAG
       RB8       BIT       09AH      ;SCON.2 - RECEIVE BIT 8
       TB8       BIT       09BH      ;SCON.3 - TRANSMIT BIT 8
       REN       BIT       09CH      ;SCON.4 - RECEIVE ENABLE
       SM2       BIT       09DH      ;SCON.5 - SERIAL MODE CONTROL BIT 2
       SM1       BIT       09EH      ;SCON.6 - SERIAL MODE CONTROL BIT 1
       SM0       BIT       09FH      ;SCON.7 - SERIAL MODE CONTROL BIT 0
     
     ************************************************************************
       for the 83C751/83C752                                                
       MASTER    BIT(READ) 099H      ;I2CON.1 - MASTER
       STP       BIT(READ) 09AH      ;I2CON.2 - STOP
       STR       BIT(READ) 09BH      ;I2CON.3 - START
       ARL       BIT(READ) 09CH      ;I2CON.4 - ARBITRATION LOSS
       DRDY      BIT(READ) 09DH      ;I2CON.5 - DATA READY
       ATN       BIT(READ) 09EH      ;I2CON.6 - ATTENTION
       RDAT      BIT(READ) 09FH      ;I2CON.7 - RECEIVE DATA
       XSTP      BIT(WRITE)098H      ;I2CON.0 - TRANSMIT STOP
       XSTR      BIT(WRITE)099H      ;I2CON.1 - TRANSMIT REPEATED START
       CSTP      BIT(WRITE)09AH      ;I2CON.2 - CLEAR STOP
       CSTR      BIT(WRITE)09BH      ;I2CON.3 - CLEAR START
       CARL      BIT(WRITE)09CH      ;I2CON.4 - CLEAR ARBITRATION LOSS
       CDR       BIT(WRITE)09DH      ;I2CON.5 - CLEAR DATA READY
       IDLE      BIT(WRITE)09EH      ;I2CON.6 - GO IDLE
       CXA       BIT(WRITE)09FH      ;I2CON.7 - CLEAR TRANSMIT ACTIVE
     ************************************************************************
     
       EX0       BIT       0A8H      ;IE.0 - EXTERNAL INTERRUPT 0 ENABLE
       ET0       BIT       0A9H      ;IE.1 - TIMER 0 INTERRUPT ENABLE
       EX1       BIT       0AAH      ;IE.2 - EXTERNAL INTERRUPT 1 ENABLE
       ET1       BIT       0ABH      ;IE.3 - TIMER 1 INTERRUPT ENABLE
       ES        BIT       0ACH      ;IE.4 - SERIAL PORT INTERRUPT ENABLE    


                                    B-12




     ************************************************************************
       for the 83C751/83C752                                                
       EI2       BIT       0ACH      ;IE.4 - SERIAL PORT INTERRUPT ENABLE
     ************************************************************************
     ************************************************************************
       for the 8052/8032, 80C154/83C154, 80C252(80C51FA), 80515/80535       
       ET2       BIT       0ADH      ;TIMER 2 INTERRUPT ENABLE              
     ************************************************************************
     ************************************************************************
       for the 80C652/83C652                                                
       ES1       BIT       0ADH      ;IE.5 - SERIAL PORT 1 INTERRUPT ENABLE
     ************************************************************************
     ************************************************************************
       for the 80C252(80C51FA)                                              
       EC        BIT       0AEH      ;IE.6 - ENABLE PCA INTERRUPT
     ************************************************************************
     ************************************************************************
       for the 80515/80535                                                   
       WDT       BIT       0AEH      ;IEN0.6 - WATCHDOG TIMER RESET         
     ************************************************************************
     ************************************************************************
       for the 83C552/80C552                                                
       ES1       BIT       0ADH      ;IEN0.5 - SERIAL PORT 1 INTERRUPT ENABLE
       EAD       BIT       0AEH      ;IEN0.6 - ENABLE A/D INTERRUPT
     ************************************************************************
     ************************************************************************
       for the 80C517/80C537                                                
       ET2       BIT       0ADH      ;IEN0.5 - TIMER 2 INTERRUPT ENABLE
       WDT       BIT       0AEH      ;IEN0.6 - WATCHDOG TIMER RESET
     ************************************************************************
     
       EA        BIT       0AFH      ;IE.7 - GLOBAL INTERRUPT ENABLE         
       RXD       BIT       0B0H      ;P3.0 - SERIAL PORT RECEIVE INPUT       
       TXD       BIT       0B1H      ;P3.1 - SERIAL PORT TRANSMIT OUTPUT     
       INT0      BIT       0B2H      ;P3.2 - EXTERNAL INTERRUPT 0 INPUT      
       INT1      BIT       0B3H      ;P3.3 - EXTERNAL INTERRUPT 1 INPUT      
       T0        BIT       0B4H      ;P3.4 - TIMER 0 COUNT INPUT             
       T1        BIT       0B5H      ;P3.5 - TIMER 1 COUNT INPUT             
       WR        BIT       0B6H      ;P3.6 - WRITE CONTROL FOR EXT. MEMORY   
       RD        BIT       0B7H      ;P3.7 - READ CONTROL FOR EXT. MEMORY    
       PX0       BIT       0B8H      ;IP.0 - EXTERNAL INTERRUPT 0 PRIORITY   
       PT0       BIT       0B9H      ;IP.1 - TIMER 0 PRIORITY                
       PX1       BIT       0BAH      ;IP.2 - EXTERNAL INTERRUPT 1 PRIORITY   
       PT1       BIT       0BBH      ;IP.3 - TIMER 1 PRIORITY                
       PS        BIT       0BCH      ;IP.4 - SERIAL PORT PRIORITY            
                                                                             
     ************************************************************************
       for the 80C154/83C154                                                 
       PT2       BIT       0BCH      ;IP.5 - TIMER 2 PRIORITY
       PCT       BIT       0BFH      ;IP.7 - INTERRUPT PRIORITY DISABLE     
     ************************************************************************





                                    B-13




     ************************************************************************
       for the 80C652/83C652                                                
       PS1       BIT       0BDH      ;IP.5 - SERIAL PORT 1 PRIORITY
     ************************************************************************
     ************************************************************************
       for the 80C51FA/83C51FA(83C252/80C252)              
       PT2       BIT       0BDH      ;IP.5 - TIMER 2 PRIORITY               
       PPC       BIT       0BEH      ;IP.6 - PCA PRIORITY                   
     ************************************************************************
     ************************************************************************
       for the 80515/80535 and 80C517/80C537
       EADC      BIT       0B8H      ;IEN1.0 - A/D CONVERTER INTERRUPT EN   
       EX2       BIT       0B9H      ;IEN1.1 - EXT. INTERRUPT 2 ENABLE      
       EX3       BIT       0BAH      ;IEN1.2 - EXT. INT 3/CAPT/COMP INT 0 EN
       EX4       BIT       0BBH      ;IEN1.3 - EXT. INT 4/CAPT/COMP INT 1 EN
       EX5       BIT       0BCH      ;IEN1.4 - EXT. INT 5/CAPT/COMP INT 2 EN
       EX6       BIT       0BDH      ;IEN1.5 - EXT. INT 6/CAPT/COMP INT 3 EN
       SWDT      BIT       0BEH      ;IEN1.6 - WATCHDOG TIMER START         
       EXEN2     BIT       0BFH      ;IEN1.7 - T2 EXT. RELOAD INTER START   
       IADC      BIT       0C0H      ;IRCON.0 - A/D CONVERTER INTER REQUEST 
       IEX2      BIT       0C1H      ;IRCON.1 - EXT. INTERRUPT 2 EDGE FLAG  
       IEX3      BIT       0C2H      ;IRCON.2 - EXT. INTERRUPT 3 EDGE FLAG  
       IEX4      BIT       0C3H      ;IRCON.3 - EXT. INTERRUPT 4 EDGE FLAG  
       IEX5      BIT       0C4H      ;IRCON.4 - EXT. INTERRUPT 5 EDGE FLAG  
       IEX6      BIT       0C5H      ;IRCON.5 - EXT. INTERRUPT 6 EDGE FLAG  
       TF2       BIT       0C6H      ;IRCON.6 - TIMER 2 OVERFLOW FLAG       
       EXF2      BIT       0C7H      ;IRCON.7 - TIMER 2 EXT. RELOAD FLAG    
       T2IO      BIT       0C8H      ;T2CON.0 - TIMER 2 INPUT SELECT BIT 0  
       T2I1      BIT       0C9H      ;T2CON.1 - TIMER 2 INPUT SELECT BIT 1  
       T2CM      BIT       0CAH      ;T2CON.2 - COMPARE MODE                
       T2R0      BIT       0CBH      ;T2CON.3 - TIMER 2 RELOAD MODE SEL BIT 0
       T2R1      BIT       0CCH      ;T2CON.4 - TIMER 2 RELOAD MODE SEL BIT 1
       I2FR      BIT       0CDH      ;T2CON.5 - EXT. INT 2 F/R EDGE FLAG    
       I3FR      BIT       0CEH      ;T2CON.6 - EXT. INT 3 F/R EDGE FLAG    
       T2PS      BIT       0CFH      ;T2CON.7 - PRESCALER SELECT BIT        
     ************************************************************************
     ************************************************************************
       for the 83C552/80C552                                                
       PS1       BIT       0BDH      ;IP0.5 - SIO1
       PAD       BIT       0BEH      ;IP0.6 - A/D CONVERTER
       CMSR0     BIT       0C0H      ;P4.0 - T2 COMPARE AND SET/RESET OUTPUTS
       CMSR1     BIT       0C1H      ;P4.1 - T2 COMPARE AND SET/RESET OUTPUTS
       CMSR2     BIT       0C2H      ;P4.2 - T2 COMPARE AND SET/RESET OUTPUTS
       CMSR3     BIT       0C3H      ;P4.3 - T2 COMPARE AND SET/RESET OUTPUTS
       CMSR4     BIT       0C4H      ;P4.4 - T2 COMPARE AND SET/RESET OUTPUTS
       CMSR5     BIT       0C5H      ;P4.5 - T2 COMPARE AND SET/RESET OUTPUTS
       CMT0      BIT       0C6H      ;P4.6 - T2 COMPARE AND TOGGLE OUTPUTS
       CMT1      BIT       0C7H      ;P4.7 - T2 COMPARE AND TOGGLE OUTPUTS
       CTI0      BIT       0C8H      ;TM2IR.0 - T2 CAPTURE 0
       CTI1      BIT       0C9H      ;TM2IR.1 - T2 CAPTURE 1
       CTI2      BIT       0CAH      ;TM2IR.2 - T2 CAPTURE 2
       CTI3      BIT       0CBH      ;TM2IR.3 - T2 CAPTURE 3
       CMI0      BIT       0CCH      ;TM2IR.4 - T2 COMPARATOR 0
       CMI1      BIT       0CDH      ;TM2IR.5 - T2 COMPARATOR 1
       CMI2      BIT       0CEH      ;TM2IR.6 - T2 COMPARATOR 2
       T2OV      BIT       0CFH      ;TM2IR.7 - T2 OVERFLOW


                                    B-14




     ************************************************************************
     ************************************************************************
       for the RUPI-44                                                      
       RBP       BIT       0C8H      ;STS.0 - RECEIVE BUFFER PROTECT        
       AM        BIT       0C9H      ;STS.1 - AUTO/ADDRESSED MODE SELECT    
       OPB       BIT       0CAH      ;STS.2 - OPTIONAL POLL BIT             
       BOV          BIT       0CBH      ;STS.3 - RECEIVE BUFFER OVERRUN      
       SI        BIT       0CCH      ;STS.4 - SIU INTERRUPT FLAG            
       RTS       BIT       0CDH      ;STS.5 - REQUEST TO SEND               
       RBE       BIT       0CEH      ;STS.6 - RECEIVE BUFFER EMPTY          
       TBF       BIT       0CFH      ;STS.7 - TRANSMIT BUFFER FULL          
     ************************************************************************
     ************************************************************************
       for the 8052/8032, 80C154/83C154, 80C51FA/83C51FA(83C252/80C252)     
       CAP2      BIT       0C8H      ;T2CON.0 - CAPTURE OR RELOAD SELECT    
       CNT2      BIT       0C9H      ;T2CON.1 - TIMER OR COUNTER SELECT     
       TR2       BIT       0CAH      ;T2CON.2 - TIMER 2 ON/OFF CONTROL      
       EXEN2     BIT       0CBH      ;T2CON.3 - TIMER 2 EXTERNAL ENABLE FLAG
       TCLK      BIT       0CCH      ;T2CON.4 - TRANSMIT CLOCK SELECT       
       RCLK      BIT       0CDH      ;T2CON.5 - RECEIVE CLOCK SELECT        
       EXF2      BIT       0CEH      ;T2CON.6 - EXTERNAL TRANSITION FLAG    
       TF2       BIT       0CFH      ;T2CON.7 - TIMER 2 OVERFLOW FLAG       
     ************************************************************************
     ************************************************************************
       for the 83C152/80C152                                                 
       EGSRV     BIT       0C8H      ;IEN1.0 - GSC RECEIVE VALID
       EGSRE     BIT       0C9H      ;IEN1.1 - GSC RECEIVE ERROR
       EDMA0     BIT       0CAH      ;IEN1.2 - DMA CHANNEL REQUEST 0
       EGSTV     BIT       0CBH      ;IEN1.3 - GSC TRANSMIT VALID
       EDMA1     BIT       0CCH      ;IEN1.4 - DMA CHANNEL REQUEST 1
       EGSTE     BIT       0CDH      ;IEN1.5 - GSC TRANSMIT ERROR
     ************************************************************************
     ************************************************************************
       for the 80512/80532                                                  
       IADC      BIT       0C0H      ;IRCON.0 - A/D CONVERTER INTERRUPT REQ
     ************************************************************************
     
       P         BIT       0D0H      ;PSW.0 - ACCUMULATOR PARITY FLAG
     
     ************************************************************************
       for the 83C552/80C552                                                
       F1        BIT       0D1H      ;PSW.1 - FLAG 1
     ************************************************************************
     ************************************************************************
       for the 80512/80532                                                  
       F1        BIT       0D1H      ;PSW.1 - FLAG 1
       MX0       BIT       0D8H      ;ADCON.0 - ANALOG INPUT CH SELECT BIT 0
       MX1       BIT       0D9H      ;ADCON.1 - ANALOG INPUT CH SELECT BIT 1
       MX2       BIT       0DAH      ;ADCON.2 - ANALOG INPUT CH SELECT BIT 2
       ADM       BIT       0DBH      ;ADCON.3 - A/D CONVERSION MODE
       BSY       BIT       0DCH      ;ADCON.4 - BUSY FLAG
       BD        BIT       0DFH      ;ADCON.7 - BAUD RATE ENABLE
     ************************************************************************
     
       OV        BIT       0D2H      ;PSW.2 - OVERFLOW FLAG
       RS0       BIT       0D3H      ;PSW.3 - REGISTER BANK SELECT 0


                                    B-15




       RS1       BIT       0D4H      ;PSW.4 - REGISTER BANK SELECT 1
       F0        BIT       0D5H      ;PSW.5 - FLAG 0
       AC        BIT       0D6H      ;PSW.6 - AUXILIARY CARRY FLAG
       CY        BIT       0D7H      ;PSW.7 - CARRY FLAG
     
     ************************************************************************
       for the 80C51FA/83C51FA(83C252/80C252)                        
       CCF0      BIT       0D8H      ;CCON.0 -PCA MODULE 0 INTERRUPT FLAG   
       CCF1      BIT       0D9H      ;CCON.1 -PCA MODULE 1 INTERRUPT FLAG   
       CCF2      BIT       0DAH      ;CCON.2 -PCA MODULE 2 INTERRUPT FLAG   
       CCF3      BIT       0DBH      ;CCON.3 -PCA MODULE 3 INTERRUPT FLAG   
       CCF4      BIT       0DCH      ;CCON.4 -PCA MODULE 4 INTERRUPT FLAG   
       CR        BIT       0DEH      ;CCON.6 - COUNTER RUN                  
       CF        BIT       0DFH      ;PCA COUNTER OVERFLOW FLAG             
     ************************************************************************
     ************************************************************************
       for the RUPI-44                                                      
       SER       BIT       0D8H      ;NSNR.0 - RECEIVE SEQUENCE ERROR       
       NR0       BIT       0D9H      ;NSNR.1 - RECEIVE SEQUENCE COUNTER-BIT 0
       NR1       BIT       0DAH      ;NSNR.2 - RECEIVE SEQUENCE COUNTER-BIT 1
       NR2       BIT       0DBH      ;NSNR.3 - RECEIVE SEQUENCE COUNTER-BIT 2
       SES       BIT       0DCH      ;NSNR.4 - SEND SEQUENCE ERROR          
       NS0       BIT       0DDH      ;NSNR.5 - SEND SEQUENCE COUNTER-BIT 0  
       NS1       BIT       0DEH      ;NSNR.6 - SEND SEQUENCE COUNTER-BIT 1  
       NS2       BIT       0DFH      ;NSNR.7 - SEND SEQUENCE COUNTER-BIT 2  
     ************************************************************************
     ************************************************************************
       for the 80515/80535                                                   
       MX0       BIT       0D8H      ;ADCON.0 - ANALOG INPUT CH SELECT BIT 0
       MX1       BIT       0D9H      ;ADCON.1 - ANALOG INPUT CH SELECT BIT 1
       MX2       BIT       0DAH      ;ADCON.2 - ANALOG INPUT CH SELECT BIT 2
       ADM       BIT       0DBH      ;ADCON.3 - A/D CONVERSION MODE         
       BSY       BIT       0DCH      ;ADCON.4 - BUSY FLAG                   
       CLK       BIT       0DEH      ;ADCON.5 - SYSTEM CLOCK ENABLE         
       BD        BIT       0DFH      ;ADCON.7 - BAUD RATE ENABLE            
     ************************************************************************
     ************************************************************************
       for the 80C652/83C652                                                
       CR0       BIT       0D8H      ;S1CON.0 - CLOCK RATE 0
       CR1       BIT       0D9H      ;S1CON.1 - CLOCK RATE 1
       AA        BIT       0DAH      ;S1CON.2 - ASSERT ACKNOWLEDGE
       SI        BIT       0DBH      ;S1CON.3 - SIO1 INTERRUPT BIT
       STO       BIT       0DCH      ;S1CON.4 - STOP FLAG
       STA       BIT       0DDH      ;S1CON.5 - START FLAG
       ENS1      BIT       0DEH      ;S1CON.6 - ENABLE SIO1
     ************************************************************************











                                    B-16




     ************************************************************************
       for the 83C152/80C152                                                 
       DMA       BIT       0D8H      ;TSTAT.0 - DMA SELECT
       TEN       BIT       0D9H      ;TSTAT.1 - TRANSMIT ENABLE
       TFNF      BIT       0DAH      ;TSTAT.2 - TRANSMIT FIFO NOT FULL
       TDN       BIT       0DBH      ;TSTAT.3 - TRANSMIT DONE
       TCDT      BIT       0DCH      ;TSTAT.4 - TRANSMIT COLLISION DETECT
       UR        BIT       0DDH      ;TSTAT.5 - UNDERRUN
       NOACK     BIT       0DEH      ;TSTAT.6 - NO ACKNOWLEDGE
       LNI       BIT       0DFH      ;TSTAT.7 - LINE IDLE
       HBAEN     BIT       0E8H      ;RSTAT.0 - HARDWARE BASED ACKNOWLEDGE EN
       GREN      BIT       0E9H      ;RSTAT.1 - RECEIVER ENABLE
       RFNE      BIT       0EAH      ;RSTAT.2 - RECEIVER FIFO NOT EMPTY
       RDN       BIT       0EBH      ;RSTAT.3 - RECEIVER DONE
       CRCE      BIT       0ECH      ;RSTAT.4 - CRC ERROR
       AE        BIT       0EDH      ;RSTAT.5 - ALIGNMENT ERROR
       RCABT     BIT       0EEH      ;RSTAT.6 - RCVR COLLISION/ABORT DETECT
       OR        BIT       0EFH      ;RSTAT.7 - OVERRUN
       PGSRV     BIT       0F8H      ;IPN1.0 - GSC RECEIVE VALID
       PGSRE     BIT       0F9H      ;IPN1.1 - GSC RECEIVE ERROR
       PDMA0     BIT       0FAH      ;IPN1.2 - DMA CHANNEL REQUEST 0
       PGSTV     BIT       0FBH      ;IPN1.3 - GSC TRANSMIT VALID
       PDMA1     BIT       0FCH      ;IPN1.4 - DMA CHANNEL REQUEST 1
       PGSTE     BIT       0FDH      ;IPN1.5 - GSC TRANSMIT ERROR
     ************************************************************************
     ************************************************************************
       for the 80C452/83C452                                                
       OFRS      BIT       0E8H      ;SLCON.0 - OUTPUT FIFO CH REQ SERVICE
       IFRS      BIT       0E9H      ;SLCON.1 - INPUT FIFO CH REQ SERVICE
       FRZ       BIT       0EBH      ;SLCON.3 - ENABLE FIFO DMA FREEZE MODE
       ICOI      BIT       0ECH      ;SLCON.4 - GEN INT WHEN IMMEDIATE COMMAN
                                        OUT REGISTER IS AVAILABLE
       ICII      BIT       0EDH      ;SLCON.5 - GEN INT WHEN A COMMAND IS 
                                        WRITTEN TO IMMEDIATE COMMAND IN REG
       OFI       BIT       0EEH      ;SLCON.6 - ENABLE OUTPUT FIFO INTERRUPT
       IFI       BIT       0EFH      ;SLCON.7 - ENABLE INPUT FIFO INTERRUPT
       EFIFO     BIT       0F8H      ;IEP.0 - FIFO SLAVE BUS I/F INT EN
       PDMA1     BIT       0F9H      ;IEP.1 - DMA CHANNEL REQUEST 1
       PDMA0     BIT       0FAH      ;IEP.2 - DMA CHANNEL REQUEST 0
       EDMA1     BIT       0FBH      ;IEP.3 - DMA CHANNEL 1 INTERRUPT ENABLE
       EDMA0     BIT       0FCH      ;IEP.4 - DMA CHANNEL 0 INTERRUPT ENABLE
       PFIFO     BIT       0FDH      ;IEP.5 - FIFO SLAVE BUS I/F INT PRIORITY
     ************************************************************************
     ************************************************************************
       for the 80C451/83C451                                                
       IBF       BIT       0E8H      ;CSR.0 - INPUT BUFFER FULL
       OBF       BIT       0E9H      ;CSR.1 - OUTPUT BUFFER FULL
       IDSM      BIT       0EAH      ;CSR.2 - INPUT DATA STROBE
       OBFC      BIT       0EBH      ;CSR.3 - OUTPUT BUFFER FLAG CLEAR
       MA0       BIT       0ECH      ;CSR.4 - AFLAG MODE SELECT
       MA1       BIT       0EDH      ;CSR.5 - AFLAG MODE SELECT
       MB0       BIT       0EEH      ;CSR.6 - BFLAG MODE SELECT
       MB1       BIT       0EFH      ;CSR.7 - BFLAG MODE SELECT
     ************************************************************************
     ************************************************************************


                                    B-17




       for the 83C751/83C752                                                
       CTO       BIT(READ) 0D8H      ;I2CFG.0 - CLOCK TIMING 0
       CT1       BIT(READ) 0D9H      ;I2CFG.1 - CLOCK TIMING 1
       T1RUN     BIT(READ) 0DCH      ;I2CFG.4 - START/STOP TIMER 1
       MASTRQ    BIT(READ) 0DEH      ;I2CFG.6 - MASTER I2C
       SLAVEN    BIT(READ) 0DFH      ;I2CFG.7 - SLAVE I2C
       CT0       BIT(WRITE)0D8H      ;I2CFG.0 - CLOCK TIMING 0
       CT1       BIT(WRITE)0D9H      ;I2CFG.1 - CLOCK TIMING 1
       TIRUN     BIT(WRITE)0DCH      ;I2CFG.4 - START/STOP TIMER 1
       CLRTI     BIT(WRITE)0DDH      ;I2CFG.5 - CLEAR TIMER 1 INTERRUPT FLAG
       MASTRQ    BIT(WRITE)0DEH      ;I2CFG.6 - MASTER I2C
       SLAVEN    BIT(WRITE)0DFH      ;I2CFG.7 - SLAVE I2C
       RSTP      BIT(READ) 0F8H      ;I2STA.0 - XMIT STOP CONDITION
       RSTR      BIT(READ) 0F9H      ;I2STA.1 - XMIT REPEAT STOP COND.
       MAKSTP    BIT(READ) 0FAH      ;I2STA.2 - STOP CONDITION
       MAKSTR    BIT(READ) 0FBH      ;I2STA.3 - START CONDITION
       XACTV     BIT(READ) 0FCH      ;I2STA.4 - XMIT ACTIVE
       XDATA     BIT(READ) 0FDH      ;I2STA.5 - CONTENT OF XMIT BUFFER
       RIDLE     BIT(READ) 0FEH      ;I2STA.6 - SLAVE IDLE FLAG
     ************************************************************************
     ************************************************************************
       for the 83C552/80C552                                                
       CR0       BIT       0D8H      ;S1CON.0 - CLOCK RATE 0
       CR1       BIT       0D9H      ;S1CON.1 - CLOCK RATE 1
       AA        BIT       0DAH      ;S1CON.2 - ASSERT ACKNOWLEDGE
       SI        BIT       0DBH      ;S1CON.3 - SERIAL I/O INTERRUPT
       STO       BIT       0DCH      ;S1CON.4 - STOP FLAG
       STA       BIT       0DDH      ;S1CON.5 - START FLAG
       ENS1      BIT       0DEH      ;S1CON.6 - ENABLE SERIAL I/O 
       ECT0      BIT       0E8H      ;IEN1.0 - ENABLE T2 CAPTURE 0
       ECT1      BIT       0E9H      ;IEN1.1 - ENABLE T2 CAPTURE 1 
       ECT2      BIT       0EAH      ;IEN1.2 - ENABLE T2 CAPTURE 2
       ECT3      BIT       0EBH      ;IEN1.3 - ENABLE T2 CAPTURE 3
       ECM0      BIT       0ECH      ;IEN1.4 - ENABLE T2 COMPARATOR 0
       ECM1      BIT       0EDH      ;IEN1.5 - ENABLE T2 COMPARATOR 1
       ECM2      BIT       0EEH      ;IEN1.6 - ENABLE T2 COMPARATOR 2
       ET2          BIT       0EFH      ;IEN1.7 - ENABLE T2 OVERFLOW
       PCT0      BIT       0F8H      ;IP1.0 - T2 CAPTURE REGISTER 0
       PCT1      BIT       0F9H      ;IP1.1 - T2 CAPTURE REGISTER 1
       PCT2      BIT       0FAH      ;IP1.2 - T2 CAPTURE REGISTER 2
       PCT3      BIT       0FBH      ;IP1.3 - T2 CAPTURE REGISTER 3
       PCM0      BIT       0FCH      ;IP1.4 - T2 COMPARATOR 0
       PCM1      BIT       0FDH      ;IP1.5 - T2 COMPARATOR 1
       PCM2      BIT       0FEH      ;IP1.6 - T2 COMPARATOR 2
       PT2          BIT       0FFH      ;IP1.7 - T2 OVERFLOW
     ************************************************************************











                                    B-18




     ************************************************************************
       for the 80C517/80C537                                                
       F1        BIT       0D1H      ;PSW.1 - FLAG 1
       MX0       BIT       0D8H      ;ADCON0.0 - ANALOG INPUT CH SELECT BIT 0
       MX1       BIT       0D9H      ;ADCON0.1 - ANALOG INPUT CH SELECT BIT 1
       MX2       BIT       0DAH      ;ADCON0.2 - ANALOG INPUT CH SELECT BIT 2
       ADM       BIT       0DBH      ;ADCON0.3 - A/D CONVERSION MODE
       BSY       BIT       0DCH      ;ADCON0.4 - BUSY FLAG
       CLK       BIT       0DEH      ;ADCON0.5 - SYSTEM CLOCK ENABLE
       BD        BIT       0DFH      ;ADCON0.7 - BAUD RATE ENABLE
     ************************************************************************
     ************************************************************************
       for the 80C154/83C154                                                 
       ALF       BIT       0F8H      ;IOCON.0 - CPU POWER DOWN MODE CONTROL  
       P1F       BIT       0F9H      ;IOCON.1 - PORT 1 HIGH IMPEDANCE        
       P2F       BIT       0FAH      ;IOCON.2 - PORT 2 HIGH IMPEDANCE        
       P3F       BIT       0FBH      ;IOCON.3 - PORT 3 HIGH IMPEDANCE        
       IZC       BIT       0FCH      ;IOCON.4 - 10K TO 100 K OHM SWITCH (P1-3)
       SERR      BIT       0FDH      ;IOCON.5 - SERIAL PORT RCV ERROR FLAG   
       T32       BIT       0FEH      ;IOCON.6 - 32 BIT TIMER SWITCH          
       WDT       BIT       0FFH      ;IOCON.7 - WATCHDOG TIMER CONTROL       
     *************************************************************************



































                                    B-19






                                      APPENDIX C
           
           
                                   RESERVED SYMBOLS
           
           
           
           The following is a list of reserved symbols used by the Cross 
           Assembler.  These symbols cannot be redefined.
           
           
           
           A               AB              ACALL           ADD
           ADDC            AJMP            AND             ANL             
           AR0             AR1             AR2             AR3
           AR4             AR5             AR6             AR7
           BIT             BSEG            C               CALL
           CJNE            CLR             CODE            CPL
           CSEG            DA              DATA            DB
           DBIT            DEC             DIV             DJNZ
           DPTR            DS              DSEG            DW
           END             EQ              EQU             GE
           GT              HIGH            IDATA           INC
           ISEG            JB              JBC             JC
           JMP             JNB             JNC             JNZ
           JZ              LCALL           LE              LJMP
           LOW             LT              MOD             MOV
           MOVC            MOVX            MUL             NE
           NOP             NOT             OR              ORG
           ORL             PC              POP             PUSH
           R0              R1              R2              R3
           R4              R5              R6              R7
           RET             RETI            RL              RLC
           RR              RRC             SET             SETB
           SHL             SHR             SJMP            SUBB
           SWAP            USING           XCH             XCHD
           XDATA           XOR             XRL             XSEG
           
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                          C-1








                                      APPENDIX D
           
           
                             CROSS ASSEMBLER CHARACTER SET
           ---------------------------+----------------+-------------------
                                    |   PRINTABLE   |    ASCII CODE
                CHARACTER NAME      |     FORM      |   HEX  |  DECIMAL
           ---------------------------+----------------+---------+----------
           Horizontal Tab           |               |   09   |     9
           Line Feed                |               |   0A   |    10 
           Carriage Return          |               |   0D   |    13
           Space                    |               |   20   |    32
           Exclamation Point        |       !       |   21   |    33
           Pound Sign               |       #       |   23   |    35
           Dollar Sign              |       $       |   24   |    36
           Percent Sign             |       %       |   25   |    37
           Ampersand                |       &       |   26   |    38
           Apostrophe               |       '       |   27   |    39
           Left Parenthesis         |       (       |   28   |    40
           Right Parenthesis        |       )       |   29   |    41
           Asterisk                 |       *       |   2A   |    42
           Plus sign                |       +       |   2B   |    43
           Comma                    |       ,       |   2C   |    44
           Hyphen                   |       -       |   2D   |    45
           Period                   |       .       |   2E   |    46
           Slash                    |       /       |   2F   |    47
           Number 0                 |       0       |   30   |    48
             "    1                 |       1       |   31   |    49
             "    2                 |       2       |   32   |    50
             "    3                 |       3       |   33   |    51
             "    4                 |       4       |   34   |    52
             "    5                 |       5       |   35   |    53
             "    6                 |       6       |   36   |    54
             "    7                 |       7       |   37   |    55
             "    8                 |       8       |   38   |    56
             "    9                 |       9       |   39   |    57
           Colon                    |       :       |   3A   |    58
           Semi-colon               |       ;       |   3B   |    59
           Left Angle Bracket       |       <       |   3C   |    60
           Equal Sign               |       =       |   3D   |    61
           Right Angle Bracket      |       >       |   3E   |    62
           Question Mark            |       ?       |   3F   |    63
           At Sign                  |       @       |   40   |    64
           Upper Case A             |       A       |   41   |    65
             "    "   B             |       B       |   42   |    66
             "    "   C             |       C       |   43   |    67
             "    "   D             |       D       |   44   |    68
             "    "   E             |       E       |   45   |    69
             "    "   F             |       F       |   46   |    70
             "    "   G             |       G       |   47   |    71
             "    "   H             |       H       |   48   |    72
      
      
      
      
                                          D-1


      
      
      
           ---------------------------+----------------+-------------------
                                    |   PRINTABLE   |    ASCII CODE
                CHARACTER NAME      |     FORM      |   HEX  |  DECIMAL
           ---------------------------+----------------+---------+----------
           Upper Case I             |       I       |   49   |    73
             "    "   J             |       J       |   4A   |    74
             "    "   K             |       K       |   4B   |    75
             "    "   L             |       L       |   4C   |    76
             "    "   M             |       M       |   4D   |    77
             "    "   N             |       N       |   4E   |    78
             "    "   O             |       O       |   4F   |    79
             "    "   P             |       P       |   50   |    80
             "    "   Q             |       Q       |   51   |    81
             "    "   R             |       R       |   52   |    82
             "    "   S             |       S       |   53   |    83
             "    "   T             |       T       |   54   |    84
             "    "   U             |       U       |   55   |    85
             "    "   V             |       V       |   56   |    86
             "    "   W             |       W       |   57   |    87
             "    "   X             |       X       |   58   |    88
             "    "   Y             |       Y       |   59   |    89
             "    "   Z             |       Z       |   5A   |    90
           Underscore               |       _       |   5F   |    95
           Lower Case A             |       a       |   61   |    97
             "    "   B             |       b       |   62   |    98
             "    "   C             |       c       |   63   |    99
             "    "   D             |       d       |   64   |   100
             "    "   E             |       e       |   65   |   101
             "    "   F             |       f       |   66   |   102
             "    "   G             |       g       |   67   |   103
             "    "   H             |       h       |   68   |   104
             "    "   I             |       i       |   69   |   105
             "    "   J             |       j       |   6A   |   106
             "    "   K             |       k       |   6B   |   107
             "    "   L             |       l       |   6C   |   108
             "    "   M             |       m       |   6D   |   109
             "    "   N             |       n       |   6E   |   110
             "    "   O             |       o       |   6F   |   111
             "    "   P             |       p       |   70   |   112
             "    "   Q             |       q       |   71   |   113
             "    "   R             |       r       |   72   |   114
             "    "   S             |       s       |   73   |   115
             "    "   T             |       t       |   74   |   116
             "    "   U             |       u       |   75   |   117
             "    "   V             |       v       |   76   |   118
             "    "   W             |       w       |   77   |   119
             "    "   X             |       x       |   78   |   120
             "    "   Y             |       y       |   79   |   121
             "    "   Z             |       z       |   7A   |   122
           
           
      
      
      
      
      
      
      
                                          D-2





                                          INDEX
            
            A
            ASCII Literals, 2-6
            Assembler
              Comments, 2-6
              Control Description ($), 6-1
              Controls, 2-3
              Directives, 2-3
              Error codes/messages, 8-1
              Labels, 2-2
              Location Counter, 2-7
              Numbers, 2-7
              Operators, 2-7
              Running it, 3-1
              Symbols, 2-1
              Syntax Summary, 2-7
            
            B
            Bit Addressing, 2-6
            
            C
            Character Set, D-1
            Comments, 2-6
            Control Description ($)
              DATE, 6-1
              DEBUG, 6-2
              EJECT, 6-2
              INCLUDE, 6-2
              LIST, 6-3
              MOD152, 6-3
              MOD154, 6-3
              MOD252, 6-3
              MOD44, 6-3
              MOD451, 6-3
              MOD452, 6-3
              MOD51, 6-3
              MOD512, 6-3
              MOD515, 6-3
              MOD517, 6-3
              MOD52, 6-3
              MOD521, 6-3
              MOD552, 6-3
              MOD652, 6-3
              MOD751, 6-3
              MOD752, 6-3
              MOD851, 6-3
              NODEBUG, 6-2
              NOLIST, 6-3
              NOMOD, 6-3
              NOOBJECT, 6-5
              NOPAGING, 6-5
              NOPRINT, 6-6
              NOSYMBOLS, 6-6
              OBJECT, 6-5
      
      
                                              1


      
      
      
              PAGELENGTH, 6-5
              PAGEWIDTH, 6-6
              PAGING, 6-5
              PRINT, 6-6
              SYMBOLS, 6-6
              TITLE, 6-7
            Controls
              Description, 6-1
              Introduction, 2-3, 6-1
            
            D
            Directive
              Assembler, 2-3
              Conditional Assembly, 5-8
              Introduction, 5-1
              Memory Reservation, 5-5
              Miscellaneous, 5-7
              Segment Selection, 5-4
              Storage, 5-5
              Symbol, 5-1
            Directives
              BIT, 5-2
              BSEG, 5-4
              CODE, 5-2
              CSEG, 5-4
              DATA, 5-3
              DB, 5-5
              DBIT, 5-5
              DS, 5-5
              DSEG, 5-4
              DW, 5-6
              ELSE, 5-8
              END, 5-8
              ENDIF, 5-8
              EQU, 5-1
              IDATA, 5-3
              IF, 5-8
              ISEG, 5-4
              ORG, 5-7
              SET, 5-1
              XDATA, 5-3
              XSEG, 5-4
            
            E
            Error Codes
              Explainations, 8-2
              Introduction, 8-1
              Numerical Listing, 8-2
            Executing
              Assembler, 3-1
              Assembler Example, 3-3
            
      
      
      
      
      
      
                                              2


      
      
      
            F
            File
              ASM51 Cross Assembler Diskette, 3-1
              Object, 2-11
              Source Listing, 2-10
              Source Listing Sample, A-4
            
            H
            Hardware
              Requirements, 3-1
            
            I
            Instruction
              BYT, 4-3
              CYC, 4-3
              Dest/Source ADDR Mode, 4-2
              HEX Opcode, 4-3
              Language Form, 4-2
              Mnemonics, 2-4, 4-1
              Notation, 4-1
              Operation, 4-1
              PSW, 4-3
              Set, 4-4
            Introduction
              Controls, 6-1
              Cross Assembler, 2-1
              Directives, 5-1
              Error codes/messages, 8-1
              Macro Processor, 7-1
            
            L
            Labels, 2-2
            Location Counter, 2-7
            
            M
            Macro
              Definition, 7-1
              Special Operators, 7-4
              Using, Labels, 7-6
              Using, Nesting, 7-4
              Using them, 7-4
            Macro Processor
              Introduction, 7-1
            Microcontroller
              Architecture MCS-51, 1-2
              Background MCS-51, 1-1
              Supported, 1-4
            Mnemonics
              MCS-51, 2-4
              Notations, 4-1
              Summary, 4-4
            
      
      
      
      
      
      
                                              3


      
      
      
            N
            Numbers, 2-7
            
            O
            Operators, 2-7
            Overview
              Cross Assembler, 2-1
              Symbols, 2-1
            
            P
            Program Sample, A-1
            
            R
            Reserved Symbols, 2-2
            
            S
            Sample program, A-1
            Symbols
              Directive Definition, 5-1
              Labels, 2-2
              Overview, 2-1
              Reserved, 2-2
              Reserved list, C-1
            Syntax Summary, 2-7
            System
              DOS hints, 3-3
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
                                              4