If you have suggestions for improvements or find any bugs please submit
via fax or mail.

	EMAC Inc.
	POB 2042
	Carbondale IL, 62902
	fax. 618-457-0110



This document supercedes ATBMON.DOC and documents the improvements made to
the monitor in version X2.1a.

The backspace key can now be used to erase a character.

Access to all of the 80535's SFRs is possible now through the addition of
the following: ADCON, ADDAT, CCEN, CCH1, CCH2, CCH3, CCL1, CCL2, CCL3, CRCH,
CRCL, DAPR, IEN1, IP1, IRCON, P2, P4, P5, PCON, SBUF, T2CON, TH0, TH1, TH2,
TL0, TL1, TL2.

The IE and IP SFRs were replaced with IEN0 and IP0 respectively.

DBYTE was modified to allow access to internal RAM addresses 80 to FF.

The HELP command was added which displays an abbreviated command summary.

UPLOAD/DOWNLOAD have been changed so all I/O is through the main serial port.
UPLOAD no longer gives the "LOADING" message and no CTRL-Z or RUBOUT are
output at the end of the hex file.  DOWNLOAD no longer expects or sends
a comment.  Also, it now grabs the checksum on the end record (though 
it doesn't check it).

SEND has been eliminated.

Interrupt vectors for the 80535 have been added and are offset to 8000h.

8003H		Remap address for ext. interrupt 0.
800BH		Timer 0 interrupt.
8013H		External interrupt 1.
801BH		Timer 1 interrupt.
8023H		Serial port interrupt.
802BH		TF2 + EXF2 interrupt
8043H		IADC interrupt.
804BH		IEX2 interrupt.
8053H		IEX3 interrupt.
805BH		IEX4 interrupt.
8063H		IEX5 interrupt.
806BH		IEX6 interrupt.




GETTING STARTED

The following jumper settings are required on Rev 2 boards:
	
  JP2	o o-o a		JP1	1 2 3 4 5 6
	o o-o b			o o-o o o-o
	1 3 5

To start the monitor after power up, you must connect the main serial (CN1)
port to a terminal or terminal emulator with no parity, 8 data and 1 stop
bit and a baud rate of 1200, 2400, 4800 or 9600.  Pressing a space key twice
will set the baud rate to that of the terminal and the logon message will
appear.  In this version, if any other key is pressed or if there is a
non-standard baud rate, the monitor will default to 9600 baud.

Once communication has been established you can now type "HELP" and enter,
to see an abbreviated command list.  Type DOWNLOAD and enter to ready 
the monitor to receive an Intel hex file.  Send the hex file that is on
the distribution disk (the file with the ".HEX" extension) to the Micropac
535 using the text transfer (or file upload) function of your terminal 
emulator.  Once initiated, you will see each line of the hex file as it
is loading into the board.  

When it is done, you will see the "*" prompt.  You may now start the program
by typing "MGO 8000" and enter.

If you want to single-step or set breakpoints, don't execute the
init section of the program since this section changes parameters
used by the monitor.  Instead, start at the section you want to debug.
You may want to install a JMP instruction over the init section until
your program is debugged.