MX-11: A Multitasking Executive for the MC68HC11.

                                     Version 2.0

                                    Kevin J White

                            Copyright 1994 Kevin J White

                                       3/14/94

          Introduction

          MX-11 provides a preemptive multitasking environment for the
          Motorola MC68HC11 that can be used with programs written using
          Dunfield Development Systems' MICRO-C/11 C compiler.

          I created MX-11 to simplify the task of writing software for data
          acquisition and house automation projects.  I wanted to be able
          to write modular software in a high-level language that could
          retrieve data from sensors or switches, operate on the data and
          then feed the data to displays or control other peripherals.
          MX-11 does this by providing a library of C callable functions
          that allow multiple operations to be performed on one processor
          in an event-driven manner.  Actions can be triggered by external
          events or internally by timers or another software task.

          I have used the software mainly on MC68HC11A8's using the BUFFALO
          monitor, it can be configured for other monitors, and other
          variants of the 68HC11 by modifying the equate files.

          Using MX-11

          MX-11 is used by defining one or more tasks in your code and then
          activating them according to your needs.

          A task is created by writing a C function, and then defining it
          as a MX-11 task using the function deftask().  This task can then
          be activated by passing a message from another task or at
          specific time intervals by adding the task to the polling list.

          When a task is running it can communicate with other tasks by
          messages or semaphores.  It can also use sleep() to inhibit the
          task for a specified period.



                                                                   Page - 2



          Tasks have a fixed priority that is set when the task is defined,
          tasks have increasing priority as in the order they are defined.
          Currently it is not possible to modify the priority once the task
          is defined.  Whenever a task is made runnable or a running task
          is blocked, MX-11 will enable the highest priority runnable task.
          A suspended task will be reactivated when the task is unblocked
          by, for example a timer expiring or a semaphore being set.

          Compiling your program with MX-11.

          In order to use the MX-11 functions they must be made available
          to the MICRO-C source linker.  This is done by putting the
          library files in the appropriate directory (usually \mc\lib11),
          modifying the index file so that MICRO-C knows in which file the
          functions are placed and then compiling and assembling the source
          in the normal fashion to produce a hex file for download to the
          target processor.  The header file "MX.H" must be included in
          your program and mxinit() called before you use any of the MX-11
          functions.

          MX-11 takes about 1.5-2.5k of memory space (depending upon which
          functions you link in).  There are some areas where it could be
          shrunk a bit.  For most of the applications I have had so far it
          has not been a critical problem.

          Running your Program.

          The hexfile should be transferred to the target using a terminal
          emulation program and a monitor such as BUFFALO or MON11.  When
          the program is started the mxinit() function will set up the data
          structures for MX-11 and OC1 for its real-time clock.  The MX-11
          function are then available for use.

          Installation.

          MX-11 should be installed on a machine that has the Dunfield
          Systems Micro-C MC68HC11 compiler already in place.  I have used
          it with both version 2.14 and 3.0 although the examples use
          structs which are not provided in version 2.14.

          1:   Decompress the archive using PKUNZIP with the -d option.
               Copy all of the files from the "lib11" directory into your
               LIB11 directory (usually c:\mc\lib11).

          2:   Merge the file "MXINDEX.LIB" into the file "EXTINDEX.LIB"
               which is usually in \MC\LIB11.  (This is so SLINK can find
               the MX functions).  If you are using MON11 rather than the
               BUFFALO monitor you should edit the MXVECT.EQU file.



                                                                   Page - 3



          3:   Edit and compile your Micro-C programs in the normal fashion
               remembering to include the "MX.H" header file.  The MX-11
               code will be linked with your software by the MICRO-C source
               linker.

          The example programs show the basic methods of using MX-11.
          These programs are compiled to run on the hardware descried
          below, they will need recompiling if your hardware configuration
          is different.

          Hardware Configuration

          My designs have all used a MC68HC11A8 with the BUFFALO monitor
          (version 2.5 in ROM or 3.4 in non-volatile RAM).  For the
          development of MX-11 I used a system with 32k of SRAM from $0-
          $7FFF and 32k of non-volatile RAM from $8000-$FFFF (this is a 32k
          RAM in a DALLAS Smartsocket).  I use BUFFALO version 3.4 with the
          registers allocated at $1000.  Programs (Including the example
          programs) start at $1040.

          MX-11 uses output compare 1 for its real-time clock to give the
          main system tick at 20Hz.  It assumes an 8MHz clock.  If the
          clock is different you will need to adjust the divide ratio
          defined by TM1CNT in MXEQU.ASM  (The counter actually runs at
          40Hz and divides by 2 because the maximum time for the counter is
          32 milliseconds).

          The SCI and its interrupt vector is also used by the serial port
          driver.  No other hardware specific resources are used.  Note
          that BUFFALO uses 0C5 and the XIRQ for its trace function.  Be
          careful if you re using BUFFALO 2.5 as it doesn't use the XIRQ
          and if you have OC5 connected to XIRQ as needed for version 3.4
          then the system will crash when MX-11 initializes.

          Interrupt Service Routines

          Version 2.0 of MX-11 adds the capability of writing ISR's in C.

          The interrupt service routine is written as a normal C function
          that is entered as a result of the interrupt.  It is defined as a
          MX-11 task using deftask().  The task is then bound to a
          particular interrupt using defintr().  The task should run to
          completion every time it is called.  Interrupts are disabled when
          it is entered but they may be enabled if desired.  If this is
          done and another interrupt occurs the interrupt nesting count
          will be incremented.  This ensures that all nested interrupts are
          processed before returning to the process level task that was
          originally interrupted.



                                                                   Page - 4



          The ISR is passed the interrupt vector number as a parameter.  It
          is thus possible to have a common interrupt routine for multiple
          interrupt sources.  Be careful about allowing reentrant ISR's.
          If you enable interrupts it is possible for the same interrupt to
          occur again, while the first invocation is still executing.  This
          is not allowed because the two invocations will be executing with
          the same execution context: the second invocation will destroy
          variables from the first.

          It is also not permissible to allow the ISR to block.  Normally
          the ISR should be as short as possible and communicate with
          process level tasks by setting semaphores, sending messages or
          using global variables.

          The addresses of the interrupt vectors are defined in the
          MXVECT.ASM file.  Edit this if your system uses has the interrupt
          vectors at a different location.  The MXINT.ASM interrupt support
          functions need to know the size of each redirected vector and the
          address of the first interrupt vector, again edit MXVECT.ASM as
          needed for your system.

          On an 8MHz cpu it will take about 70 microseconds for the code to
          start executing assuming the processor had interrupts enabled.
          Example 3 measures the interrupt latency.  Much of the kernel is
          interruptable to allow this.



          ROM code

          MX-11 can execute out of ROM.  The only function that would need
          modification is the MXSTKCHK() function that patches the core
          task dispatcher.  The stack check function is mainly for debug
          purposes so this should not be a problem.

          How does MX-11 work?

          The core parts of MX-11 are in the file MXKERNAL.ASM.  The
          central routine is MXSWCH: the task switcher.  Whenever a
          significant event, such as the expiration of a timer, or any of
          the MX-11 function calls are made, they exit through MXSWCH.  It
          then searches through all the tasks that have been defined and
          starts up the highest priority one that is runnable.

          Information about the task is contained in the Task Control Block
          (TCB) that is allocated for every task when it is defined.  The
          address of the TCB is returned by deftask().  It should be saved
          in a C variable as many of the MX-11 functions require that you
          supply the TCB of the target task.



                                                                   Page - 5



          When mxswch is called, the current task has it's context stored
          on the stack as if it had been interrupted.  MX-11 can then use
          an RTI to resume a task.  It also saves the contents of the ?PARM
          and ?TEMP locations that are used by the MICRO-C library.

          The current status of a task is maintained in the "tstat" record
          of the TCB.  A task can be dormant, sleeping, waiting on a
          semaphore etc.  (The various states are defined in MXEQU.ASM).
          Some of the function calls modify the state of a task.  For
          example the sleep() call puts the task into a sleep state and
          also sets up a timer to reawaken the task after a specified
          interval.

          MX-11 sets up OC1 as a real time clock to interrupt every 25
          milliseconds, on alternate ticks the timer functions are
          processed.  The timers use another important data structure, the
          Event Control Block (ECB).  A pool of these structures is created
          in the heap at initialization time and they are used for
          messages, semaphores, event flags and the pollqueue.

          One use of an ECB is for defining the pollqueue:  A task can be
          linked onto one of five pollqueues.  Every task is sent a defined
          message at the interval for that queue.  Currently there are
          queues defined for 1/20 second, second, minute hour and day
          polling.

          Messages and semaphores also use ECB's, they are linked in a
          chain to the destination task or semaphore.  When the message is
          received or the semaphore is signaled the ECB is returned to the
          pool.

          Hints for writing software using MX-11.

          Writing code for use in a multitasking environment requires
          additional care over writing normal code, you must be prepared at
          any moment for a task to be interrupted and be suspended, while
          another task takes over the CPU.  You must ensure that whenever
          this could happen all global data structures are in a coherent
          state; for example if you had a structure that had an X and Y
          coordinate values for writing to the screen, if one task had
          modified X but had not yet modified Y and another task started
          executing and used this intermediate value, it would update a
          screen position that was neither the old position or the new one,
          but a combination of both.

          A typical program design would have each task waiting as an
          infinite loop waiting for an event or message, it would then have
          a switch statement and perform appropriate processing depending
          upon the message.  After completion it would resume waiting for a
          message.



                                                                   Page - 6



          You should use semaphores and messages to communicate between
          tasks, and be aware of the activity of all tasks. If multiple
          tasks need access to a common resource then you should use a
          semaphore to control access and ensure mutual exclusion.
          Cputstr() and Cprintf() use this technique to ensure that one
          task does not interrupt data coming from another task.  You can
          also disable interrupts, but this prevents any other tasks from
          executing and is not recommended except for very short duration
          sequences.

          You should not spin wait on an event.  If you do, then lower
          priority tasks will not be able to execute.  It is permissible
          for main() to do this as there are no lower priority tasks that
          have to execute.  Although since the nulltask() may never execute
          it will not be possible to get the CPU utilization measurement.

          Changes from Version 1.0

          Version 2.0 has the following changes from version 1.0

          1)   Removed the sendmsgd() call.

          2)   Added capability of doing ISRs in C.

          3)   Rationalized the use of timeouts on semaphores and messages.
               There is only one call for each of these functions that now
               includes timeout parameters.  These may be set to NULL if
               timeouts are not required.

          4)   Much of the kernel is now interruptable to improve interrupt
               latency.  (Typically about 70 microseconds)

          5)   Added event flags.  Similar to semaphores but multiple tasks
               may wait on them and be resumed simultaneously.

          6)   Added wait for character with timeout function (Cgetcr())
               and one for sending characters without translation Cputcr().

          7)   The communication routines now have there own predefined
               semaphores, they do not need to come from the pool of ECBs.

          The remainder of the document is a description of the MX-11
          function calls.  Also study the example code to see how to use
          them.

          Please contact me if you find bugs or if there are any features
          that you would find useful.  I would also like to know if you
          successfully use the software.  Good luck.



                                                                   Page - 7



          Kevin J. White.
          337 Pennsylvania Avenue
          Los Gatos
          CA 95030

          Internet address kevin@novell.com



                                                                   Page - 8


                             Summary of MX-11 functions.
                             ---------------------------
          Initialization functions
          ------------------------
          defpoll(taskh,pollq,msg)           add task to poll list.
          deftask(&task, stack_size, name)   initialize task.
          defintr(taskh, vector_number)      bind task to interrupt vector
          mxinit(stack_size,num_tcb,num_mcb) initialize MX-11.

          Timer functions
          ---------------
          gettime()                     get hardware timer.
          getTOD(time)                  get time of day.
          setTOD(time)                  set time of day.
          sleep(timeout)                pause task.

          Message Functions
          -----------------
          chkmsg()                      check if message available.
          flushmsg()                    flush all messages for task.
          getmsg(timeout)               get next message from queue.
          sendmsg(taskh,msg)            send message to task.

          Semaphore functions
          -------------------
          sclose(&sema)                 close semaphore.
          sopen(initial_value)          get handle to semaphore.
          ssignal(&sema)                signal semaphore.
          swait(&sema,timeout)          wait on semaphore with timeout

          Event Flag Functions
          --------------------
          efopen(initial_value)
          efclose(&eflag)
          efwait(&eflag, mask, timeout)
          efset(&eflag, value)
          efclear(&eflag, value)

          Serial port functions
          ---------------------
          Cgetc()                       get character from serial port.
          Cgetcr(timeout)               get raw character with timeout
          Copen(inbufsize,outbufsize)   initialize serial I/O.
          Cprintf(format_string,args..) printf to serial port.
          Cputc(c)                      print character to serial port.
          Cputcr()                      printf raw character.
          Cputstr(string)               print string to serial port.
          Ctestc()                      test for character at serial port.



                                                                   Page - 9


          CGETC

          PROTOTYPE:

          char Cgetc ()

          ARGUMENTS:

          none.

          RETURN VALUE:

          character from serial port.

          DESCRIPTION:

          The "Cgetc" function obtains a character from the serial port.
          Copen must have been called to initialize the serial port.

          If there is already a character in the input buffer, the function
          will return immediately.  If not the task will block waiting for
          one.  Multiple tasks can wait simultaneously, although it will be
          ambiguous which task receives which character.

          EXAMPLE:

          c=Cgetc(); /* Get a character from the serial port */



                                                                  Page - 10


          CGETCR

          PROTOTYPE:

          int Cgetcr (timeout)

          ARGUMENTS:

          timeout value in ticks

          RETURN VALUE:

          0-255          received character from serial port.
          -1             no character received before timeout.
          DESCRIPTION:

          The "Cgetcr" function obtains a character from the serial port.
          No translation of the character is performed.  Copen must have
          been called to initialize the serial port.  If no character is
          received before the timeout is reached, the value -1 is returned.

          If there is already a character in the input buffer, the function
          will return immediately.  If not the task will block waiting for
          one.  Multiple tasks can wait simultaneously, although it will be
          ambiguous which task receives which character.

          EXAMPLE:

          i=Cgetcr(20); /* Wait for up to 1 second to get a character */



                                                                  Page - 11


          CHKMSG

          PROTOTYPE:

          int chkmsg()

          ARGUMENTS:

          None

          RETURN VALUE:

          Zero if none available.
          One if at least one message available.

          DESCRIPTION:

          This function checks for availability of a message without
          blocking the task.

          EXAMPLE:

          if (chkmsg()) printf("Message is %d\n", getmsg());

          else printf("No Message Available\n");



                                                                  Page - 12


          COPEN

          PROTOTYPE:

          Copen(int in_buffer_size, int out_buffer_size)

          ARGUMENTS:

          in_buffer_size      Size of input buffer to allocate (bytes).
          out_buffer_size     Size of output buffer to allocate (bytes).

          RETURN VALUE:

          0 for success
          -1 for failure.

          DESCRIPTION:

          The "Copen" initializes the interrupt driven serial I/O driver.
          It allocates buffer space from the heap for circular input and
          output buffers.  It is assumed that the monitor program will have
          initialized the baud rate, and this is not changed (BUFFALO sets
          it to 9600bps).

          This function must be called before any of the communication
          functions are called.  The driver is interrupt driven and uses
          semaphores to block tasks waiting for data transmission or
          reception.  The serial port routines use semaphores for mutual
          exclusion of multiple tasks using the serial port.  Ensure that
          there are three MCB's available when Copen() s called.

          EXAMPLE:

          Error=Copen(8,80);/* byte input buffer, 80 byte output buffer */



                                                                  Page - 13


          CPRINTF

          PROTOTYPE:

          Cprintf(char *format_string, arg, arg,..)

          ARGUMENTS:

          Same as standard printf()

          RETURN VALUE:

          None

          DESCRIPTION:

          The "Cprintf" function prints to the serial port as in the
          conventional printf.  A semaphore is used to ensure that the
          entire string will be printed as one stream, not being
          interspersed with characters from other tasks.

          If the serial transmit buffer is full or another task has the use
          of the port, then the task will be blocked.

          Cprintf() needs to be passed the number of parameters in the D
          register, to achieve this it must be declared as a register
          function.  This can be done by including mx.h in your program.

          EXAMPLE:

          Cprintf("This is some text to printf and a number %d\n",j);



                                                                  Page - 14


          CPUTC

          PROTOTYPE:

          Cputc (char c)

          ARGUMENTS:

          c              character to print.

          RETURN VALUE:

          none

          DESCRIPTION:

          The "Cputc" function prints one character to the serial port.
          Copen must have been called to initialize the serial port.
          If the transmit buffer has space the character is put into the
          buffer and the function returns.  If the buffer is full, the task
          is set waiting on a semaphore and will be blocked.  If multiple
          tasks attempt to transmit simultaneously, the characters will be
          transmitted in the order of function calls, regardless of the
          priority of the calling task.  If the buffer is full there may be
          multiple tasks waiting on the semaphore.

          EXAMPLE:

          Cputc('A'); /* Output the letter 'A' to the serial port */



                                                                  Page - 15


          CPUTCR

          PROTOTYPE:

          Cputc (char c)

          ARGUMENTS:

          c              character to print.

          RETURN VALUE:

          none

          DESCRIPTION:

          The "Cputc" function prints one character to the serial port
          without translation of carriage returns.  Copen must have been
          called to initialize the serial port.

          If the transmit buffer has space the character is put into the
          buffer and the function returns.  If the buffer is full, the task
          is set waiting on a semaphore and will be blocked.  If multiple
          tasks attempt to transmit simultaneously, the characters will be
          transmitted in the order of function calls, regardless of the
          priority of the calling task.  If the buffer is full there may be
          multiple tasks waiting on the semaphore.

          EXAMPLE:

          Cputcr('A'); /* Output the letter 'A' to the serial port */



                                                                  Page - 16


          CPUTSTR

          PROTOTYPE:

          Cputstr(char *s)

          ARGUMENTS:

          char           pointer to a string

          RETURN VALUE:

          none

          DESCRIPTION:

          The "Cputstr" function prints a string to the serial port.  A
          semaphore is used to ensure that the entire string will be
          printed as one stream, not being interspersed with characters
          from other tasks.

          If the serial transmit buffer is full or another task has the use
          of the port, then the task will be blocked.

          EXAMPLE:

          Cputstr("This is some text to print\n");



                                                                  Page - 17


          CTESTC

          PROTOTYPE:

          int  Ctestc()

          ARGUMENTS:

          None

          RETURN VALUE:

          0-255          Character from serial port.
          -1             No character available.

          DESCRIPTION:

          Ctestc() tests for a character at the serial port.  If none
          available then -1 is returned.  If a character is available its
          value is returned.  This function does not block if no character
          is available.

          EXAMPLE:

          if ((i = ctestc())==-1) printf("No character available\n");



                                                                  Page - 18


          DEFINTR

          PROTOTYPE:

          defintr( char *taskh, int vector_number)

          ARGUMENTS:

          taskh          task handle.
          vector_number  interrupt vector for task. (Defined in MX.H)

          RETURN VALUE:

          none

          DESCRIPTION:

          The "defintr" function binds a task to an interrupt vector.  When
          the interrupt occurs a new C context is set up and the function
          called.  The function should exit in the normal fashion.  The
          interrupted task will then be resumed.  It is not permissible to
          block while in an ISR.  in general ssignal(), efset() or
          sendmsg() should be used to synchronize process level tasks.
          MX.H defines the interrupts that a task can be attached to

          EXAMPLE:

          char task1h;/* Handle for task1 */
          task1()
               {
               ...
               }
          task1h = deftask(&task1, 128, "Task One");

          defintr(task1h, OC2); /* Attach to Output Compare 2 interrupt */



                                                                  Page - 19


          DEFPOLL

          PROTOTYPE:

          defpoll( char *taskh, int pollq, int msg)

          ARGUMENTS:

          taskh          task handle.
          pollq          queue to attach task to.
          msg            integer message to send to task at each wake up.

          RETURN VALUE:

          Zero if error, one if no error.

          DESCRIPTION:

          The "defpoll" function attaches a task to a poll queue to be sent
          a message at regular intervals.  If the task is dormant it is
          awoken with the message available as its argument.  If it is
          awake the message is queued for the task to retrieve it by a
          getmsg() call or the task will be re-awoken when the task becomes
          dormant.  An error will be returned if an MCB cannot be obtained.
          The messages are synchronous with the TimeofDay so for example
          the hour polling will occur at the beginning of the hour.

          The implemented polling queues currently are:

          0    Once per tick (1/20 second)
          1    Once per second
          2    Once per minute
          3    Once per hour
          4    Once per day at midnight.

          EXAMPLE:

          char task1h;/* Handle for task1 */
          task1()
               {
               ...
               }
          task1h = deftask(&task1, 128, "Task One");

          defpoll(task1h, 1, 255); /* Send value of 255 once per second */



                                                                  Page - 20


          DEFTASK

          PROTOTYPE:

          char *deftask( char *function, int stack_size, char *name)

          ARGUMENTS:
          function       address of function to be defined as a task
          stack_size     number of bytes on stack to reserve for task
          name           pointer to name of task

          RETURN VALUE:

          Pointer to Task Control Block for task().

          DESCRIPTION:

          The "deftask" function allocates a Task Control Block for the
          task and initializes it with starting address and stack.  The
          task is set into a dormant state.  Tasks are assigned priority in
          ascending order of their definition so define low priority tasks
          first.  A task is started by sending a message to it or putting
          it on a poll queue.

          The address of the TCB for the task is returned by deftask.  The
          value should be stored in a variable for use as a task handle in
          later MX-11 calls e.g.. to send a message to it.

          EXAMPLE:

          char *task1h; /* Handle for task1 */

          task1()
               {

               }

          task1h = deftask(&task1, 128, "Task One");
          /* Provide for 128 bytes of stack and give it a name */
          sendmsg(task1h,0); /* Start it */



                                                                  Page - 21


          EFCLEAR

          PROTOTYPE:

          efclear(char *eflagh, int value)

          ARGUMENTS:

          eflagh         Pointer to event flag
          value          Bits to clear in the event flag

          RETURN VALUE:

          none

          DESCRIPTION:

          This function clears bits in the event flag.  The existing value
          of the event flag is anded with the complement of the value
          parameter.  This cannot cause any tasks to become active.

          EXAMPLE:

          char *eflagh; /* Handle for eflag */

          efclear (eflagh, 0xFFFF); /* clear all bit of event flag */



                                                                  Page - 22


          EFCLOSE

          PROTOTYPE:

          char *efclose(char *eflagh)

          ARGUMENTS:

          eflagh         pointer to the event flag

          RETURN VALUE:

          none

          DESCRIPTION:

          This function returns an event flag to the kernal.

          EXAMPLE:

          char *eflagh; /* Handle for eflag */

          efclose(eflagh);



                                                                  Page - 23


          EFOPEN

          PROTOTYPE:

          char *efopen(int initial_value)

          ARGUMENTS:

          initial_value  Starting value of the event flag

          RETURN VALUE:

          handle to event flag data structure

          DESCRIPTION:

          This function obtains a handle to an event flag data structure
          for use with the efwait() and efset() and efclear() functions.
          The initial value can be in the range zero to 0xFFFF and each bit
          is typically used to indicate a separate event.  A task can wait
          on a particular event by providing a 16 bit mask that is anded
          with the event flag.

          EXAMPLE:

          char *eflagh; /* Handle for eflag 1 */

          if !(eflagh = efopen(0)) printf("Error opening Event Flag\n");



                                                                  Page - 24


          EFSET

          PROTOTYPE:

          efset(char *eflagh, int value)

          ARGUMENTS:

          eflagh         Pointer to event flag
          value          Bits to set in the event flag

          RETURN VALUE:

          none

          DESCRIPTION:

          This function sets bits in the event flag.  The existing value of
          the event flag is OR'ed with the value parameter.  Any tasks
          waiting on the event flag are then evaluated and if any tasks are
          able to run they are scheduled for execution.  Multiple tasks can
          be activated simultaneously.  The actual task that executed will
          depend on the relative priority.

          EXAMPLE:

          char *eflagh; /* Handle for eflag */

          task1()
          {
          ...
          efwait(eflagh, 0x0001, 0);/*Wait for bit 1 ,no timeout */
          ...
          }

          efset (eflagh, 0xFFFF); /* set all bits of the event flag */



                                                                  Page - 25


          EFWAIT

          PROTOTYPE:

          efset(char *eflagh, int mask, int timeout)

          ARGUMENTS:

          eflagh         Pointer to event flag
          mask           mask value to select which bits to wait for in
                         event flag
          Timeout        Timeout value, if zero waits forever

          RETURN VALUE:

          value of event flag if task didn't timeout
          0 if timeout

          DESCRIPTION:

          This function waits for the event flag to be set.  The mask is
          anded with the current value of the event flag, if the result is
          zero the task is put onto a list waiting for the event flag to be
          set.  If either the event flag is set using efset() or the
          timeout value expires, the task is removed from the waiting list
          and resumed.  The return value is either the event flag value or
          zero if a timeout occurred.

          EXAMPLE:

          char *eflagh; /* Handle for eflag */

          task1()
          {
          ...
          efwait(eflagh, 0x0001, 0);/*Wait for bit 1 ,no timeout */
          ...
          }

          efset (eflagh, 0xFFFF); /* set all bits of the event flag */



                                                                  Page - 26


          FLUSHMSG

          PROTOTYPE:

          flushmsg()

          ARGUMENTS:

          none

          RETURN VALUE:

          none

          DESCRIPTION:

          This function discards all messages pending on the current task's
          message queue.

          EXAMPLE:

          flushmsg();  /* Discard messages */



                                                                  Page - 27


          GETMSG

          PROTOTYPE:

          int getmsg(int timeout)

          ARGUMENTS:

          timeout        maximum time to wait for message (0=wait forever)

          RETURN VALUE:

          Value of message (Task blocked until message available).
          0    Timed out

          DESCRIPTION:

          Retrieve next message of current task's message queue, if none
          available the task is blocked until one is available or a timeout
          occurs.  If a timeout value of zero is defined it will wait
          forever.

          The message can be sent by sendmsg() or defpoll().

          EXAMPLE:
          int message;

          message = getmsg(20);/* Obtain next message, wait one second*/



                                                                  Page - 28


          GETTIME

          PROTOTYPE:

          int gettime()

          ARGUMENTS:

          None

          RETURN VALUE:

          Value of 68HC11 hardware timer.

          DESCRIPTION:

          Get the value of the hardware timer.  With an 8MHz clock this
          timer does two counts per microsecond.  This function is useful
          for timing very short events.  Since the maximum time is less
          than one system tick, the timer will wrap between clock ticks.

          EXAMPLE:
          int i,j;

          i=gettime();
          ...            /* Do function you wish to time */
          j=gettime();
          printf("Function takes %d microseconds\n",(j-i)/2);



                                                                  Page - 29


          GETTOD

          PROTOTYPE:

          int getTOD(char *time)

          ARGUMENTS:

          Pointer to 5 byte array to receive time of day.

          RETURN VALUE:

          Time of day.

          DESCRIPTION:

          MX-11 maintains a time of day clock with a resolution of a
          twentieth of a second.  It operates as a twenty four hour clock
          and rolls over at 23:59:59.  This function copies the time into
          the array given as an argument.  The fifth byte contains the day
          of the week with 0 meaning Sunday.

          The time is incremented every twentieth of a second, and is
          updated before tasks on the pollqueue are called.

          time[0] = 1/20 seconds
          time[1] = seconds
          time[2] = minutes
          time[3] = hours
          time[4] = day of week ( 0=Sunday )

          EXAMPLE:

          char time[4];

          getTOD(time);
          printf("The time is %2d:%02d:%02d\n",time[3], time[2], time[1]);



                                                                  Page - 30


          MXINIT

          PROTOTYPE:

          char *mxinit(int stack_size, int numtcb, int numecb);

          ARGUMENTS:

          stack_size     number of bytes on stack to reserve for main().
          numtcb         number of Task Control Blocks to create.
          numecb         number of Event Control Blocks to create.

          RETURN VALUE:

          Pointer to Task Control Block for main().

          DESCRIPTION:

          The "mxinit" function initializes MX-11.  It must be executed
          from main() before any other MX-11 functions are called.  It
          allocates memory from the heap for the TCBs and ECBs, sets up the
          task main() and nulltask().  Timer OC1 is used to provide a 20 Hz
          real time interrupt.

          Be careful about the amount of stack space that is set aside,
          some library functions require large amounts for local variables.
          e.g.. printf uses a 100 byte buffer.

          MXSTKCHK can assist in avoiding stack overflow problems.

          EXAMPLE:

          char mainh; /* Handle for main */

          mainh = mxinit(256, 8, 32); /* Provide for 8 tasks and 32 ECBs */



                                                                  Page - 31


          MXSTKCHK

          PROTOTYPE:

          mxstkchk()

          ARGUMENTS:

          none

          RETURN VALUE:

          none

          DESCRIPTION:

          This enables stack checking whenever a taskswitch occurs.  This
          adds about 250 microseconds to each task switch.  It patches the
          mxswch function so will only function correctly when loaded into
          RAM.  If ROM use is desired the file mxkernal.asm should be
          modified.

          It should be invoked after mxinit().

          When a task is defined the maximum stack extent is recorded in
          the TCB, also a stack signature is placed at the maximum stack-1.
          At every task switch all tasks are checked to verify whether
          there is sufficient space to support the space needed for an
          interrupt, and whether the stack signature has been corrupted.
          If it has, a message is output via the SCI and execution
          transfers to the debugger routine "monitor" as defined in MX.EQU
          file.

          EXAMPLE:

          char mainh; /* Handle for main */

          mainh = mxinit(256, 8, 32);/* Provide for 8 tasks and 32 ECBs */

          mxstkchk();



                                                                  Page - 32


          SCLOSE

          PROTOTYPE:

          int sclose(char * semaphore_handle)

          ARGUMENTS:

          semaphore_handle    Pointer to semaphore

          RETURN VALUE:

          none

          DESCRIPTION:

          Returns a semaphore to kernel after completion of use.  Recycles
          the data structure for other tasks.

          EXAMPLE:

          char *sema; /* Handle for semaphore */
          ...
          if !(sema = sopen(0)) printf("Error opening Semaphore\n");
          ...
          swait(sema); /* wait for it to be signaled */
          ...
          sclose(sema); /* Not needed any more, recycle it */



                                                                  Page - 33


          SENDMSG

          PROTOTYPE:

          sendmsg (char *taskh, int msg)

          ARGUMENTS:

          taskh          task handle
          msg            integer message to send to task

          RETURN VALUE:

          0 if error.
          1 if no error.

          DESCRIPTION:

          This function puts a message on a task's message queue.  If the
          task is dormant, the task is scheduled to be run with the message
          as its input parameter.  Alternatively the task can obtain the
          message by performing the getmsg() call.

          Although the message is only a 16 bit variable, it can be used as
          a pointer so data of any size can be passed.

          EXAMPLE:

          char *task1h; /* Handle for task1 */
          task1(msg)
          {
               switch (msg)
               {
               ...
               }
          }

          task1h = deftask(&task1, 128, "Task One");

          sendmsg (task1h, 127); /* Send value of 127 to task 1 */



                                                                  Page - 34


          SETTOD

          PROTOTYPE:

          int setTOD(char *time)

          ARGUMENTS:

          Pointer to 5 byte array containing time of day.

          RETURN VALUE:

          None.

          DESCRIPTION:

          MX-11 maintains a time of day clock with a resolution of a
          twentieth of a second.  It operates as a twenty four hour clock
          and rolls over at 23:59:59.  This function copies the time from
          the array given as an argument.  The fifth byte gives day of the
          week.

          EXAMPLE:

          char time[5];

          /* Set time to Monday : 13:20 */

          time[0]=0;
          time[1]=0;
          time[2]=20;
          time[3]=13;
          time[4]=1; /* Monday */

          setTOD(time);



                                                                  Page - 35


          SLEEP

          PROTOTYPE:

          sleep( int timeout)

          ARGUMENTS:

          timeout        Value for timeout in clock ticks (1/20 second)

          RETURN VALUE:

          none

          DESCRIPTION:

          This function causes a pause in the execution of the calling
          task.  Other tasks can still execute.

          EXAMPLE:

          sleep (20);    /* Cause a one second pause */



                                                                  Page - 36


          SOPEN

          PROTOTYPE:

          char *sopen(int initial_value)

          ARGUMENTS:

          initial_value  Starting value of the semaphore

          RETURN VALUE:

          handle to semaphore data structure

          DESCRIPTION:

           This function obtains a handle to a semaphore data structure for
          use with the swait() and ssignal() functions.  The initial value
          can be in the range zero to 32767 and determines how many
          resources can be consumed before the task will be blocked.  If it
          is set to zero the task will be blocked initially.

          EXAMPLE:

          char *sema1; /* Handle for semaphore 1 */

          if !(sema1 = sopen(0)) printf("Error opening Semaphore\n");



                                                                  Page - 37


          SSIGNAL

          PROTOTYPE:

          void ssignal(char *semaphore_handle)

          ARGUMENTS:

          semaphore_handle    Pointer to semaphore

          RETURN VALUE:

          none

          DESCRIPTION:

          Increments the value of a  semaphore if no tasks are waiting on
          the semaphore.  If any tasks are waiting in the semaphore, the
          first one on the list is unblocked and the semaphore is left at
          zero.

          A semaphore can be used to provide mutual exclusion of use of a
          resource.

          EXAMPLE:

          task1()
          {
          swait(sema1);   /* wait for serial I/O to be available */
          printf("We don't want this to be interrupted by another task\n");
          ssignal(sema1); /* Somebody else can use the serial I/O now */
          }



                                                                  Page - 38


          SWAIT

          PROTOTYPE:

          int swait(char *semaphore_handle, timeout)

          ARGUMENTS:

          semaphore_handle    Pointer to semaphore
          timeout             Timeout value in ticks, 0 means wait forever
          RETURN VALUE:

          1    Semaphore signaled
          0    Timeout

          DESCRIPTION:

          MX-11 supports counting semaphores for inter-task
          synchronization.  The "swait" function tests a semaphore
          previously opened with "sopen", if it has a value greater than
          zero, it is decremented and the task continues.  If the value is
          zero, then the task is placed on the end of the list of tasks
          waiting on the semaphore and the task is blocked.  Multiple tasks
          can be waiting on a semaphore and will be unblocked in list order
          as "ssignal" called.  If a timeout occurs swait() will return
          zero.

          A semaphore can be used to provide mutual exclusion of use of a
          resource.

          EXAMPLE:

          task1()
          {
          swait(sema1,0);   /* wait forever serial I/O to be available */
          printf("We don't want this to be interrupted by another task\n");
          ssignal(sema1); /* Somebody else can use the serial I/O now */
          }