2/1/1996
                      SCO UNIX RTL 8019  MDI Driver
         ==================================================


The following files will be used in this installation:

Files          Contents
-----------    -----------------------------------------
Driver.o       RTL 8019 MDI Driver Program
setup          Transfer dos format to unix format setup program
Master         Used by netconfig
System         Used by netconfig
Node           Used by netconfig
Space.c        Used by netconfig
space.h        Used by netconfig
lkcfg          Used by netconfig
AOF/r2e        Used by netconfig



1.  Installation Diskette in DOS format.
    Put RTL SCO UNIX Driver diskette to floppy A: and use doscp
    command to copy RTL SCO UNIX PCI Driver into UNIX's directories.

       # cd /
       # doscp A:setup  /setup
       # chmod +x /setup
       # ./setup


2.     Use netconfig utility

       Avaiable options:

       # netconfig

3.  To add adapters, select "Add New Lan Adapter" from "Hardware".

4.  Add Protocol to select SCO TCP/IP. 
       
5.  Enter the internet Address of this interface         n.n.n.n

6.  Enter the netmask for this interface                 (default 255.255.255.0)

7.  Enter the boardcast address for this interface       default: n.n.n.n

8.  Do you want to relink to kernel now ?               y

9.  Do you want this kernel to boot by default (y/n)    y

10. Do you want the kernel environment rebuilt (y/n)    y

11. Reboot unix

        # shutdown -y -g0