PCM-4823 Utility Disk V1.1              2/27/1998
-----------------------------------------------------------------------------

The PCM-4823 is supplied with a software utility disk. This disk contains the
necessary file for setting up the VGA display and LAN controller.
Directories and files on the disk are as follows:

 ROOT
   ³
   ÃÄÄÄ README.DOC
   ÃÄÄÄ 4823-SYS.BIN
   ÃÄÄÄ 4823-STN.BIN
   ÃÄÄÄ 4823-EL.BIN
   ÃÄÄÄ 4823-MON.BIN
   ÃÄÄÄ 4823-CRT.BIN
   ÃÄÄÄ 4823-TFT.BIN
   ÃÄÄÄ AWDFLASH.EXE
   ÀÄÄÄ CBROM.EXE

AWDFLASH.EXE
------------
This program allows you to write the VGA display driver files to the BIOS
Flash ROM. The VGA files all come ready formatted for the PCM-4823 with .BIN
extensions. These files support various CRT and flat-panel displays. They
are custom written and can be made available upon request.

4823-SYS.BIN
------------
This binary file contains the system BIOS.

4823-TFT.BIN
------------
Supports 640x480 color 18/24-BIT TFT (Sharp LQ9D011, Toshiba LTM10C042)

4823-STN.BIN
------------
Supports 640x480 color STN DD 8/16-bit displays (Sharp LM64C142)

4823-MON.BIN
------------
Supports 640x480 dual scan monochrome displays (Sharp LM64183)

4823-EL.BIN
------------
Supports 640x480 EL displays (PLANAR EL640.480-A Series)

4823-CRT.BIN
------------
This binary file supports CRT display only.

CBROM.EXE
------------
This program allows you to combine your own VGA BIOS with system BIOS.

If you have your own VGA BIOS ( which supports special flat panel ) for
PCM-4823, please update your BIOS refer to the following example:

              COPY 4823-SYS.BIN 4823-NEW.BIN
              CBROM 4823-NEW.BIN /VGA NEW-VGA.DAT
              AWDFLASH 4823-NEW.BIN

NEW-VGA.DAT : Your own VGA BIOS file (which supports special LCD) for PCM-4823.
4823-NEW.BIN: The NEW BIOS supports your own special LCD for PCM-4823.
-------------------------------------------------------------------------------