Technical support notes No. 980519004

PCM-3115 Using ATA Devices Under Win95

The following procedure is for PCM-3115 to support ATA compatible devices such as PCMCIA Flash disk card or PCMCIA hard disk drive under the Windows95 environment.

To Install The PCMCIA Wizard

Windows95 default driver can support PCMCIA ATA hard disk, ATA Flash and I/O cards without other software drivers such as CardWork.  If you do not use the PCMCIA SRAM or Flash cards, you will not need to install CardWork driver.  The following procedure will show you how to enable the PCMCIA support under Windows95.

To install PCMCIA Wizard, your hard disk must be installed with Windows95.  The system also requires a floppy drive and a CD-ROM.

When you install the PCM-3115 onto your system, please be careful of the pin orientation.  To install PCM-3115, some CPU cards/motherboards require either a special adapter or a reversed board insertion.

Remove the jumper on JP1 of the PCM-3115 completely to disable the boot ROM function.

Before you turn on the power, you should check the jumper setting again.  And make sure no PCMCIA device is inserted in the PCMCIA socket at this time.

First, boot from the hard disk and start Windows95.

Go to Control Panel and double click on PC Card (PCMCIA) icon to open it.

If you will not use these PCMCIA devices --Ethernet cards or SCSI controller cards, you could select No to continue with installation.

Select No to continue.

Select Finish to end installation.

Windows95 will ask you to shout down Windows now.  Please select Yes to shout down Windows95.

Windows95 should be able to support the PCM-3115 PCMCIA adapter after you restart your system.

Format ATA Devices

In order to read, write or boot with ATA devices, you should initialize your ATA devices before using them.  The following procedure will show you how to initialize your ATA devices in Windows95:

Boot from the HDD; then insert the PCMCIA card into the PCM-3115 socket-0 (lower socket).  If PCM-3115 detects that PCMCIA device, you will hear a beep sound.  And you will see the ATA device appears onthe My Computer window.  For example, the following picture shows Windows95 recognizes the ATA Flash card and maps it onto drive-E.

Select Disk-E, File, Format to open the format window.

Select format type as Full, then click Start icon to start formating the ATA device.

The Format results will be displayed on the screen when Windows95 finishes the format.

If you don’t need to boot from your ATA device, you could bypass the following procedure and enjoy your new ATA drive now.

Install Windows95 To ATA Device

In order to install Windows95 in your ATA device, it must have more than 100MB of free space.  And you should know that the performance of the PCMCIA hard disk is slower than the regular hard disks.

Remove the hard disk drive.  Install a CD-ROM to the IDE interface and a floppy disk to the FDC interface.

Turn on the power and enter the CMOS setting manual.  Please change your COMS setup to the following setting:

Drive C: Auto,  MODE: Auto

Drive D: Auto,  MODE: Auto

Drive A: 1.44MB

Boot Sequence: A,C

Swap Floppy Drive: Disabled

Boot Up Floppy Seek: Enabled

Before you exit the COMS setup manual, do not forget to save the changes.

Insert the Windows95 installation CD to the CD-ROM; and insert the Windws95 CD-ROM Setup Boot Disk to floppy disk.

Now, re-boot the system.  And simply follow the Windows95 setup procedure to install Windows95.

After you finish the installation, Please shout down your system and change the jumper setting of JP1to enable the boot-ROM function.  For example, you could short JP1’s pin 3-4 and 7-8 to assign the memory address D8000~DFFFF for boot-ROM.

Reboot the system and go to CMOS setting manual.  Please change your COMS setup to the following setting:

Boot Sequence: C,A

Now, when you re-boot the system, you should see the system boot from the ATA drive as drive-C.

Note: This procedure has been verified by testing PCM-3115 with

Viper 170E, 170MB PCMCIA type-3 ATA hard disk manufactured by Integral Peripherals

AAEON Electronics, Inc.

AE Department

approve by:		edited by:

Vincent Hsu	Sheila Chang

http://www.aaeon.com

Tel:(732)203-9300 ext.123

Fax:(732)203-9311