PCM-5820 Utility Disk (V1.10)  Date : 2/4/1999

-----------------------------------------------------------------------------

The PCM-5820 is supplied with a software utility disk. This disk contains the
necessary file for setting up the LCD control parameters.

ROOT
   ³   README.DOC
   ³
   ³
   ÀÄÄÄBIOS
           5820V110.BIN
           AWDFLASH.EXE
           CBROM.EXE
           LCD.BIN
           PANEL.EXE

AWDFLASH.EXE
------------
This program allows you to write the new BIOS file to the BIOS Flash ROM.

5820V110.BIN
------------
This binary file contains the original system BIOS.

CBROM.EXE
------------
This program allows you to combine your own LCD parameter file with
the original system BIOS.

If you have your own LCD file ( which supports special flat panel ) for
PCM-5820 , please update your BIOS refer to the following example:

              COPY 5820V110.BIN 5820-NEW.BIN
              CBROM 5820-NEW.BIN /other 1800:0 LCD.BIN
              AWDFLASH 5820-NEW.BIN

PANEL.EXE
------------
A windows application program. It can be used to acquire LCD control parameters.


LCD.BIN
------------
The default LCD control parameter file.

This file contains three types of LCD control parameter in three groups.
Each group consists of 30 bytes. The first group is for 640X480 LCD panel.
the second group is for 800X600 LCD panel, and the third group is for 1024X768
LCD panel. The format of each group is describe in follows:

Group 1:     (INDEX,VALUE)
BYTE 1,2        51H,xxH         ;Type
BYTE 3,4        52h,xxH         ;Resolution
BYTE 5,6        53H,xxH         ;Control
BYTE 7,8        54H,xxH         ;Dither
BYTE 9,10       55H,xxH         ;CLOCK
BYTE 11,12      56H,xxH         ;HTOTAL
BYTE 13,14      57H,xxH         ;VTOTAL
BYTE 15,16      58H,xxH         ;LCD HSYNC START
BYTE 17,18      59H,xxH         ;LCD HSYNC END
BYTE 19,20      5AH,xxH         ;LCD VSYNC START
BYTE 21,22      5BH,xxH         ;LCD VSYNC END
BYTE 23,24      5CH,xxH         ;CRT HSYNC START
BYTE 25,26      5DH,xxH         ;CRT HSYNC END
BYTE 27,28      5EH,xxH         ;CRT VSYNC START
BYTE 29,30      5FH,xxH         ;CRT VSYNC END


------------------------------------------------------------------------------