************************************************************************
*             How to compile and link C or C++ application             *
*             program with the PCM-3718 Device Driver                  *
************************************************************************

1. How to compile and link with the driver for Microsoft C  ?
          Example for SMALL mode :
               cl  /AS  /c  3718demo.c
               link 3718demo + 3718CS.LIB;

          Note :    /AS for SMALL Mode
                    /AM for MEDIUM Mode
                    /AC for COMPACT Mode
                    /AL for LARGE Mode

2. How to compile and link with the driver for Turbo C  ?
          Example for SMALL mode :
          1. In Integrated Development Environment
               . Set project name (*.prj) in project options
                    Example : 3718.prj
               . 3718.prj file contents :
                    3718demo.c
                    3718cs.lib
               . Select Compile \ Build all
          2. In DOS Command Use TCC Program
               . TCC   -ms  3718demo.c  3718cs.lib
               Note :    -ms for SMALL Mode
                         -mm for MEDIUM Mode
                         -mc for COMPACT Mode
                         -ml for LARGE Mode

3. How to compile and link with the driver for Borland C++  ?
          Example for SMALL mode :
              BCC   -ms 3718demo.c 3718cs.lib
          Note :    -ms for SMALL Mode
                    -mm for MEDIUM Mode
                    -mc for COMPACT Mode
                    -ml for LARGE Mode

************************************************************************
*  If linker error, undefined symbol pcm3718(int, unsigned int far*),  *
*  occurred when using .CPP as program extension name                  *
************************************************************************

1. Add the following code paragraph before the declaration
   extern pcm3718(int, unsigned int *):

        #ifdef __cplusplus
        extern "C" {
        #endif

        _cdecl pcm3718(int, unsigned int *);

        #ifdef __cplusplus
        }
        #endif