PCM-4825 Utility Disk (Rev.1.20)  Date :11/27/1997
-----------------------------------------------------------------------------

The PCM-4825 is supplied with a software utility disk. This disk contains the
necessary file for setting up the VGA display.
Directories and files on the disk are as follows:

ROOT
       README.DOC
       AWDFLASH.EXE
       4825_SYS.BIN
       4825_CRT.BIN
       4825_TFT.BIN
       4825_STN.BIN
       4825_MON.BIN
       4825_EL.BIN
       CBROM.EXE
       SM.COM
       CT.COM
       FP.COM
       ON.COM
       OFF.COM

AWDFLASH.EXE
------------
This program allows you to write the VGA display driver files to the BIOS
Flash ROM. The VGA files all come ready formatted for the PCM-4825 with .BIN
extensions. They are custom written and can be made available upon request.

4825_SYS.BIN
------------
This binary file contains the system BIOS

4825_CRT.BIN
------------
Supports CRT only

4825_TFT.BIN
------------
Supports 640X480 color TFT
(Toshiba LTM10C042)

4825_STN.BIN
------------
supports 640X480 color STN DD 8/16-bit displays
(Sharp LM64C142)

4825_MON.BIN
------------
Supports 640X480 dual scan monochrome displays
(Sharp LM64P83/64P89)

4825_EL.BIN
-----------
Supports 640X480 EL displays
(PLANAR EL640X480-A series)

CBROM.EXE
----------
This program allows you to combine your own VGA BIOS with
system BIOS(4825_SYS.BIN)

SM.COM
------
Enables both displays at the same time

CT.COM
------
Enables CRT display only

FP.COM
------
Enables panel display only

ON.COM
------
Switches to normal display mode

OFF.COM
-------
Switches to sleep mode